## Slide 1
Revisiting the Operating Reserve Demand Curve
Randy Jones
November 13, 2015

## Slide 2: ORDC: Time for Review
PUCT directed ERCOT and stakeholders to review the market impact of the ORDC
Actual market data is available for review, market participants have ~16-months experience with the ORDC, including two summer peak seasons (2014 and 2015)
NERC adopted new reliability standard, BAL-003-01; ORDC change needed to be consistent with new standard
ORDC is intended to and should reflect ERCOT’s willingness to pay for reserves – current design is not consistent with new NERC requirements, e.g. application in DAM could result in under-procurement of RUS and/or RRS

## Slide 3: ORDC: Set “X” to Reflect New NERC Reliability Standard
Adjust Minimum Contingency Limit (“X”) to reflect new NERC reliability standard, BAL-003-01
  Set X equal to the Responsive Reserve Service (“RRS”) and Regulations Up Service (“RUS”) reliability requirements
In the Real-time Co-Optimization development in ERCOT, demand curves for RRS and RUS would both be set at SWOC
Setting X equal to RRS + RUS requirements makes ORDC consistent with concept ORDC is designed to mimic RTC
RRS requirment is based on protecting the grid against loss of the two largest units (2750MW) in ERCOT; to be conservative, set X equal to RUS plus the greater of RRS requirement or 2750 MW

## Slide 4: ORDC: Market Participant Behavior Impacts Expected Results
Assume ORDC implemented in 2012 (most similar to June 2014-May 2015 weather) Using ERCOT backcast for 2012 :
  ERCOT's backcast spreadsheet with VOLL = $9,000/MWh and X = 2,000MW results in PNM estimate of $87,174/MW-year
  Actual PNM for 2012 was $33,952/MW-year, <40% of ERCOT backcast
In contrast, actual PNM was just under $29,000/MW-year for similar ORDC year of June 2014-May 2015
Post-ORDC implementation results indicate a slight reduction in PNM compared to ERCOT backcast estimate more than double actual 2012 PNM
Takeaway: More realistic views of adder results require backcast scenarios to reflect market participant behavior; avoid significant overestimates of various proposals
Note: ERCOT backcast for 2012 is based on piecewise linear curve. Using actual LOLP curve would decrease ERCOT’s backcast for 2012 to roughly $60,000/MW-year.

## Slide 5: Summary
Calpine’s proposal is in direct response to the Commissioner Anderson’s request to review “The level of X used in the ORDC formula, which is 2,000 MW of operating reserves… .”
Set X to reflect reliability standards, i.e. set X equal to RRS plus RUS reliability requirements
Resetting X has the most immediate and significant impact on signals sent to loads and resources as the system approaches scarcity conditions
A change in X does not require a rule change and can be done without much complexity