## Slide 1: ERCOT MARKET EDUCATION
Retail 101

## Slide 2: Smart Meter Technology

## Slide 3: Overview
Topics in this lesson . . .
  Meter Data – The Big Picture
  A Few Definitions
  Impacts of Smart Meter Technology on REPs

## Slide 4: Smart Meter Technology
Meter Data – The Big Picture
Meter Data
Qualified Scheduling Entity (QSE)
Losses
Unaccounted For Energy (UFE)
Adjusted Metered Load (QSE)
Calculated for each 15 minute interval
Collected by TDSPs
Retail Electric Provider (REP)
Notes: We saw this picture earlier in the course. <Click for animation> Load meter data is collected and sent to ERCOT by TDSPs. Ultimately, ERCOT must roll all meter data up to the QSE level in order to settle the Wholesale Markets. ERCOT adjusts the metered load data to incorporate Losses and UFE and calculates each QSE’s Adjusted Metered Load. <Click for animation> Since ERCOT settles the Wholesale Markets on a fifteen minute interval, the QSEs’ Adjusted Metered Load must be calculated for each fifteen minute interval.

## Slide 5: Smart Meter Technology
ERCOT settles with QSE based on Adjusted Metered Load
  Energy usage
  Other load-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Load Related Charges

## Slide 6: Smart Meter Technology
QSE Settles with REP
  Energy usage
  Other load-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Retail Electric Provider (REP)
Load Related Charges

## Slide 7: Smart Meter Technology
REP Bills Customers
  Energy usage based on Meter Data
  Other service-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Retail Electric Provider (REP)

## Slide 8: A Few Definitions

## Slide 9: A Few Definitions
Meter – A device that measures electrical usage over some period of time
Notes: Just so everyone is clear, when we speak of a meter, we are speaking of a device that measures electrical usage over some period of time. The time component of this definition is important, because it will help us distinguish between the various meters that are utilized in ERCOT.

## Slide 10: A Few Definitions
Non-Standard
Interval Data Recorder (IDR)
Non-IDR
Standard
Advanced Meter System (AMS)
Meters come in multiple flavors

## Slide 11: A Few Definitions
Usage is measured in 15-minute intervals
Data is already shaped for 15 minute Wholesale Settlement
Typically reported monthly
Interval Data Recorder (IDR) Meter
ERCOT Settles the Real-time Wholesale Market in 15-minute intervals

## Slide 12: A Few Definitions
Traditional Meter
Usage is a scalar measurement for an entire month
Data must be shaped for 15 minute Wholesale Settlement
Non-IDR Meter

## Slide 13: A Few Definitions
Usage is measured in 15 minute intervals
Data is already shaped for 15 minute Wholesale Settlement
Remote capabilities
  Typically read remotely
  May be disconnected and reconnected remotely
Advanced Meter System (AMS)
Also known as a “Smart Meter”

## Slide 14: Impacts of Smart Meter Technology on the Retail Market

## Slide 15: Impact of Smart Meter Technology
So, what does Smart Meter Technology mean for the Retail Market?
  Meter data is more precise
  Meter data is available faster
  More opportunities for retail products?

## Slide 16: More Precise Meter Data
Before Smart Meters
  ~58% of competitive load was settled with NIDR meters
    Had to be shaped with Load Profile
    Actual customer load pattern might have been different
    Errors contributed to UFE
Chart: Profile vs. Actual usage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
RESLODG_NCENT | 0.193 | 0.177 | 0.169 | 0.173 | 0.183 | 0.208 | 0.293 | 0.277 | 0.25 | 0.245 | 0.246 | 0.233 | 0.224 | 0.219 | 0.219 | 0.221 | 0.243 | 0.309 | 0.378 | 0.382 | 0.381 | 0.351 | 0.288 | 0.242
Actual Customer Usage | 0.2 | 0.185 | 0.172 | 0.173 | 0.183 | 0.208 | 0.26 | 0.243 | 0.25 | 0.245 | 0.246 | 0.233 | 0.243 | 0.265 | 0.281 | 0.32 | 0.34 | 0.345 | 0.35 | 0.35 | 0.345 | 0.34 | 0.32 | 0.281

## Slide 17: More Precise Meter Data
After Smart Meters
  ~98% of competitive load is now settled using interval data
    REP can discover customer’s actual usage pattern
    More accurate REP settlement with QSE
Chart: Actual usage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Actual Customer Usage | 0.2 | 0.185 | 0.172 | 0.173 | 0.183 | 0.208 | 0.26 | 0.243 | 0.25 | 0.245 | 0.246 | 0.233 | 0.243 | 0.265 | 0.281 | 0.32 | 0.34 | 0.345 | 0.35 | 0.35 | 0.345 | 0.34 | 0.32 | 0.281

## Slide 18: Meter Data is Available Faster
More Accurate Initial Settlement
  Today, ~73% actual load data used in Initial
  Before Smart Meters, ~ 39% actual load data was used in Initial
ERCOT Real-Time Settlements Timeline
Day 180
Operating Day
Day 5
Initial Statement
Final Statement
True-Up Statement
Day 55

## Slide 19: Meter Data is Available Faster
Faster Execution of Retail Market Processes
Enrollment type Initiating Transaction | AMS Remote (AMSR) | AMS Manual (AMSM) | Non-AMS
Move-In 814_16 | Same Day | 2 Business Days | 2 Business Days
Standard Switch 814_01 | Same Day | Same Day | Within Next 4 Business Days
Self Selected Switch 814-01 | Same Day | Same Day | At Least 2 Business Days
Move-Out 814_24 | Same Day | Same Day | Within Next 4 Business Days

## Slide 20: More Opportunities?
Does Smart Meter technology offer the promise of new Retail products?
  Prepay
  Demand Response
  Time-of-Use Rates
Qualified Scheduling Entity (QSE)
Retail Electric Provider (REP)
Only time will tell!
Notes: Does Smart Meter technology offer the promise of new Retail products? Does the greater timeliness of meter data allow for better prepay products, where a customer pays in advance to use a certain amount of electricity over a certain period of time? Does the greater precision and interval measure of meter data allow for enhanced demand response products? Does having interval data for most customers allow REPs to offer the long-sought time-of-use pricing?
<Click for animation> Only time will tell!