## Slide 1: MIRTM Temporal Constraints Discussion
Loads in SCEDv2 Subgroup
Jan. 8, 2016

## Slide 2: Background
The Multi-Interval Real-Time Market (MIRTM) would lengthen the time horizon for SCED commitment and dispatch
This would open SCED to Resources that are otherwise unable to participate in the RTM, such as:
  Blocky Load Resources, and/or
  Resources with Temporal Constraints

## Slide 3: Temporal Constraints
Four values (in minutes) associated with Load Resources’ demand response:
  Ramp Period (time needed from dispatch to response)
  Minimum down time (minimum time of response)
  Maximum down time (maximum time able to respond)
  Return to Service time (time needed to be available for re-dispatch after recall)
Note: terminology not set in stone
Potentially these values could be established in the LRARF, but subject to modification via real-time telemetry

## Slide 4: Key elements
Ramp Period + Minimum Down Time must be ≤ MIRTM time horizon
  For example, 30 minutes (or 6 SCED runs)
This means (one-part) bid/offer price should allow the LR to recover its opportunity cost within the Minimum Down Time window
LR would not be dispatched beyond its Maximum Down Time
LR would not be subject to re-dispatch until Return to Service Time has elapsed

## Slide 5: Key elements
LR would be eligible for make-whole payment if the forecasted price that triggered the commitment failed to materialize in real-time
Make-whole payment may apply only to the Minimum Down Time window – this is TBD

## Slide 6: Appendix
The following slides were presented to DSWG on March 9, 2015

## Slide 7: Load Resource Inputs to the Multi-Interval Real-Time Market
ERCOT is requesting input from LRs and QSEs to enable running meaningful MIRTM simulations

## Slide 8: Background
Loads in SCED v2 Subgroup seeks to simulate MIRTM behavior with participation by LRs
  ‘Blocky’ LRs not capable of responding to incremental SCED base points and/or with temporal constraints
  Growth in residential DR due to enabling technology (smart meters, smart thermostats, etc)
LRs and QSEs are asked to submit best-estimate inputs for bid/offer prices and temporal constraints
  Multiple scenarios OK
Submitters will be known only to ERCOT
  All data will be anonymized for simulated market runs

## Slide 9: Background
Under MIRTM, the real-time market would be able to commit Resources at future intervals (beyond the current 5-minute SCED)
If the Resource’s bid/offer price failed to materialize in real time at their commitment interval, the Resource would be eligible for a make-whole payment
One objective of this exercise is to get an idea whether uplifts associated with make-whole payments would exceed the market benefits of additional RTM competition

## Slide 10: LR inputs requested
DESCRIPTION | VALUE | INPUT
Energy curtailment price (minimum real-time energy price that the LR would curtail consumption based on the minimum curtailment duration) | $/MWh | 
DR Quantity (Curtailable MWs available now [2015]) | MW | 
Ramp period (duration needed to reach full curtailment – a.k.a. “notification period”) | minutes | 
Minimum curtailment duration (a.k.a., “minimum down time”) | minutes | 
Maximum curtailment duration (a.k.a., “maximum down time”) | minutes | 
Post recall unavailability duration (a.k.a., “return to service time”) | minutes | 
Future DR Quantity (Curtailable MW expected to be available in 2018) | MW | 
And for future consideration….

## Slide 11: Example to assist in preparing input data (1)
LR’s assumptions & bid/offer parameters:
DR capacity | 10 MW
Fixed cost of curtailment | $2,000
Running cost of curtailment | $500 per hour
Minimum curtailment duration | 15 minutes
Maximum curtailment duration | 2 hours
Post-recall unavailability (return-to-service time) | 1 hour

## Slide 12: Example to assist in preparing input data (2)
Based on the data from slide #5:
If LR wants to recover curtailment cost based on minimum curtailment duration (15 min.):
  Cost = $2,000 (fixed) + 1.25 * $500 (hourly) = $2,625
    (where 1.25 = 15-minute deployment + 1 hour return to service)
  $2,625 * 4 / 10 = $1,050/MWh
    (where multiplying 15-minute min. duration by 4 = hourly; dividing by 10 = per MW)

## Slide 13: Example to assist in preparing input data (3)
Based on the data from slide #5:
If LR wants to recover curtailment cost based on maximum curtailment duration:
  Cost: $2,000 (fixed) + 3.0 * $500 = $3,500
    (where 3.0 = 2-hour deployment + 1 hour return to service)
  $3,500 / 10 = $350/MWh
So, this LR’s cost recovery range would be: >$350/MWh to $1,050/MWh

## Slide 14: Example
TIME
MIRTM commitment instruction
Ramp period
Curtailment deadline
Min duration
Max duration
Post recall unavailability duration
LOAD MW
MIRTM Recall instruction
LR available for next MIRTM commitment
DR MW
Quantity
(bid/offer)

## Slide 15: Request to LRs and QSEs
Please populate cells in the right-hand column on the following slide(s)
Submit as many scenarios as you like
To ensure apples ↔ apples, please assume the following for cost calculation (if used):
  Natural gas: $3.00 per MMBtu
  Diesel fuel: $2.75 per gallon
Also, assume participation is energy-only – capacity in MIRTM not carrying AS responsibility
Please email populated tables by Fri., March 27, to paul.wattles@ercot.com and sainath.moorty@ercot.com
Thanks!

## Slide 16: LR inputs requested
DESCRIPTION | VALUE | INPUT
Energy curtailment price (minimum real-time energy price that the LR would curtail consumption based on the minimum curtailment duration) | $/MWh | 
DR Quantity (Curtailable MWs available now [2015]) | MW | 
Ramp period (duration needed to reach full curtailment – a.k.a. “notification period”) | minutes | 
Minimum curtailment duration (a.k.a., “minimum down time”) | minutes | 
Maximum curtailment duration (a.k.a., “maximum down time”) | minutes | 
Post recall unavailability duration (a.k.a., “return to service time”) | minutes | 
Future DR Quantity (Curtailable MW expected to be available in 2018) | MW | 
And for future consideration….