## Slide 1: LOAD Resources in SCED Treatment of Snapback
Carl Raish
January 8, 2016

## Slide 2: What is Snapback?
Snapback is unusually high load that occurs following release of a load curtailment
Is not uncommon with weather sensitive loads because of the buildup of demand for heating or cooling
Is a function of curtailment duration and prevailing weather conditions

## Slide 3: What is Snapback?
Snap back can be mitigated by using carefully designed recall strategies
Depending on event timing can be insignificant for commercial weather sensitive load … business shutdown near the recall time

## Slide 4: Settlement Treatment for Snapback
ERCOT should infer that snap back is occurring if actual load following a recall is greater than the baseline and the difference is statistically significant.
Snap back can occur during a deployment if blocks of customers within an aggregation are deployed and recalled at different times
  This is commonly done to extend the duration of the response capability of the aggregation
  Such a deployment strategy would decrease the maximum load reduction capability at any point in time
The DR QSE should be responsible for the snap back costs, if any, incurred by the LSE for the associated
  The DR QSE should be charged at the rate of LMP - $G for the energy associated with snap back
  The LSE should be paid that same amount
  Note: if LMP < $G, the DR QSE would actually be paid instead of charged
If more than one LSE has sites in the aggregation, the snap back, the payment and charge calculations need to be individualized to the LSE

## Slide 5: Settlement Treatment for Snapback
Scenario 1 … one REP in aggregation

## Slide 6: Settlement Treatment for Snapback
Scenario 2 … two REPs in aggregation
  REP A’s sites were deployed first
  REP B’s sites were deployed just as REP A’s sites were recalled

## Slide 7: Questions?
ON
OFF