## Slide 1: ERCOT MARKET EDUCATION
Retail 101

## Slide 2: Advanced Meter Technology

## Slide 3: Overview
Topics in this lesson . . .
  Meter Data – The Big Picture
  A Few Definitions
  Impacts of Smart Meter Technology on REPs

## Slide 4: Advanced Meter Technology
Meter Data – The Big Picture
Meter Data
Qualified Scheduling Entity (QSE)
Losses
Unaccounted For Energy (UFE)
Adjusted Metered Load (QSE)
Calculated for each 15 minute interval
Collected by TDSPs
Retail Electric Provider (REP)
Notes: We saw this picture earlier in the course. <Click for animation> Load meter data is collected and sent to ERCOT by TDSPs. Ultimately, ERCOT must roll all meter data up to the QSE level in order to settle the Wholesale Markets. ERCOT adjusts the metered load data to incorporate Losses and UFE and calculates each QSE’s Adjusted Metered Load. <Click for animation> Since ERCOT settles the Wholesale Markets on a fifteen minute interval, the QSEs’ Adjusted Metered Load must be calculated for each fifteen minute interval.

## Slide 5: Advanced Meter Technology
ERCOT settles with QSE based on Adjusted Metered Load
  Energy usage
  Other load-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Load Related Charges

## Slide 6: Advanced Meter Technology
QSE Settles with REP
  Energy usage
  Other load-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Retail Electric Provider (REP)
Load Related Charges

## Slide 7: Advanced Meter Technology
REP Bills Customers
  Energy usage based on Meter Data
  Other service-related charges
Meter Data – The Big Picture
Qualified Scheduling Entity (QSE)
Adjusted Metered Load (QSE)
Retail Electric Provider (REP)

## Slide 8: A Few Definitions

## Slide 9: A Few Definitions
Meter – A device that measures electrical usage over some period of time
Notes: Just so everyone is clear, when we speak of a meter, we are speaking of a device that measures electrical usage over some period of time. The time component of this definition is important, because it will help us distinguish between the various meters that are utilized in ERCOT.

## Slide 10: A Few Definitions
Advanced Meter System (AMS) Meters
  AMSR – remote (R) connectivity
  AMSM – manual (M) connectivity
Non AMS Meters
  Scalar, Analog, Digital
  Interval Data Recorder (IDR) Meters
Advanced Meters vs Old Technology

## Slide 11: A Few Definitions
Standard
  Advanced Meter System– Remote (AMSR)
Non-Standard
  Advanced Meter System- Manual (AMSM)
  Interval Data Recorder (IDR) Meter
  Non-IDR
Various types of meters today

## Slide 12: A Few Definitions
  Usage is measured in 15-minute intervals
  Data is already shaped for 15 minute Wholesale Settlement
  Typically reported monthly through 867 transactions
  Predominantly installed on large customers > 700 kW/kVA demand
  Requires manual field activities
Interval Data Recorder (IDR) Meter
ERCOT Settles the Real-time Wholesale Market in 15-minute intervals

## Slide 13: A Few Definitions
  Traditional Meter
  Usage is a scalar measurement for an entire month
  Data must be shaped for 15 minute Wholesale Settlement
  Requires manual field activities
Non-IDR Meter

## Slide 14: A Few Definitions
  Usage is recorded in 15 minute intervals
  Data is already shaped for 15 minute Wholesale Settlement
  Remote capabilities
    AMSR (≤ 200 amp)
      Remote / automatic reading
      Remote disconnect
    AMSM
      Remote / automatic reading
      Manual Disconnect
Advanced Meter System (AMS) Meter
Also known as a “Smart Meter”

## Slide 15: Impacts of Advanced Meter Technology on the Retail Market

## Slide 16: Impact of Advanced Meter Technology
So, what does Advanced Meter Technology mean for the Retail Market?
  Meter data is more precise
  Meter data is available faster
  Greater visibility of data
  More opportunities for retail products
  Other benefits

## Slide 17: More Precise Meter Data
Before Advanced Meters
  ~58% of competitive load was settled with NIDR meters
    Had to be shaped with Load Profile
    Actual customer load pattern might have been different
    Errors contributed to UFE
Chart: Profile Usage vs. Actual Usage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
RESLODG_NCENT | 0.193 | 0.177 | 0.169 | 0.173 | 0.183 | 0.208 | 0.293 | 0.277 | 0.25 | 0.245 | 0.246 | 0.233 | 0.224 | 0.219 | 0.219 | 0.221 | 0.243 | 0.309 | 0.378 | 0.382 | 0.381 | 0.351 | 0.288 | 0.242
Actual Customer Usage | 0.2 | 0.185 | 0.172 | 0.173 | 0.183 | 0.208 | 0.26 | 0.243 | 0.25 | 0.245 | 0.246 | 0.233 | 0.243 | 0.265 | 0.281 | 0.32 | 0.34 | 0.345 | 0.35 | 0.35 | 0.345 | 0.34 | 0.32 | 0.281

## Slide 18: More Precise Meter Data
After Smart Meters
  ~98% of competitive load is now settled using interval data
    REP can discover customer’s actual usage pattern
    More accurate REP settlement with QSE
Chart: Actual usage
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Actual Customer Usage | 0.2 | 0.185 | 0.172 | 0.173 | 0.183 | 0.208 | 0.26 | 0.243 | 0.25 | 0.245 | 0.246 | 0.233 | 0.243 | 0.265 | 0.281 | 0.32 | 0.34 | 0.345 | 0.35 | 0.35 | 0.345 | 0.34 | 0.32 | 0.281

## Slide 19: Meter Data is Available Faster
More Accurate Initial Settlement
  Today, ~73% actual load data used in Initial
  Before Advanced Meters, ~ 39% actual load data was used in Initial
ERCOT Real-Time Settlements Timeline
Day 180
Operating Day
Day 5
Initial Statement
Final Statement
True-Up Statement
Day 55

## Slide 20: Meter Data is Available Faster
Faster Execution of Retail Market Processes
Enrollment type Initiating Transaction | AMS Remote (AMSR) | AMS Manual (AMSM) | Non-AMS
Move-In 814_16 | Same Day | 2 Business Days | 2 Business Days
Standard Switch 814_01 | Same Day | Same Day | Within Next 4 Business Days
Self Selected Switch 814-01 | Same Day | Same Day | At Least 2 Business Days
Move-Out 814_24 | Same Day | 2 Business Days | 2 Business Days

## Slide 21: Greater Visibility of Data
AMS Meter Data – The Extra Picture
Transmitted periodically
Uploaded Day 1
Available Day 2
Available Day 2
Customer
Notes: We saw this picture earlier in the course. <Click for animation> Load meter data is collected and sent to ERCOT by TDSPs. Ultimately, ERCOT must roll all meter data up to the QSE level in order to settle the Wholesale Markets. ERCOT adjusts the metered load data to incorporate Losses and UFE and calculates each QSE’s Adjusted Metered Load. <Click for animation> Since ERCOT settles the Wholesale Markets on a fifteen minute interval, the QSEs’ Adjusted Metered Load must be calculated for each fifteen minute interval.

## Slide 22: More Opportunities
Advanced Meter technology offers the promise of new Retail products
  Prepay
  Demand Response
  Time-of-Use Rate offerings
Qualified Scheduling Entity (QSE)
Retail Electric Provider (REP)
These products are available now. More are on the way!
Notes: Smart Meter technology also offers the promise of new Retail products? The greater timeliness of meter data allows for better prepay products, where a customer pays in advance to use a certain amount of electricity over a certain period of time. The greater precision and interval measure of meter data allows for further enhancement of demand response products. Having interval data for most customers allows REPs to offer the long-sought time-of-use pricing.
<Click for animation> These products are available now, in some form. But there is probably more to come. Convenience and economic incentives should spur demand for these types of products, inproving the current offerings, and bringing new offerings to market!

## Slide 23: Other Benfits
Fringe Benefits of AMS
  Improved service reliability with automated outage notification
  Earlier detection
    Faulty meters
    Meter tampering
  Environmental benefits – remote service orders minimize the need for manual field activities