## Slide 1
Reliability Deployment Price Adder and RUC ONOPTOUT
ERCOT
QSE Managers Working Group
1/29/2015

## Slide 2: Current Implementation
Current implementation of the Reliability Deployment Price Adder (NPRR 626) (RDPA) and ONOPTOUT settlement (NPRR416).
  Issue List
    Resource is not RUCed and telemeters ONRUC at anytime
    Resource is RUCed and has not opted-out and telemeters other than ONRUC at anytime during the RUC block
    Resource is RUCed and has opted-out and telemeters ONRUC instead of ONOPTOUT
    Resource is RUCed for an hour in the operating period after the Adjustment Period
      Resource is RUCed in the hour before the operating hour with the operating hour being the first RUC hour
      Resource is RUCed within the operating hour with the operating hour being the first RUC hour

## Slide 3: Proposed Solution
1. Resource is not RUCed and telemeters ONRUC at any
  A RUC commitment validation prior to running the RTRDP pricing run is in progress and we will communicate to the market when this change will go into production
Resource is RUCed and has not opted-out and telemeters other than ONRUC at anytime during the RUC block
  NPRR744 proposes a solution to fix this issue
Resource is RUCed and has opted-out and telemeters ONRUC instead of ONOPTOUT or RTRDP to RUC settlement mismatch
  NPRR744 proposes a solution to fix this issue

## Slide 4: Proposed Solution
Resource is RUCed for an hour in the operating period after the Adjustment Period
  Resource is RUCed in the hour before the operating hour with the operating hour being the first RUC hour
    NPRR679 and NPRR744 propose solutions to fix this issue
  Resource is RUCed within the operating hour with the operating hour being the first RUC hour
    Operator training to not RUC within the operating hour
    NPRR744 proposes a solution to fix this issue

## Slide 5: NPRR 744
5.5.2 Reliability Unit Commitment (RUC) Process

## Slide 6: NPRR 744
Regardless of when the RUC is communicated take a Resource Status telemetry snapshot when the following are all true:
    The resource has a confirmed RUC commitment
    The first hour of the RUC commitment block
    First SCED run when resource is on-line and available for SCED dispatch
  This Resource status snapshot would be used for the entire RUC block and any extensions of the RUC commitment block, unless the RUC goes into the next operating day. This status would be used in the QSE’s settlement for the entire RUC commitment block as well as the RUC trigger for the RTRDP pricing run. If snapshot is ONOPTOUT then Resource is opted-out of RUC settlement and RTRDP pricing run will not be initiated. If any online status , since unit is RUC-committed, then Resource will be settled as per RUC settlement and the RTRDP pricing runs will be initiated for the entire block.

## Slide 7: RUC timeline
HE 12
HE 11
HE 10
Example A
Example B
Example C

## Slide 8: NPRR 744 Examples
Off-line Example A: Off-line resource, is committed by a RUC process and communicated by ERCOT at 08:20 for Hour Ending 11-12
8:25 Updates COP resource status of RUCed resource to ONOPTOUT for HE 11 and 12
9:45 Real-Time telemeters a resource status of STARTUP
9:58 Real-Time telemeters a resource status of ONOPTOUT
10:02 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch (TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 9: NPRR 744 Examples
On-line Example A: On-line resource, is committed by a RUC process and communicated by ERCOT at 08:20 for Hour Ending 11-12
8:25 Updates COP resource status of RUCed resource to ONOPTOUT from OFF for HE 11 and 12
9:30 Real-Time telemeters a resource status of ON
9:58 Real-Time telemeters a resource status of ONOPTOUT
10:02 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch (TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 10: NPRR 744 Examples
Off-line Example B: Off-line resource, is committed by a RUC process and communicated by ERCOT at 10:30 for Hour Ending 12
10:50 Real-Time telemeters a resource status of STARTUP
10:58 Real-Time telemeters a resource status of ONOPTOUT
11:02 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch (TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 11: NPRR 744 Examples
On-line Example B: On-line resource, is committed by a RUC process and communicated by ERCOT at 10:30 for Hour Ending 12
10:30 Real-Time telemeters a resource status of ON
10:58 Real-Time telemeters a resource status of ONOPTOUT
11:02 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch (TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 12: NPRR 744 Examples
Off-line Example C: Off-line resource, is committed by a RUC process and communicated by ERCOT at 11:20 for Hour Ending 12
11:22 Real-Time telemeters a resource status of STARTUP
11:28 Real-Time telemeters a resource status of ONOPTOUT
11:29 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch (TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 13: NPRR 744 Examples
On-line Example C: On-line resource, is committed by a RUC process and communicated by ERCOT at 11:20 for Hour Ending 12
11:22 Real-Time telemeters a resource status of SHUTDOWN
11:28 Real-Time telemeters a resource status of ONOPTOUT
11:29 SCED snapshot captures ONOPTOUT status
    The resource has a confirmed RUC commitment (TRUE)
    The first hour of the RUC commitment block (TRUE)
    SCED snapshot when resource is on-line and available for SCED dispatch(TRUE)
Outcome:
  QSE opted out of RUC settlement for RUC committed resource and the RTRDP was NOT calculated

## Slide 14: NPRR 744 Summary

## Slide 15
Questions / Comments?
David Thompson
512-248-4519
David.Thompson@ercot.com
Client Services for Market Participants
  512-248-3900 ClientServices@ercot.com

## Slide 16: NPRR 679 implementation
A Resource receives a VDI RUC, and one of the hours of the block can still be updated in the COP before the start of the first hour of the block, then the Resource can OPTOUT in two ways.
  Update COP for hours still available in COP before start of first hour
  Telemeter ONOPTOUT for the entire RUC block without exception
Having multiple ways to opt-out could cause additional confusion and make internal settlements, reports and compliance checks more complicated. Telemetering ONOPTOUT during the RUC block is still required for RTRDP.