## Slide 1
Congestion Revenue Right Market Update
David Maggio
Congestion Management Working Group
February, 2016

## Slide 2: Agenda Items
Outages in the February Monthly Auction Model
Distribution factors for Hubs
General auction activity update

## Slide 3: Outages in the February Monthly auction model

## Slide 4: February Monthly Auction Model Outages
While preparing recent auction models, ERCOT reviewed updated network data along with the February Monthly model information and identified discrepancies in how three planned transmission outages were applied to the February Monthly auction model.
These outages were:
Equipment Name | From Station Acronym | To Station Acronym | Equipment Type | Nature of Work
ARCO_DENARCOC21 | ARCO | DENARCOC | 138 kV Line | New Equipment Energization
WYL_ELMG1 | ELMGROVE | WYLIESW | 138 kV Line | New Equipment Energization
WYL_NEVA1 | NEVADA | WYLIESW | 138 kV Line | New Equipment Energization

## Slide 5: February Monthly Auction Model Outages
This discovery occurred after the February Monthly auction had been executed.
Because Market Participants would not be able to adjust their portfolios and given historical feedback and the potential delays in auction deadlines, ERCOT used the posted model.
The impact of the model difference was minimal.
ERCOT wanted to bring this issue to your attention, and discuss how the market would like to handle similar scenarios should they occur in the future.

## Slide 6: February Monthly Auction Model Outages
During the model build process, there was uncertainty in how the outages should be applied to the new transmission equipment given the current system one-lines and the CRR bus-branch model
As a result, three branches were manually taken out of service in an attempt to capture the outages
  Details about the specific branches are provided on the next two slides
We are working with other teams within ERCOT to find any additional information about future equipment that can be used and are increasing the amount of peer review for the model build process moving forward

## Slide 7: February Monthly Auction Model Outages
The ARCO_DENARCOC21 outage:

## Slide 8: February Monthly Auction Model Outages
The WYL_ELMG1 and WYL_NEVA1 outages:

## Slide 9: Distribution factors for Hubs

## Slide 10: Distribution of Flows for Hubs during Outages
ERCOT has discovered an inconsistency with how flows into or out of Hubs are being modeled between CRR and DAM in cases in which a PSS-E bus that is part of a Hub is on outage.
  A simple example illustrating the difference will be discussed.
ERCOT believes that an internal change should improve consistency between CRR and DAM for planned transmission outages and wanted to make CMWG aware of the change before implementing it.

## Slide 11: Illustrative Example of the Current Systems
As a simple example, lets assume a Hub that is defined by two Hub Busses:
  One Hub Bus consists of two PSS-E busses
  The other Hub Bus consists of one PSS-E bus
  A PSS-E bus represents one or more Electrical Busses
There is a 100 MW PTP that “sinks” at this Hub and that is the only PTP in the system.
The next slides will examine how that 100 MW would flow based on current CRR logic, both with and without a disconnection of one of the three PSS-E busses in the base case.

## Slide 12: Flow in CRR with No PSS-E Bus Outages
Rest of the Transmission System
Hub
Hub Bus 1
Hub Bus 2
PSS-E Bus 1
PSS-E Bus 2
PSS-E Bus 3
100 MW
50 MW
50 MW
25 MW
25 MW
50 MW

## Slide 13: Flow in CRR with PSS-E Bus 1 Disconnected
Rest of the Transmission System
Hub
Hub Bus 1
Hub Bus 2
PSS-E Bus 1
PSS-E Bus 2
PSS-E Bus 3
100 MW
33 MW
67 MW
0 MW
33 MW
67 MW

## Slide 14: Flow in DAM with No PSS-E Bus Outages
Rest of the Transmission System
Hub
Hub Bus 1
Hub Bus 2
PSS-E Bus 1
PSS-E Bus 2
PSS-E Bus 3
100 MW
50 MW
50 MW
25 MW
25 MW
50 MW
Flows are no different, relative to CRR

## Slide 15: Flow in DAM with PSS-E Bus 1 Disconnected
Rest of the Transmission System
Hub
Hub Bus 1
Hub Bus 2
PSS-E Bus 1
PSS-E Bus 2
PSS-E Bus 3
100 MW
50 MW
50 MW
0 MW
50 MW
50 MW
Flows are different, relative to CRR

## Slide 16: Future Steps
There is a relatively simple change that ERCOT can make for CRR and DAM to be consistent for planned transmission outages of an PSS-E bus that is part of a Hub.
This change will be implemented for all CRR Auction models moving forward.
  ERCOT plans to implement the change with the April Monthly CRR Auction.

## Slide 17: General auction activity Update

## Slide 18: CRR Cost vs. Value
Chart: Monthly CRR Settlement vs. Auction Cost
| 41640 | 41671 | 41699 | 41730 | 41760 | 41791 | 41821 | 41852 | 41883 | 41913 | 41944 | 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339
Final CRR Shortfall Amount | 25044668.9369 | 47710240.8952 | 31286527.8121 | 73879281.7859 | 55023624.4055 | 28722580.6093 | 32883761.2952 | 25541674.7275 | 38414161.2483 | 114358076.5829 | 38285684.3034 | 9801350.6194 | 18347323.6815 | 18138434.2362 | 20109873.286 | 23145708.168 | 23024824.5374 | 40406239.0593 | 32692770.7988 | 21840220.3116 | 21786548.8046 | 19184106.7943 | 9580847.6138 | 14382897.8137
CRR Deration Amount after Hedge Value | 25044668.9369 | 47710240.8952 | 31286527.8121 | 62729548.1459 | 55023624.4055 | 28722580.6093 | 32883761.2952 | 25541674.7275 | 38414161.2483 | 114358076.5829 | 38285684.3034 | 9801350.6194 | 18347323.6815 | 18138434.2362 | 20109873.286 | 23145708.168 | 23024824.5374 | 40406239.0593 | 32692770.7988 | 21840220.3116 | 21786548.8046 | 19184106.7943 | 9580847.6138 | 14382897.8137
Final CRR Payment | 24942465.82 | 47361202.83 | 30905884.45 | 60146016.47 | 54131267.67 | 28521684.37 | 32650499.71 | 25517890.28 | 35738221.82 | 105770988.05 | 35996684.13 | 9110429.56 | 17862382.81 | 17708717.37 | 19342866.47 | 22633009.69 | 21918808.02 | 40011785.21 | 32561236.48 | 21824965.43 | 21665459.91 | 19071563.92 | 9478470.76 | 14253445.25
Load-Allocated CRR Amount After Rolling Fund | -3685632.01 | -9055518.51 | -5418730.32 | 0 | -127275.69 | -1980934.62 | -3686296.43 | -9302875.39 | -974674.13 | -1001607.47 | -1455336.09 | -20580 | -1747349 | -2096606 | -2853013 | -1270628.04 | 1295855.26 | -3211328.79 | -4428381.84 | -5578528.36 | -3452239.45 | -3962069.03 | -2080168.79 | -2166073.06
Monthly Change to the Rolling CRR Balancing Account Fund | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | -20580 | -1747349 | -2096606 | -2853013 | -1270628.04 | 1295855.26 | -3211328.79 | -96350.43 | 0 | 0 | 0 | 0 | 0
CRR Auction Cost | 20626904.4339 | 17786887.6281 | 25841719.7721 | 29082309.5365 | 33053043.5202 | 39972428.7804 | 50868177.9354 | 44213375.4611 | 35104495.8309 | 30750547.2906 | 22509724.093 | 25086268.4977 | 22650803.1262 | 21254656.3564 | 25371852.3622 | 31609362.994 | 34488133.0642 | 35567334.577 | 38030496.4824 | 36981942.4829 | 31136907.0762 | 27380217.2479 | 22102303.3464 | 18971484.9142

## Slide 19: CRR Balancing Account Fund
Chart: Total Accumulated and Monthly Changes to the Rolling CRR Balancing Account Fund
| 41974 | 42005 | 42036 | 42064 | 42095 | 42125 | 42156 | 42186 | 42217 | 42248 | 42278 | 42309 | 42339
Monthly Change to the Rolling CRR Balancing Account Fund | 20580 | 1747349 | 2096606 | 2853013 | 1270628.04 | -1295855.26 | 3211328.79 | 96350.43 | 0 | 0 | 0 | 0 | 0
Load-Allocated CRR Amount After Rolling Fund | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 4332031.41 | 5578528.36 | 3452239.45 | 3962069.03 | 2080168.79 | 2166073.06
Rolling CRR Balancing Account Fund at Month End | 20580 | 1767929 | 3864535 | 6717548 | 7988176.04 | 6692320.78 | 9903649.57 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000 | 10000000

## Slide 20: Monthly Auction Transactions
Chart: Comparison of the Number of Transactions Submitted for Each Auction
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Latest Year | 162953 | 159583 | 146478 | 148138 | 142853 | 168578 | 194859 | 182990 | 178409 | 178723 | 174718 | 159460
Previous Year | 145340 | 127175 | 123444 | 146179 | 135708 | 154060 | 149985 | 155636 | 153794 | 141261 | 142456 | 129574
2 Years Prior | 103937 | 107111 | 124147 | 126540 | 137937 | 137492 | 147919 | 145753 | 143498 | 164969 | 158329 | 112598

## Slide 21: Long-Term Auction Sequence Transactions
Chart: Comparison of the Number of Transactions Submitted for Each Auction
| Seq. 1 | Seq. 2 | Seq. 3 | Seq. 4
Latest LTAS | 147056 | 141212
Previous LTAS | 130426 | 141636 | 173447 | 153090
Year Prior LTAS | 117079 | 126494 | 122166 | 121726

## Slide 22: Monthly Auction Net Revenue
Chart: Comparison of the Net Auction Revenue for Each Auction
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Latest Year | 6303390.37 | 5883125.33 | 5728678.5 | 7096735.91 | 8613809.62 | 7474151.8 | 9886476.29 | 8723734.65 | 7409269.37 | 5320194.52 | 5125017.46 | 2877659.32
Previous Year | 4089380.85 | 2876982.2 | 6757852.67 | 5980819.03 | 8914194.5 | 13210623.98 | 15502819.82 | 8685427.33 | 7752803.34 | 6542350.48 | 5472916.61 | 7717846.72
2 Years Prior | 6721674.64 | 4727604.69 | 3182774.81 | 7665958.15 | 12869258.42 | 16145997.59 | 12026872.8 | 10254875.69 | 6286784.47 | 7632553.41 | 7999601.91 | 3803905.85

## Slide 23: Long-Term Auction Sequence Net Revenue
Chart: Comparison of the Net Auction Revenue for Each Auction
| Seq. 1 | Seq. 2 | Seq. 3 | Seq. 4
Latest LTAS | 23761327.83 | 27691924.71
Previous LTAS | 32213568.98 | 31033849.7 | 32080788.35 | 35605773.41
Year Prior LTAS | 32898683.5 | 37104447.34 | 35481308.3 | 39046436.13

## Slide 24: Current CRR Inventory (as of 1/25/16)
Chart: Month
| 42415 | 42444 | 42475 | 42505 | 42536 | 42566 | 42597 | 42628 | 42658 | 42689 | 42719 | 42750 | 42781 | 42809 | 42840 | 42870 | 42901 | 42931 | 42962 | 42993 | 43023 | 43054 | 43084
Annual Allocation | 251 | 253 | 256 | 272 | 284 | 282 | 280 | 264 | 245 | 244 | 260 | 230 | 219 | 217 | 242 | 242 | 249 | 254 | 252 | 241 | 249 | 233 | 225
Year 2 Annual Auction | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Year 1 Annual Auction | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Seq. 4 Auction | 4626 | 5074 | 5112 | 4986 | 4952 | 6515 | 6484 | 6693 | 6984 | 6813 | 6206 | 7460 | 7407 | 7995 | 7989 | 7794 | 7798 | 0 | 0 | 0 | 0 | 0 | 0
Seq. 3 Auction | 6211 | 7626 | 7785 | 7365 | 6760 | 8064 | 8082 | 7898 | 7854 | 7948 | 7972 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Seq. 2 Auction | 7459 | 8000 | 7941 | 7639 | 7699 | 6108 | 6023 | 6167 | 7719 | 7568 | 6636 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Seq. 1 Auction | 6320 | 6513 | 6691 | 6599 | 6981 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Monthly Allocation | 15 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Monthly Auction | 15669 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Bilateral Trade | 118 | 133 | 134 | 160 | 150 | 39 | 25 | 141 | 148 | 107 | 60 | 8 | 5 | 9 | 9 | 8 | 5 | 0 | 0 | 0 | 0 | 0 | 0