## Slide 1
Settlement Update
Blake Holt
ERCOT
2/15/2016

## Slide 2
Agenda
NPRR689 – R1 – 02/10/16
NPRR744 – Buy-Back notification
NPRR746 – Negative load impacts
2016 Settlement changes

## Slide 3: NPRR689 – 2/10/2016 production release (R1)
NPRR689 - Settlement of Ancillary Service Assignment in Real-Time Operations
Settlement mechanism for NPRR663 Ancillary Service Insufficiency Actions
If sufficient Ancillary Services cannot be procured via DAM, SASM and RUC, then Ancillary Service will be assigned to QSEs.
QSE assigned the Ancillary Services (Reg-Up or RRS) is paid the assigned MW times the RTSPP minus the ORDC price adder.
Costs are spread the same way as current AS costs are spread, on Load Ratio Share basis.
The QSE will receive a Verbal Dispatch Instruction from ERCOT for the assignment.
The QSE must file a settlement dispute to be considered for the payment.
ERCOT implemented this process manually:
  Data will not be provided in the extracts (can be requested from account manager)
  Will be invoiced via a Misc. Invoice.

## Slide 4: NPRR689 – 2/10/2016 production release (R1)
QSE share of total costs:
ARUCOST q = ARUPR * ARUQ q
Where:
ARUPR = ARUCOSTTOT / ARUQTOT
ARUQTOT = ARUQq
ARUQq = ARUOq – SARUQq
ARUOq = WAURUTOT * HLRSq + RUOq
WAURUTOT = RTAURURq,r,p
QSE incremental costs:
NETARTRUAMTq = ARUCOSTq - RUCOSTq
Total Costs during a Watch:
ARUCOSTTOT = (-1) * RTAURUAMTTOT + RUCOSTTOT
Where: RTAURUAMTTOT = RTAURAMTq,r,p
Payment for Un-deployed Assigned AS:
RTAURUAMT q,r,p,i = (-1) * 1/4 * RTAURUR q,r,p * (RTSPPp,i - RTRSVPOR)

## Slide 5: NPRR689 – 2/10/2016 production release (R1)
QSE share of total costs:
Step 1: WAURUTOT = RTAURURq,r,p
Step 2: ARUOq = WAURUTOT * HLRSq + RUOq
Step 3: ARUQq = ARUOq – SARUQq
Step 4: ARUQTOT= ARUQq
Step 5: ARUPR = ARUCOSTTOT / ARUQTOT
Step 6: ARUCOST q = ARUPR * ARUQ q
QSE incremental costs:
NETARTRUAMTq = ARUCOSTq - RUCOSTq
Total Costs during a Watch:
ARUCOSTTOT = (-1) * RTAURUAMTTOT + RUCOSTTOT
Where: RTAURUAMTTOT = RTAURAMTq,r,p
Payment for Un-deployed Assigned AS:
RTAURUAMT q,r,p,i = (-1) * 1/4 * RTAURUR q,r,p * (RTSPPp,i - RTRSVPOR)
Total Reg-Up Costs
Total Assignment payments converted to a cost
QSE share of Watch Assignment and Reg-Up Obligation
QSE total costs
Assignment +Reg-Up
Un-deployed Assigned MW
S&B will work with Operations to determine the correct amount to consider during dispute resolution.
PR 6.7.2 (1)
Isolated Assignment Costs

## Slide 6: How do you know RUC hours have been successfully “bought-back”?
NOW
Settlement Eligibility process COP status and sets RUC interval value = 5
AFTER 744
MMS will determine if “buy back” is successful.
CSI_S&B will transform MMS data into a flag where an interval value of 1 will indicate successful “buy back”.
Settlement Eligibility process consumes MMS flag and sets RUC interval value = 5 where MMS flag interval value = 1

## Slide 7: NPRR746- Adjustments Due to Negative Load
What’s changing?
RTAMLTOT = (max(0, RTAML q,p))
LRSq = (max(0, RTAML q,p )) / RTAMLTOT
HRTAMLTOT = (max(0, RTAML q,p))
HLRSq=
(max(0, RTAML q,p))/(HRTAMLTOT)
URTAML = max(0, (RTAML mp,p,i))
ESACAMTq = LAFF * max(0, RTAML q,p)
ERSLRS qc(tp) - “…If the resultant QSE-level share is negative, the QSE’s share will be set to zero and
all other QSE shares
will be adjusted on a pro rata basis such that the sum of all shares is equal to one.”

## Slide 8: NPRR746- Adjustments Due to Negative Load
What’s not?
RTAML- Real-Time Adjusted Metered Load per QSE per Settlement Point
RUCSFSNAP ruc,q,i = Max (0, (( RTAML q,p,i * 4) + RTDCEXP q, p, i – RUCCAPSNAPruc,q,i))
RUCSFADJ ruc,q,i = Max (0, (( RTAMLq,p,i) *4) + RTDCEXP q, p, i –
( r=WGRsOnly HASLSNAP ruc, q, r, h + RUCCAPADJq,i))
RTEIAMT q, p = (-1) * {[RTSPP p * [(SSSK q, p * ¼) + (DAEP q, p * ¼) + (RTQQEP q, p * ¼) –
(SSSR q, p * ¼) – (DAES q, p * ¼) – (RTQQES q, p * ¼)]]
+ [RTSPPEW p * (RTMGNM q, p – RTAML q, p)]}
MLRS(Z) = LRS in the peak interval of the month. LRS will be adjusted to handle negative load.
        Between 1/1/2012 and 1/21/2016, there was only one instance of MLRS being negative (JULY 2015). MLRSZ was negative twice (JUNE 2014 and JULY 2015). All negative values were seen from a single QSE.
        June 2014- LACMRZAMT = $69.90
        July 2015- LACMRNZAMT = $21.49 ; LACMRZAMT = $59.43 ; LACRRAMT = $18.80

## Slide 9: What’s on the horizon?
NPRR | Description | Release | Timeframe | Discussion
NPRR419 | RTEI/RMR revisions | R2 | APR-2016 | MAR-2016
NPRR617 | Energy Offer Flexibility | R3 | JUN-2016 | MAY-2016
NPRR700 | Actual Fuel Costs in Start Up Offer Caps | R3 | JUN-2016 | MAY-2016
NPRR662 | Proxy Energy Offer Curves | R4 | AUG-2016 | JUL-2016
NPRR272 | Definition and Participation of QSGRs | R6 | DEC-2016 | NOV-2016