## Slide 1: PRC-005-6 Protection System, Automatic Reclosing, and Sudden Pressure Relaying Maintenance
Dennis Glass
Compliance Analyst III
January 21, 2016

## Slide 2: Effective Date
Enforcement Date of Standard:
  January 1, 2016

## Slide 3: Key Changes
Nine changes from PRC-005-1 to PRC-005-6:
  Requirements now apply to BES dispersed power producing resources
  Special Protection System and SPS now Remedial Action Scheme and RAS
  Automatic Reclosing now included in maintenance programs
  Sudden Pressure Relaying now included in maintenance programs
  Added supervisory relays, voltage sensing devices, and associated control circuitry to Automatic Reclosing

## Slide 4: Implementation Plan – Overview
The PRC-005-6 Implementation Plan addresses:
  The implementation of changes relating to maintenance and testing of Automatic Reclosing and Sudden Pressure Relay devices
  The phased implementation approach included in PRC‐005‐2 will remain as‐is and is carried forward and incorporated by reference
  This implementation plan replaces all previous PRC-005 implementation plans
  PRC‐005‐2(i) will remain in effect until entities are required to be compliant with R1, R2, and R5 of PRC‐005‐6 under this implementation plan

## Slide 5: Implementation Plan – Considerations
The Implementation Plan considers the following:
  PRC‐005‐6 establishes minimum maintenance activities and maximum allowable maintenance intervals for Protection System, Automatic Reclosing, and Sudden Pressure Relaying Components
  The maintenance activities may not be presently performed by some registered entities and the established maximum allowable intervals may be shorter than those currently in use by some entities
  The implementation schedule carries forward and incorporates by reference the implementation schedules contained in all previous PRC-005 implementation schedules

## Slide 6: Implementation Plan – General
General Considerations:
  Each entity shall maintain documentation to demonstrate compliance with PRC‐005‐1.1b, PRC‐008‐0, PRC‐011‐0, and PRC‐017‐0 until that entity meets all of the requirements of PRC‐005‐6 in accordance with this implementation plan
  Each registered entity must be prepared to identify whether its applicable Protection System, Automatic Reclosing, and Sudden Pressure Relaying Components were last maintained according to PRC‐005‐6, or PRC‐005‐1.1b, PRC‐008‐0, PRC‐011‐0, PRC‐017‐0, or a combination thereof
    Complete the PRC-005 Spreadsheet Template that is provided with the engagement notification package

## Slide 7: Resources
FAQ, plans, timelines, and reference documents:
  PRC-005-2 Implementation Plan
    http://www.nerc.com/pa/Stand/PRC0052RD/Project_2007-17_Implementation_Plan_Clean_errata.pdf
  PRC-005-2 R3 and R4 Implementation Timelines
    http://www.nerc.com/pa/Stand/PRC0052iRD/PRC-005-2_R3_and_R4_Implementation_Timelines.pdf
  PRC-005-2 Supplementary Reference and FAQ
    http://www.nerc.com/pa/Stand/PRC0052RD/Project_200717_Protection_System_Maintenance_and%20T_Supplementary_Reference_clean_10-2012_2.pdf
  PRC-005-2(i) Implementation Plan (Update)
    http://www.nerc.com/pa/Stand/PRC0052iRD/PRC-005-2i%20Implementation%20Plan%20Errata%20clean.pdf
  PRC-005-6 Implementation Plan
    http://www.nerc.com/pa/Stand/PRC0056RD/PRC-005-6_Implementation_Plan_clean_2015Oct09.pdf

## Slide 8: Questions?