## Slide 1
Update Multi-Interval Real Time Market Prototype
SAWG
02/22/2016

## Slide 2: MIRTM Update
Status:
  First iteration of MIRTM prototype coding completed
  Software Testing in progress
Next Steps:
  Update “Proposed Study Process MIRTM” to address inclusion of Fast Generation Resources
    http://www.ercot.com/content/wcm/key_documents_lists/51007/Proposed_Study_Process_MIRTM.doc
  ERCOT will give presentation on the mathematical model of the MIRTM prototype once the software is ready for conducting studies
  Request clarification on the Offer, Temporal constraints data to be used for Fast Generation Resources
      Generic?
      Verifiable?
      Other?
Notes: Slide #5

## Slide 3: MIRTM update
General Features MIRTM prototype:
Study period 30 minutes
Telemetered ramp rates used for entire study period
Telemetered status used for entire study period
Ramp Rate constraints coupling intervals in study period
Notes: Slide #5

## Slide 4: MIRTM update
Load Resource Modelling
Parameters:
  Single part Energy Bid to Buy $/MWh (Not to exceed price, MW)
    Same Energy Bid for all intervals in study period
  Ramp Period (start time): Advance notice required
  Minimum Run Time: If struck, the minimum time that the Load Resource is curtailed
  Maximum Run Time: If struck, the maximum time that the Load Resource can be curtailed
  Return to Service Time: After recall, the time period when Load Resource is not available to MIRTM
MIRTM will not consider a Load Resource if its Ramp Period + Minimum Run Time is more than the study period (30 minutes)
Maximum Run Time and Return to Service Time are partially managed outside the MIRTM engine
Notes: Slide #5

## Slide 5: MIRTM update
Load Resource Modelling
Request Clarification (Settlements issue):
For what time period is a Load Resource eligible for Make Whole IF Real-Time binding LMP does not materialize?
  Options:
    Fixed number of 15 minute settlement intervals (e.g. 1)
    Other ?
Notes: Slide #5

## Slide 6: MIRTM update
Fast Generator Resource Modelling
Parameters:
  Three Part Offer (Temperature dependent StartUp Cost $, Minimum Energy Cost @LSL, EOC)
  Temperature dependent Start Time (Hot, Intermediate, Cold)
  Minimum On Time
  Minimum Off Time
  StartUp and Shutdown constraints to cycle Fast Generator Resources
MIRTM will not consider a Fast Generator Resource if its applicable temperature dependent StartTime+ Minimum On Time is more than the study period (30 minutes)
Notes: Slide #5