## Slide 1
Update on NPRR615 PVGR Forecasting
ERCOT Staff
March 1, 2016

## Slide 2: ERCOT Solar Installations by Year

## Slide 3: Solar Forecast Implementation
Conducted RFP selecting MDA as our Solar Forecast vendor
Pass solar observation data to MDA every 5 minutes
Receive solar forecast from MDA hourly for the next 168-hour and distribute that to the Solar QSEs
The Solar QSEs use that forecast to update their COP

## Slide 4: Current Operating Plan (COP) Submission
3.9.1 Current Operating Plan (COP) Criteria
(8) For the first 168 hours of the COP, a QSE representing a Wind-powered Generation Resource (WGR) must enter an HSL value that is less than or equal to the amount for that Resource from the most recent Short-Term Wind Power Forecast (STWPF) provided by ERCOT, and a QSE representing a PhotoVoltaic Generation Resource (PVGR) must enter an HSL value that is less than or equal to the amount for that Resource from the most recent Short-Term PhotoVoltaic Power Forecast (STPPF) provided by ERCOT.

## Slide 5: COP Submission
All photovoltaic solar units are updating their COP on an hourly basis.
Chart: February 24th Aggregate Hour Ahead COP performance
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Forecast | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13.1 | 106.7 | 173.1 | 179.7 | 174.3 | 172.8 | 173.9 | 175.8 | 174.3 | 156 | 66.3 | 1.9 | 0 | 0 | 0 | 0 | 0
COP_hour Ahead | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 13.1 | 106.7 | 173.1 | 179.7 | 174.3 | 172.8 | 173.9 | 175.8 | 174.3 | 156 | 67.4 | 1.9 | 0 | 0 | 0 | 0 | 0