## Slide 1: PLWG Update to ROS
March 3, 2016

## Slide 2: PLWG Feb Meeting
Approve revisions to PLWG Whitepaper
  Corrects error in Table.
  Revises recommended method for modeling DC-ties
Request Direction on:
  Stability Issues Identified During FIS
  Clarification of Planning Guide Section 6.9(a)

## Slide 3: FIS Stability Study Issue
March 3, 2016

## Slide 4: Background
Recently there has been an increase in the number of stability issues identified in generation interconnection full interconnection studies (FIS)
This is likely due to: (1) better study tools and techniques to identify problems; and (2) more inverter based generators connecting to weaker parts of the system
Given the number of solar and wind generators under study this trend is likely to amplify going forward
Currently, the only way for ERCOT Operations to manage these stability constraints is through the use of Generic Transmission Constraints (GTC)

## Slide 5: Problem
The management of GTCs in ERCOT involves a lot of manual effort
The situational awareness tools and GTC processes were set up under the assumption that there would only be a few GTCs on the system
Currently, there are 7 operational GTCs with at least 5 additional proposed by the end of 2016
The current tools and processes are not sustainable for more than a handful of GTCs

## Slide 6: Solution Option 1
Change the “grid code” requirements in ERCOT such that generators are required to mitigate any stability issues identified in the FIS prior to energization

## Slide 7: Solution Option 2
Require TSPs to mitigate any stability issues identified in the FIS prior to resource energization

## Slide 8: Solution Option 3
ERCOT takes a more conservative approach to managing GTCs
(This is likely the short term solution until a long-term option is implemented)

## Slide 9: Solution Option 4
ERCOT procures tools and/or hires additional resources to reliably manage a large number of GTCs
This is likely to have a significant budget impact on ERCOT and probably wouldn’t happen until the 2018 budget cycle at the earliest

## Slide 10: Conclusion
A hybrid option could involve a combination of the above options. As an example, based on severity of the instability, Resource Entities or TSPs could be required to mitigate the instability. ERCOT could manage via a GTC for more widespread issues
PLWG is asking for direction on this issue before being able to address related topics including:
  Confidentiality issues surrounding FIS stability studies
  Timing issues related to the completion of the FIS and commissioning of resources

## Slide 11: Clarification of Planning Guide Section 6.9(a)

## Slide 12: Clarification of Planning Guide Section 6.9(a)
CenterPoint reported more than 5 GW(2.8 GW of Capacity at Peak) of generation meeting all requirements of 6.9 except for a completed RARF.
Indications are that ERCOT is following the Planning Guide
Planning Guide 6.9 – three sections reference requirement
  (1)(a)- The Interconnecting Entity (IE) provides all data required in the Resource Registration Glossary;
  (3)The IE shall provide to ERCOT the data necessary to model the Generation Resource in the base cases created and maintained by SSWG, SPWG, and the DWG, as directed by ERCOT.
  (4)Once the IE has met these requirements, ERCOT will notify the SSWG, SPWG, and the DWG, and the proposed Generation Resource will be included in the base cases created and maintained by these working groups.

## Slide 13: Clarification of Planning Guide Section 6.9(a)
Possible solutions include revising Section 6.9 to allow for use of data used in an FIS.
May require coordination with RDWG.
Does ROS want PLWG to review and recommend Planning Guide Changes?