## Slide 1
WRUC – Long Lead Time Commitments
QSE Manager’s Working Group
ERCOT Operations
March 23, 2016

## Slide 2: Long Lead Time Resources
To ensure that we have the long lead time resources online, we will notify participants when we initiate a WATCH due to inclement weather conditions and inform that we will be running SASM for an increase in AS for the inclement weather day.
WRUC relies upon accurate COP data.
The lack of accurate COPs data makes if very difficult for the Operator to review and act upon the results.
ERCOT has recently seen changes in the behavioral pattern of coal units specifically.

## Slide 3: Operator actions – Long Lead Time Resource Example
Operator runs WRUC after 1:00am Jan. 9th and confirms a resource is needed to solve congestion starting Jan.11 at 4:00am. Resource is off and available with a 36hr startup time for an Outage scheduled to last 4 days.
Jan. 9th, Issue an Electronic Dispatch Instruction (EDI), this data is also sent to S&B
Jan. 10th Unit1 is committed in DRUC for Jan. 11th
Jan 11th Unit 1 is committed in HRUC for Jan. 12th
Jan 12th Unit 1 is committed in HRUC for Jan. 13th
Jan 13th Unit 1 is committed in HRUC for Jan. 14th
HRUC will monitor to extend commitment if resource is needed for additional time.

## Slide 4: Settlement action – Long Lead Time Resource
Unit1 was not eligible for Start Up in the previous example.
  5.6.2 RUC Startup Cost Eligibility
  (c) The generation breakers must have been open, as indicated by a telemetered Resource status of Off-Line, for at least five minutes during the six hours preceding the first RUC-Committed Hour; and
  (d) The generation breakers must have been closed, as indicated by a telemetered Resource status of On-Line, for at least one minute during the RUC commitment period or after the determined five-minute open breaker, as indicated by a telemetered Resource status of Off-Line, in the six hours preceding the first RUC-Committed Hour.
Unit1 was eligible for Minimum Energy and received a Make Whole payment for each day.
The QSEs that were short at the DRUC/HRUC each day were charged for the next day’s RUC Make Whole.

## Slide 5: Long Lead Time Resources – Changes needed for S&B Startup eligibility?
One suggestion has been to have QSE dispute and put in a settlement adjustment to pay start up. Would require Protocol language change but no system impacts.
Are there concerns with this?
Other ideas?

## Slide 6
Questions?