## Slide 1
NPRR 649 Alternatives
Austin Rosel
Chad Thompson
Resmi Surendran
March 31, 2016

## Slide 2
Agenda
  Statistics on HDL Overrides
  Operational Improvements
  NPRR649 Discussion
  Option 1: Payment for Justified Losses
  Option 2: Override RN LMP
  Option 3: Enter Constraints above RN
  Future Operational Improvements
  Preliminary Cost Estimates

## Slide 3: Statistics on HDL Overrides

## Slide 4: Statistics on HDL Overrides
Year | Cumulative SCED intervals | 
 | In Minutes | In Days
Dec - 2010 | 36,927 | 25.64
2011 | 348,190 | 241.8
2012 | 141,971 | 98.59
2013 | 32,826 | 22.8
2014 | 1,200 | 0.83
2015 | 57 | 0.04
Operations has been working hard to reduce HDL overrides over time

## Slide 5: Operational Improvements
HDL overrides have been reduced over time due to the following reasons:
  Increased operator training:
    Don’t override to resolve SCED violated constraint unless the violation is greater than 125% Emergency rating, OR it is a cascading condition, OR an unsolved contingency, OR a base case overload
    Don’t do overrides to manually resolve conflicting constraints
  The ability for the operators to enter manual constraints
  The availability of new Generic Transmission Constraints
  Improvements in topology

## Slide 6: Reasons for current HDL Overrides
Operators are currently using HDL overrides to
  Pre-posture for Outages
    This is done only when the study before initialing the outage shows that there will be big post contingency overload as soon as the outage is taken. This helps to ensure reliability and to avoid large negative prices to units which have slow ramp rates.
  Ensure reliability against unsolved contingencies
    Significant overloading on a constraint could result in unsolved contingencies which would require manual action
  Reduce post-contingency flows which are above 125%
    due to potential IROL assessment requirements
  Resolve unit control system issues

## Slide 7: NPRR 649 discussion
ERCOT submitted NPRR649 to satisfy its obligations under a settlement agreement reached with Odessa Ector Power Partners, LP in Public Utility Commission of Texas (PUCT) Docket 41790.
NPRR649 provides a lost opportunity energy payment to compensate the QSE for cost reduced lost revenues from the HDL MW amount to the expected MW output of the resource if the HDL was not in place
On February 22, 2016 ERCOT filed additional comments to NPRR 649 to propose alternative methods for addressing QSE compensation for HDL manual overrides. The methodology (Option 1) proposed in the comments was an amendment to existing NPRR 649 language to limit the payment to actual attested losses.
Other approaches (Option 2 & 3) discussed at the March 11, 2016 workshop might effectively replace NPRR 649 language.

## Slide 8: Option 1: Payment for Justified Losses
Summary of ERCOT February 22 comments:
Replaces compensation of opportunity costs with actual losses suffered by QSEs in existing contract positions.
  Variable costs only
  May include DAM or bilateral energy contracts
QSEs claiming losses would have to provide:
  Attestation of loss
  Loss calculation
  Appropriate supporting documentation
Process for ERCOT review and acceptance of claim
The HDL override payment would be the lesser of the attested losses or the loss calculated in the existing NPRR.

## Slide 9: Option 1: Payment for Justified Losses
Summary calculation:
HDLOEAMT q, r, p, i = (-1) * Min {HDLOAL q, r, p, i, Max(0, ((RTSPPp, i – RTRSVPOR i – RTRDP i – HDLOAIECq, r, p, i ) * HDLOQTY q, r, p, i ))}
Where:
HDLOEAMT | High Dispatch Limit override amount
HDLOAL | High Dispatch Limit override attested losses
RTSPP | Real-Time Settlement Point Price
RTRSVPOR | Real-Time Reserve Price for On-Line Reserves
RTRDP | Real-Time On-Line Reliability Deployment price
HDLOAIEC | HDL override Average Incremental Energy Cost
HDLOQTY | HDL override quantity: difference between HDL override break point and AVGHDL due to an ERCOT-issued override

## Slide 10: Option 2: Override Resource Node LMP
Automated post process to override LMPs at the Resource node based on the Energy Offer Curve (EOC) for a Resource limited by manually overridden HDL
Based on most recent valid EOC for the impacted intervals that was received by ERCOT before the HDL override was issued.
If no curve exists for the interval, ERCOT will use the most recent Mitigated Offer Cap Curve for the impacted interval
Create new report to show the SCED calculated prices and the adjusted prices

## Slide 11: Option 2: Override Resource Node LMP
Problems with the overriding LMP :
  Inconsistency between BP and LMP could arise if multiple resources are connected to the Resource Node and only one Resource gets the override
    Totally 98 Resource Nodes have at least 2 Resources mapped (Maximum 6)
    Totally 42 EPS Meters have at least 2 Electrical Buses mapped (Maximum 3)
  How to determine LMP if multiple resources receive the override and they each have different EOCs.
  If multiple Resources with different Energy Offer Curves at the same RN all receive HDL override and adjusted price is calculated using average prices for each resource at the held BP for each resource then the adjusted LMP could be inconsistent with the BP for all of the Resources at these RNs.

## Slide 12: Resource Nodes with Multiple Resources
GEN 1
GEN 2
GEN 3
GEN 4
GEN 5
GEN 6
Transformer
EPS Meter
RN
    Totally 98 Resource Nodes have at least 2 Resources mapped (Maximum 6)
    Totally 42 EPS Meters have at least 2 Electrical Buses mapped (Maximum 3)

## Slide 13: Option 2: Override Resource Node LMP
Problems with the overriding LMP :
  There is no way to minimize the impact in DAM clearing of the RT HDL overrides that persists for multiple days
  If the Resource knows before hand that they will receive an override, then there could be potential issues including changing their Energy Offer Curve and purchasing Point to Points
  If there is override when there is no congestion in the system then this LMP change could cause price separation and hence possible PTP payout with out congestion.

## Slide 14: Option 3 : Enter Constraint above RN
Pre-position Network Model with a Manual Constraint associated with each Resource node
Change operator display to include the ability for the operator to pull up the TCM list of Manual Constraints by Resource Node. Operator would select the appropriate constraint and input the limiting value and the time duration that the constraint should be active.
The constraint would be passed to SCED with the limit and the duration which would appropriately set the price for the appropriate time period.
If the Operator believes the limit will be needed for the 2 or 3 Operating day out, Day Ahead Market Operator will be notified and constraint limit will be entered in TCM for market systems so as to activate the constraint in the Day Ahead Market.

## Slide 15: Option 3 : Enter Constraint above RN
Problems with constraints for Resources:
  Needs to be automated since manual activation of constraint can cause the constraint to be violated setting RN LMP at -$5k
  Operator training required since it would be dependent on operator selecting appropriate constraint
  Dependent on staff developing appropriate constraints for each unique resource node case
  Once developed, constraints must be maintained on an ongoing basis to keep up to date with the N/W model changes
  Setting of limits for DAM would still be manual

## Slide 16: Option 3 : Enter Constraint above RN

## Slide 17: Potential Operational Improvements
Possible procedure changes to further minimize the aforementioned current uses of HDL overrides
  Pre-posture for Outages
    Pre-posture only if the overload is greater than 125% or is cascading
  Ensure reliability against unsolved contingencies
    Manually model the constraint and manage it until the contingency solves at which case the standard thermal constraint can be used.
  Reduce post-contingency flows which are above 125%
  Resolve unit control system issues
    Call the QSE and inform them of the issue, requesting them to self-manage their Generation Resource to resolve their issue

## Slide 18: Preliminary Cost Estimates
  Option 1: Payment for Justified Losses
    100 - 150k
  Option 2: Override RN LMP
    50 - 100k
  Option 3: Enter Constraints above RN
    200 - 300k + ongoing 150hrs/yr impact

## Slide 19: Questions?