## Slide 1
PDCWG Report to ROS
Chair: Percy Galliguez, Brazos Electric Power Cooperative, Inc.
Vice Chair: Stewart Rake, Luminant
ROS
April 7th, 2016

## Slide 2: Report Overview & Notes
Report Overview
  Meeting Minutes
  BAL-001-TRE-1 FMEs & IMFR
    No FME’s in the month of March
  Frequency Control Report

## Slide 3: Meeting Minutes
PDCWG Meeting 3/9/16
  Regulation & Frequency Control Reports
  GREDP Performance Analysis
  BAL-001-TRE-1 Mitigation Plan Requirements
    Section C 2.1 of Regional Standard
  Reviewed 3 (non-FME) ERCOT Frequency Disturbance
    2/2/2016 @ 1217
      Loss of 375 MW
      648 MW/0.1HZ Response
    2/18/2016 @ 2107
      Loss of 468 MW
      665 MW/0.1HZ Response
    3/8/2016 @ 1018
      Loss of 468 MW
      588 MW/0.1HZ Response
  FRRS Deployment Discussion

## Slide 4: Frequency Measurable Events Performance
March 2016

## Slide 5: Frequency Measurable Events
No FMEs during the month of March.

## Slide 6: Interconnection Minimum Frequency Response (IMFR) Performance

## Slide 7: Frequency Control Report
January 2016

## Slide 8: CPS1 Performance
CPS1 12 Month Rolling Average = 175.53%

## Slide 9: RMS1 Performance of ERCOT Frequency

## Slide 10: Frequency Profile Analysis

## Slide 11: Time Error Corrections
There was two Time Error Corrections (TEC) in March.

## Slide 12: Wind Generation Performance

## Slide 13: Wind Generation Performance

## Slide 14: Wind Generation Performance
Record: 21.43% Wind Penetration
(previous record 19.87% in February 2016)

## Slide 15
Questions?