## Slide 1
Market Update
QSE Managers Working Group
Jeff Gilbertson
ERCOT Market Analysis
4/15/2016

## Slide 2: Supplemental Ancillary Services Market (SASM) Update
3/31 SASM executed due to undeliverability
  System conditions on 3/31
    High RT SPPs system-wide, with highest SPPs in the South Load Zone, and many violated constraints
    SILAS_SILAS_10 HRUC HE14-22 for valley import

## Slide 3: RUC Congestion Rent Discussion
Most interest is in intervals for which RUC resource completely eliminates congestion when operating at LSL, which removes any congestion price signal
Assignment to rerun SCED for 2015 RUC intervals by ONLY setting LDL of RUC resource to zero, no other changes
  RUC resource EOC RUC floor applied at $1500
  Base Point > 0 may provide an indication of need as well as provide congestion price signal
  Study does not account for scenarios in which RUC LSL MW caused monitored element flow to be lower than threshold for activating constraint, thus the constraint did not get activated or got deactivated. A Base Point > 0 may have resulted if the appropriate constraint was active.

## Slide 4: SCED Analysis
Only 2015 SCED intervals where original RUC BP = LDL

## Slide 5: SASM Timeline Proposal
Protocols require time between SASM Notification and beginning of first awarded hour to be >= 2 hours
X
X+30 min
X+35 min
X+45 min
X+60 min
Start of Awarded Hour
Notify Market
Determine AS amount?
Execute SASM
Award Notification
COP Updated
7:00
7:30
7:35
7:45
9:00
HE10
8:00 COP Deadline for HE10
15 min to update COP
1 hour 15 min to prepare Resource

## Slide 6: SASM Timeline Proposal
Proposed to decrease this requirement to >= 1.5 hours
No COP update, and minor timeline change
X
X+30 min
X+40 min
X+60 min
Start of Awarded Hour
Determine AS amount and Notify Market
Execute SASM
Award Notification
COP Updated
7:30
8:00
COP and AS Offer Deadline for HE10
8:10
9:00
HE10
50 min to prepare Resource