## Slide 1
Settlement of Ancillary Service Infeasibility
ERCOT
QMWG
April 15, 2016

## Slide 2: Settlement Treatment for Replacement of Infeasible Ancillary Services
General Settlement Principles for discussion with QMWG:
The QSE with the infeasible AS will be charged the DAM clearing price regardless whether the responsibility was awarded, self-arranged, or traded, and regardless of whether a SASM is executed.
The replacement cost, if any, is charged to all QSEs based on LRS.
The QSE with the AS infeasible is not directly charged the full replacement cost, if any.
All revenues collected from charges to QSEs due to infeasible AS are paid to all QSEs based on LRS.

## Slide 3: Settlement Treatment for Replacement of Infeasible Ancillary Services
Definition of Ancillary Service being Undeliverable
The terms undeliverable and infeasible are used interchangeably in the Protocols
ERCOT believes the term undeliverable is misleading and will provide additional clarity in the NPRR.

## Slide 4: Questions Raised at March 2016 QMWG Meeting
ERCOT was asked to provide samples of Resource AS Responsibility being infeasible
3 distinct scenarios have been discussed
Reserved Resource capacity needed to solve transmission congestion
  Resource deployment needs to be between HSL and HASL or LASL and LSL to solve the congestion
  May be detected in HRUC or in real-time
  Common reason for AS being deemed infeasible
Reserved Resource capacity needed to match expected supply and demand
  Resource deployment needs to be between HSL and HASL or LASL and LSL to solve the congestion
  Detected in HRUC
  Expectation that AS would not be deemed infeasible and that AS would be deployed in real-time as needed
Physical deployment of AS would negatively effect transmission congestion
  For example, Reg. Up deployments on a Resource with a hurting shift factor on a constraint results in overloads that cannot be managed by SCED
  This is not captured in HRUC and would be rare for deeming as infeasible
  Likely needs Protocol clarification

## Slide 5: Questions Raised at March 2016 QMWG Meeting
ERCOT was asked to provide samples of Resource AS Responsibility being infeasible
Non-Spin is unique from other AS regarding infeasibility
Unlike other AS, Non-Spin can be deployed for solving local transmission congestion
Current operational practice is to not deem Non-Spin capacity infeasible when it is needed for transmission congestion and to deploy the Non-Spin on that specific Resource, as necessary
  Not intending to change this practice

## Slide 6: Questions Raised at March 2016 QMWG Meeting
ERCOT was asked to provide a sample of an AS Responsibility declared infeasible due to transmission constraints for Regulation Down
Example:
Resource with a 50% hurting shift factor on the constraint
SCED constraint flow is 4 MW greater than the limit
Resource must be dispatched down 8 additional MW to resolve the constraint (from 110 to 102)
Chart: Time Stamp
| 0.33333333333333331 | 0.33680555555555558 | 0.34027777777777773 | 0.34375 | 0.34722222222222199 | 0.35069444444444497 | 0.35416666666666702 | 0.35763888888888901 | 0.36111111111111099 | 0.36458333333333398
HSL | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200 | 200
LSL | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
LASL | 110 | 110 | 110 | 110 | 110 | 110 | 100 | 100 | 100 | 100
BP | 150 | 150 | 150 | 110 | 110 | 110 | 102 | 102 | 102 | 102
No
Constraint
Constraint
Resolution Limited by LASL
Reg. Down Relocated and Constraint Fully
Resolved by SCED

## Slide 7: Questions Raised at March 2016 QMWG Meeting
RTASOLIMBq =
ERCOT was asked to explain the impact of AS infeasibility on AS Imbalance
Online Capacity in Real-Time:
RTASOLIMB | Real Time Ancillary Service On-Line Reserve Imbalance
RTOLCAP | Real-Time On-Line Reserve Capacity
RTASOLIMB
RTOLCAPq
– Online Capacity already reserved
Reserved

## Slide 8: Questions Raised at March 2016 QMWG Meeting
RTASOLIMBq =
ERCOT was asked to explain the impact of AS infeasibility on AS Imbalance
Online Capacity in Real-Time:
RTASOLIMB | Real Time Ancillary Service On-Line Reserve Imbalance
RTOLCAP | Real-Time On-Line Reserve Capacity
RTASOLIMB
RTOLCAPq
– Online Capacity already reserved
(Reserved – AS Undeliverable)

## Slide 9: Ancillary Service On-Line Reserve Imbalance
RTASRESP | Real-Time Ancillary Service Supply Responsibility
RTASOFF | Real-Time Ancillary Service Schedule for the Off-Line Generation Resource
RTRUCNBBRESP | Real-Time RUC Ancillary Service Supply Responsibility in Non-Buy-Back hours
RTCLRNSRESP | Real-Time Controllable Load Resource Non-Spin Responsibility
RTRMRRESP | Real-Time Ancillary Service Supply Responsibility for RMR Units
RTASOLIMBq = RTOLCAPq – [(RTASRESPq * ¼) – RTASOFFq
– RTRUCNBBRESPq – RTCLRNSRESPq – RTRMRRESPq]
The Real-Time Ancillary Service Supply Responsibility will be reduced by the MW of infeasible AS, which will increase the Real Time Ancillary Service On-Line Reserve Imbalance volume used in the calculation of the Real-Time Ancillary Service Imbalance Amount payment.
RTASIAMTq = (-1)* [(RTASOLIMB q * RTRSVPOR) +
(RTASOFFIMB q * TRSVPOFF)]

## Slide 10: Questions Raised at March 2016 QMWG Meeting
ERCOT was asked to explain impact of an AS Responsibility declared infeasible due to transmission constraints on DAM Make Whole Payments
Day-Ahead Make-Whole Payment
DAM Guaranteed Amount
(
)
(
)
<
DAM
Revenues
  A QSE will receive a Make-Whole Payment if its revenues from the DAM are less than the Startup, Minimum Energy, and Operating costs

## Slide 11: Day-Ahead Make-Whole Payment
What if revenues are less than costs?
Difference = Make-Whole Payment
Day-Ahead Market Sales
$
Make-Whole Payment
Costs Incurred
Revenues Received
Incremental Energy Costs
Minimum Energy Costs
Start-up Costs

## Slide 12: Day-Ahead Make-Whole Payment
What if revenues are greater than costs?
Day-Ahead Market Sales
$
Costs Incurred
Revenues Received
Incremental Energy Costs
Minimum Energy Costs
Start-up Costs
No Make-Whole Payment
Day-Ahead Market Sales = DAM Energy Sales * SPP + AS Sales * MCPC

## Slide 13: Day-Ahead Make-Whole Payment
Energy Sales * SPP + AS Sales * MCPC
Day-Ahead Market Sales
$
No Make-Whole Payment
Without AS Sales
With AS Sales
Day-Ahead Market Sales
Make-Whole Payment
Energy Sales * SPP

## Slide 14: Day-Ahead Make-Whole Payment
Should DAM AS Revenues be removed from Make Whole Payments if these are clawed back due to an AS Infeasible event?
  Creates a dependency whenever ERCOT settles DAM (Requires Resettlement)
  Historically few instances of AS Infeasibility. May not justify changing DAM Make whole settlement equations
  Creates System impact to modify settlement equations

## Slide 15: Settlement Treatment for Replacement of Infeasible Ancillary Services
General Settlement Principles for discussion with QMWG:
The QSE with the infeasible AS will be charged the DAM clearing price regardless whether the responsibility was awarded, self-arranged, or traded, and regardless of whether a SASM is executed.
The replacement cost, if any, is charged to all QSEs based on LRS.
The QSE with the AS infeasible is not directly charged the full replacement cost, if any.
All revenues collected from charges to QSEs due to infeasible AS are paid to all QSEs based on LRS.

## Slide 16
Appendix

## Slide 17
Ancillary Services Replacement
Presenter: Ino González
QMWG
July 10, 2015

## Slide 18: Replacement of Undeliverable Ancillary Services
NP 6.4.9.1.2 Replacement of Undeliverable Ancillary Service
Due to Transmission Constraints
(4) If ERCOT procures additional Ancillary Services for the amount of substituted capacity that is deemed infeasible or the amount of Ancillary Services capacity that each affected QSE does not replace, then all QSEs that bought the specific Ancillary Service in the DAM are charged for their share of the net cost incurred for the Ancillary Service procured by ERCOT as part of the multiple procurement processes (DAM and SASMs) , in accordance with Section 6.7.3, Adjustments to Cost Allocations for Ancillary Services Procurement.

## Slide 19: Replacement of Undeliverable Ancillary Services
NP 6.4.9.1.2 Replacement of Undeliverable Ancillary Service Due to Transmission Constraints
(5) If the QSE’s Ancillary Service capacity that is undeliverable because of a transmission constraint identified by ERCOT, as set forth in (1) above, was not awarded in the DAM or any SASM (i.e., the capacity is part of Self-Arranged Ancillary Services for the hours of the RUC Study Period), then the QSE is charged for the insufficient Ancillary Service capacity the same price paid for the Ancillary Service as purchasers in the DAM paid for that time period, as determined under paragraph (4) above.

## Slide 20: Replacement of Undeliverable Ancillary Services
NP 6.4.9.1.2 Replacement of Undeliverable Ancillary Service Due to Transmission Constraints
(6) If the QSE’s Ancillary Service capacity that is undeliverable because of a transmission constraint identified by ERCOT, as set forth in (1) above, was awarded in the DAM or any SASM, then the QSE is not compensated for the quantity of the Ancillary Service capacity that is undeliverable.

## Slide 21: Replacement of Undeliverable Ancillary Services
NP 6.7.3 Adjustments to Cost Allocations for Ancillary Procurement
Each QSE’s share of the net total costs for Reg-Up for the Operating Hour is calculated as follows:
RUCOST q = RUPR * RUQ q + Payment COLLECTED*HLRSq
Where:
RUPR = RUCOSTTOT / RUQTOT
RUQTOT = RUQ q
RUQ q = RUO q – SARUQ q +sasm
RUO q = Sum[SARUQ q + (RTPCRU q, m) + PCRU q – RURP q – RUFQ q] * HLRS q + RURP q
SARUQ q = DASARUQ q + RTSARUQ q

## Slide 22: Questions that need to be answered to develop an NPRR
Should QSEs be charged (claw back) for undeliverable MWs?
  Options: Based on replaced MW or Undeliverable MW quantities
    Note: Replaced MWs ≤ Undeliverable MWs
    Example: DAM Award (10MW), Undeliverable (7MW), RURP(5MW), MCPCRU ($3)
    DAM Payment = (-1)*10MW*$3/MWh = ($30)
      Claw back option 1= 7MW*$3/MWh = $21 (QMWG consensus)
      Claw back option 2 = 5MW**$3/MWh = $15
To what extend QSEs with self-arrange MWs are responsible for undeliverable quantities?
  Should QSEs with DAM Obligations be charged when the self-arranged MWs are part of a trade that is undeliverable? (Yes, QMWG consensus)
Other policy questions?