## Slide 1: ERCOT-Directed dispatch of price responsive distributed generation
Distributed Resources Energy and Ancillary Service Market (DREAM) Proposed Protocol Revisions
Shell Energy North America March 2016

## Slide 2: DEFINITIONS & Cautionary Note
Reserves: Our use of the term “reserves” in this presentation means SEC proved oil and gas reserves.
Resources: Our use of the term “resources” in this presentation includes quantities of oil and gas not yet classified as SEC proved oil and gas reserves. Resources are consistent with the Society of Petroleum Engineers 2P and 2C definitions.
Organic: Our use of the term Organic includes SEC proved oil and gas reserves excluding changes resulting from acquisitions, divestments and year-average pricing impact.
Resources plays: Our use of the term ‘resources plays’ refers to tight, shale and coal bed methane oil and gas acreage.
The companies in which Royal Dutch Shell plc directly and indirectly owns investments are separate entities. In this presentation “Shell”, “Shell group” and “Royal Dutch Shell” are sometimes used for convenience where references are made to Royal Dutch Shell plc and its subsidiaries in general. Likewise, the words “we”, “us” and “our” are also used to refer to subsidiaries in general or to those who work for them. These expressions are also used where no useful purpose is served by identifying the particular company or companies. ‘‘Subsidiaries’’, “Shell subsidiaries” and “Shell companies” as used in this presentation refer to companies in which Royal Dutch Shell either directly or indirectly has control. Companies over which Shell has joint control are generally referred to as “joint ventures” and companies over which Shell has significant influence but neither control nor joint control are referred to as “associates”. The term “Shell interest” is used for convenience to indicate the direct and/or indirect ownership interest held by Shell in a venture, partnership or company, after exclusion of all third-party interest.
This presentation contains forward-looking statements concerning the financial condition, results of operations and businesses of Royal Dutch Shell. All statements other than statements of historical fact are, or may be deemed to be, forward-looking statements. Forward-looking statements are statements of future expectations that are based on management’s current expectations and assumptions and involve known and unknown risks and uncertainties that could cause actual results, performance or events to differ materially from those expressed or implied in these statements. Forward-looking statements include, among other things, statements concerning the potential exposure of Royal Dutch Shell to market risks and statements expressing management’s expectations, beliefs, estimates, forecasts, projections and assumptions. These forward-looking statements are identified by their use of terms and phrases such as ‘‘anticipate’’, ‘‘believe’’, ‘‘could’’, ‘‘estimate’’, ‘‘expect’’, ‘‘intend’’, ‘‘may’’, ‘‘plan’’, ‘‘objectives’’, ‘‘outlook’’, ‘‘probably’’, ‘‘project’’, ‘‘will’’, ‘‘seek’’, ‘‘target’’, ‘‘risks’’, ‘‘goals’’, ‘‘should’’ and similar terms and phrases. There are a number of factors that could affect the future operations of Royal Dutch Shell and could cause those results to differ materially from those expressed in the forward-looking statements included in this presentation, including (without limitation): (a) price fluctuations in crude oil and natural gas; (b) changes in demand for Shell’s products; (c) currency fluctuations; (d) drilling and production results; (e) reserves estimates; (f) loss of market share and industry competition; (g) environmental and physical risks; (h) risks associated with the identification of suitable potential acquisition properties and targets, and successful negotiation and completion of such transactions; (i) the risk of doing business in developing countries and countries subject to international sanctions; (j) legislative, fiscal and regulatory developments including potential litigation and regulatory measures as a result of climate changes; (k) economic and financial market conditions in various countries and regions; (l) political risks, including the risks of expropriation and renegotiation of the terms of contracts with governmental entities, delays or advancements in the approval of projects and delays in the reimbursement for shared costs; and (m) changes in trading conditions. All forward-looking statements contained in this presentation are expressly qualified in their entirety by the cautionary statements contained or referred to in this section. Readers should not place undue reliance on forward-looking statements. Additional factors that may affect future results are contained in Royal Dutch Shell’s 20-F for the year ended 31 December, 2015 (available at www.shell.com/investor and www.sec.gov ). These factors also should be considered by the reader. Each forward-looking statement speaks only as of the date of this presentation, April 12, 2016. Neither Royal Dutch Shell nor any of its subsidiaries undertake any obligation to publicly update or revise any forward-looking statement as a result of new information, future events or other information. In light of these risks, results could differ materially from those stated, implied or inferred from the forward-looking statements contained in this presentation. There can be no assurance that dividend payments will match or exceed those set out in this presentation in the future, or that they will be made at all.
We use certain terms in this presentation, such as discovery potential, that the United States Securities and Exchange Commission (SEC) guidelines strictly prohibit us from including in filings with the SEC. U.S. Investors are urged to consider closely the disclosure in our Form 20-F, File No 1-32575, available on the SEC website www.sec.gov. You can also obtain this form from the SEC by calling 1-800-SEC-0330.
Shell Energy North America March 2016 2

## Slide 3: Agenda
Introduction
Impetus and Rationale
Goal and Scope
Details / Proposed Market Structure
Qualitative Benefits
Quantitative Benefits
Shell Energy North America March 2016 3

## Slide 4: Introduction
ERCOT’s Technical Advisory Committee (TAC) established the Distributed Resource Energy or Ancillary Service Market (DREAM) task force to investigate the current regulatory and market framework for distributed energy resource (DER) participation.
The DREAM Task Force reviewed specific topics while considering process improvements, equity with traditional resources, practicality of implementation, and system reliability.
DER Concept Paper
Process
Practicality
Reliability
Equity
Shell Energy North America March 2016 4
Notes: Photo Credit – G Thurnher SENA

## Slide 5: Impetus and Rationale
By the end of 2016, 79% of the ERCOT DG portfolio will be dispatchable (non-renewable)
Shell Energy North America March 2016 5
Notes: Shell created Graph, from publically available data on the PUCT website.

## Slide 6: Impetus and rationale
These resources exist as two distinct populations on the ERCOT Grid: price-responsive Distributed Generation, and price-taking Distributed Generation.
Renewable DG does not vary output based upon market price
Dispatchable DG can respond quickly to changes in market price
Shell Energy North America March 2016 6
Cutten Rd. Business Park 9.375MW
Retrieved from http://www.erockhold.com/
Notes: Permission to use granted by Enchanted Rock LLC, screenshot from their public website.

## Slide 7: Impetus and Rationale
ERCOT’s high System Wide Offer Cap and associated potential for extremely high, short-duration prices likely encourage market participants to seek out a low-cost, low-utilization, highly-responsive physical hedge.
Shell Energy North America March 2016 7
Potomac Economics, LTD. (2015). 2014 State of the Market Report for the ERCOT Wholesale Electricity Markets
Retrieved from: https://www.potomaceconomics.com/uploads/ercot_documents/2014_ERCOT_State_of_the_Market_Report.pdf

## Slide 8: Impetus and Rationale
Diesel and Nat-Gas reciprocating engines can
Connect at distribution voltage, avoid high interconnection costs
Be “right-sized” and dispersed across the system
Respond to price within a 1-5 minute interval
Shell Energy North America March 2016 8
Cutten Rd. Business Park 9.375MW
Retrieved from http://www.erockhold.com/
Notes: See Slide 6, same source

## Slide 9: Impetus and Rationale
Under current market rules, when distributed generation deploys, it appears as if load/consumption decreases.
An apparent reduction in load, in turn, reduces price. In reality, load did not decrease. Rather, load is served by DG.
Must-take energy
Renewables
Thermal-Dispatchable
Peaking Resources
Marginal Resource
Distributed Resources (not in offer stack)
DG deployment looks like a reduction in load
Adjusted Marginal Resource Post DG Deployment
Quantity (MW)
Price ($/MWHr)
Shell Energy North America March 2016 9
Notes: Shell drawing for illustration purposes, does not represent actual market data. For explanation purposes only.

## Slide 10: Impetus and Rationale
If wholesale resources were all serving load, then price would be set by economic merit-order.
The last resource deployed in a given interval would establish price.
Deployed Distributed Resources contribute to price reversal rather than price formation.
Shell Energy North America March 2016 10

## Slide 11: Impetus and Rationale
Load always has the right to not consume, which may include self-service of all or part of their electricity needs.
Generation connected to the distribution system that is always a source to the grid, without load, is truly a resource, rather than a load off-setting its consumption.
Interconnection Voltage may define the ability of a resource to provide an equitable contribution to the price formation, rather than price-responsiveness of that resource.
Shell Energy North America March 2016 11
Notes: Bullet 3 is a statement of fact, if a resource selects to connect to the grid at a particular voltage, it will determine how that resource contributes to price formation.

## Slide 12: Goal and Scope:
Establish a marketplace where price-taking and price responsive resources can co-exist in an efficient marketplace.
ERCOT
Price Responsive
DG
Load with onsite DG
Price-taker DG
Wholesale Resources
Offer to Sell
Dispatch Instruction
Must-take energy
Must-serve load
Shell Energy North America March 2016 12

## Slide 13: Goal and Scope
Adjust market rules to allow DG to express its willingness to sell as an offer to SCED.
When a load-zone price reaches a DG offer curve, the resource will deploy in a coordinated, ERCOT directed dispatch.
Must-take energy
Renewables
Thermal-Dispatchable
Peaking Resources
Marginal Resource
$ Responsive DG in offer stack
Quantity (MW)
Price ($/MWHr)
DG can set marginal price
Shell Energy North America March 2016 13
Notes: Shell drawing for illustration purposes, does not represent actual market data. For explanation purposes only.

## Slide 14: Details / Proposed Market Structure
Modify market rules to allow price-responsive DG to
Express their willingness to sell as an offer to SCED
  Telemeter resource availability
  Telemeter offer curve
Deploy Price Responsive DG based upon a load-zone price
  When LZ price reaches DG SCED offer, deploy and follow SCED base points.
  DG can set marginal price
  Output mapped to logical transmission injection point
Exclude participation in CRR Markets
  Maintain status quo practice / All DG is hedged to Load Zone
  Simplify CRR markets by excluding 7,000+ DG sites
Shell Energy North America March 2016 14

## Slide 15: Details / Proposed Market Structure
Modify market rules to allow price-responsive DG to
Participate in SCED as an option
  Maintain the ability for Load to off-set production with on-site DG
  Create option for price-responsive resources to deploy efficiently
Participate in current DG 10/30 Min Products
  Exclude participation from RRS, Non-spin (similar to ERS-10, ERS-30)
  Exclude, temporarily, participation from Regulation
    If distributed storage resources emerge as a low-opportunity cost provider of regulation, then re-visit market rules to allow for participation.
    Existing distributed storage is not competitive with low-opportunity cost wholesale resources providing regulation.
Shell Energy North America March 2016 15

## Slide 16: Qualitative Benefits:
Expanding the scope of price-responsive loads and resources in SCED more accurately reflects price elasticity of demand.
Shell Energy North America March 2016 16
Hogan, W. W. (2010). Scarcity Pricing and Locational Operating Reserve Demand Curves.
Retrieved from http://www.hks.harvard.edu/fs/whogan/Hogan_FERC_060210.pdf
Notes: Web Publication Hogan, William, “An ERCOT Window of Opportunity”
Hogan, W. W. (2010). Scarcity Pricing and Locational Operating Reserve Demand Curves.
Retrieved from http://www.hks.harvard.edu/fs/whogan/Hogan_FERC_060210.pdf

## Slide 17: Qualitative benefits
Inclusion of price-responsive DG in SCED
Contributes to price formation
Improves ERCOT situational awareness.
Improves market awareness of aggregated resource base / resource adequacy.
Shell Energy North America March 2016 17

## Slide 18: Quantitative Benefits
IF the 588MW of diesel/ Nat Gas had responded to price for the 16 hours above a diesel strike price, THEN Market Revenues were reduced by over $18M (2015)
$18M reduction in Market Revenue
Marginal Resource
DG not in Stack
DG deployment looks like a reduction in load
Adjusted Marginal Resource Post DG Deployment
Price ($/MWHr)
Shell Energy North America March 2016 18
Notes: Shell drawing for illustration purposes, does not represent actual market data. For explanation purposes only.

## Slide 19: Questions?
Shell Energy North America March 2016 19