## Slide 1: Summary of NERC HILF Activities
John Brockhan
April 26, 2016

## Slide 2: Summary of NERC HILF Activities
Background
  HILF Workshop held in November 2009.
  United States’ Congressional Staff, DOD, DHS, DOE, DHHS, EMP Commission, and FERC.
  IOUs, Coops, & municipal utilities
  Produced a report that was approved by NERC BOT May 2010
  Identified HILF risks
    Coordinated Cyber, Physical, or Blended Attack
    Pandemic
    GMD
    EMP

## Slide 3: Summary of NERC HILF Activities
Common Framework Approach
  HILF risks present unique threats to the electric sector
  Have a number of characteristics in common:
    Potential to cause widespread or catastrophic impact to the sector
    Generally originate through external forces outside the control of the sector
    Can occur very quickly and reach maximum impact with little warning
    Little real-world operational experience generally exists
    Probability of HILF risks’ occurrence and impact is difficult to quantify

## Slide 4: Summary of NERC HILF Activities
Placing HILF Risk in Context
  HILF risks are only part of a much larger list of priorities facing the electric sector
  Will require re-allocation of already strained human and financial resources
  Managing HILF risks must be placed in an appropriate context
    A parallel goal must be to keep electricity affordable
    Sector cannot expect to “gold plate” the system.
    It is impossible to fully protect the system from every threat

## Slide 5: Summary of NERC HILF Activities
  HILF risk must take a holistic approach
    protection
    resilience
    restoration
  Mitigation steps taken to address HILF risk should have no unintended reliability consequences
    Cannot increase risks from other, more common, threats

## Slide 6: Summary of NERC HILF Activities
GMD Risk
  Geomagnetic storms produce impulsive disturbance of the Earth’s geomagnetic field
  Can induce currents called geomagnetically-induced currents (GIC)
  Geographical locations (latitude) and geologic properties can impact the potential for GIC to be induced
  EHV (345kV and higher) more susceptible to GIC
  March 13-14, 1989 geomagnetic storm led to the collapse of the Hydro Québec system
  Collapse only took 92 seconds

## Slide 7: Summary of NERC HILF Activities
NERC/Electric sector response
  NERC Reliability Standard EOP-010-1 became effective April 1, 2015.
    Requires responsible entities to develop and implement a GMD Operating procedure or plan to: 1) receive space weather information; 2) develop actions to mitigate possible GMD effects
  NERC Reliability Standard TPL-007-1 was filed with FERC for approval on January 21, 2015.
    Complete a GMD Vulnerability Assessment(s) every five years;
    Develop criteria for acceptable System steady state voltage
    Conduct a thermal impact assessment for its solely and jointly owned applicable BES power transformers
    Develop Corrective Action Plans to address deficiencies that may have been identified in the GMD Vulnerability Assessment(s)
  Comments period in response to FERC questions
  Waiting on FERC action

## Slide 8: Summary of NERC HILF Activities
ERCOT Region Response
  Nodal Operating Guide 4.7
    Requires ERCOT ISO to:
    maintain procedures to receive GMD alerts and warnings issued by NOAA;
    implement and maintain procedures to provide GMD alerts and warnings to TOs
    Requires applicable TO’s to:
    develop a GMD operating procedure or process to mitigate the effects of GMD events
    provide the GMD operating procedure to ERCOT ISO;
    develop a procedure for reporting unusual operating data that could be the result of GMD.

## Slide 9: Summary of NERC HILF Activities
  NERC Reliability Standards & ERCOT Nodal Operating Guides requirements are mandatory & enforceable with fines & penalties for violations.

## Slide 10: Summary of NERC HILF Activities
Possible Impact to Texas
  Metatech Simulation
    Simulation based on a GMD event almost 10x the 1989 event.
    Results indicate possibility of 350 large EHV transformers could be irreparably damaged
    Several areas in northern portion of North America subject to collapse
    Texas not identified as subject to possible collapse. 0% transformers in Texas at risk

## Slide 11: Summary of NERC HILF Activities

## Slide 12: Summary of NERC HILF Activities

## Slide 13: Summary of NERC HILF Activities
High Altitude Electromagnetic Pulse (HEMP)
  A high-altitude electromagnetic pulse (HEMP) is defined as a series of electromagnetic waveforms that are generated from a nuclear detonation at altitudes above 30 km.
  Military thought places the continent at greater risk for such an attack today than in the past.
  HEMP is three main waveforms covering times from nanoseconds to hundreds of seconds.

## Slide 14: Summary of NERC HILF Activities
GMD vs. EMP
NERC’s comments to the FERC GMD NOPR
  Some confusion between GMD & EMP
  EMP E3 wave is similar to a GMD effect - GIC
    Larger magnitude
    Shorter duration – hundreds seconds vs. hours or days
    Occurs after the grid is exposed to the more intense E1 & E2 waves.
  Significant differences between GMD & EMP
    Nature of the threat
    Science behind their impacts
    Scale & form of potential solutions

## Slide 15: Summary of NERC HILF Activities
  NERC comments continued
  Threats posed by GMD & EMP are distinct.
  Effects of GMD are primarily limited to reliability of the Bulk-Power System
  Effects of an EMP are significantly more extensive, going across multiple industries and technologies
  EMP is likely to be the result of an intentional, determined attack

## Slide 16: Summary of NERC HILF Activities
Recent Extreme Events
  October 2012 – Super Storm Sandy
    Largest Atlantic hurricane on record – 1100 miles in diameter
    US death total – 157
    US damage estimated at over $70 billion
    Approximately 8.5 million people lost power
  April 2013 – Metcalf Substation Physical Attack
    A team of gunmen opened fire using rifles on the Metcalf Transmission Substation, severely damaging 17 single phase transformers
    Prior to the attack, a series of fiber-optic telecommunications cables operated by AT&T were cut
    Approximately $15 million in damages
    Sophisticated, coordinated attack
    Resulted in NERC Reliability Standard CIP-014-2
    To date no arrest have been made

## Slide 17: Summary of NERC HILF Activities
  December 2015 – Ukraine Cyber Attack
    Third party remote access/control of electrical facilities
    Approximately 225,000 customers lost power for several hours
    Grid operators forced to manual control to restore outages
    Coordinated with telephone DOS attack on call center
    Serial to ethernet devices impacted at firmware level
    First publicly known cyber attack that resulted in outages
    Spear phishing campaign used to gather credentials to gain remote access
    Ukraine systems much more vulnerable than North American systems