## Slide 1
Settlement Update
Blake Holt
ERCOT
5/16/2016

## Slide 2
Agenda
NPRR617- Energy Offer Flexibility
NPRR700- Actual Fuel Costs in SUCAP
Revisions to DAMW
Revisions to RUCMW

## Slide 3: NPRR700- Using Actual Fuel Costs in SUCAP
Real-Time revenues earned while ramping from breaker close to LSL are not included in RUCMWAMT. Verifiable Startup Costs are reduced by an amount that approximates the Real-Time revenues to ensure a balanced equation.
The reduction in Startup Costs affects both Day-Ahead Market (DAM) and RUC procurement given that both use the same cost structure in the calculation of Startup Offer caps
Reducing Startup Costs in the DAM is not desirable since the DAM is a financial market and Qualified Scheduling Entities (QSEs) do not earn additional revenues for Generation Resources ramping to their LSL.
NPRR700 rectifies this problem by incorporating the actual fuel costs into the DAM and RUC procurement process and DAM Make-Whole Payment calculation

## Slide 4: NPRR617- Energy Offer Flexibility
NPRR617 allows Startup and Minimum Energy Offers to be up to 200% of Verifiable Costs (or Generic Cost if Verifiable Costs do not exist).
NPRR617 Settlement ensures that generators do not receive Make-Whole Payments (DAM/RUC) in excess of their generic or verifiable costs.

## Slide 5: NPRR617- Day Ahead Make Whole revisions
Bill Determinant | Short Description | Extract | Extract Table
DAPERFIPME | Percentage of FIP (specified in offer) used for generation up to LSL | DAM CODE | MKTINPUTHEADER MKTINPUTINTERVAL
DAPERFOPME | Percentage of FOP (specified in offer) used for generation up to LSL | DAM CODE | MKTINPUTHEADER MKTINPUTINTERVAL
DAFCRS | Day-Ahead Actual Fuel Consumption Rate | SID | SID_VERIFIABLECOSTS
New input bill determinants

## Slide 6: NPRR617- Day Ahead Make Whole revisions
Bill Determinant | Short Description | Extract | Extract Table
DAMEPR | Day-Ahead Minimum Energy Price | DAM CODE | PREPROCESSHEADER PREPROCESSINTERVAL
DAVERIME | Day-Ahead Verifiable Minimum Energy Cost | DAM CODE | PREPROCESSHEADER PREPROCESSINTERVAL
DAMECAP | Day-Ahead Verifiable Minimum Energy Cap | DAM CODE | PREPROCESSHEADER PREPROCESSINTERVAL
New intermediate outputs

## Slide 7: NPRR617- Day Ahead Make Whole revisions
Utilizes actual fuel consumption rate
(NPRR700)
DAVERISU_<Q>_<R>_<SP>_<ST> = [DAFCRS * ((GASPERSU * FIP) + (OILPERSU * FOP) + (SFPERSU * SFP))] + VOMS
  If Verifiable Costs present for the Resource (DAVERISU has been produced):
  DASUCAP_<Q>_<R>_<SP>_<ST> = DAVERISU_<Q>_<R>_<SP>_<ST>
  If Verifiable Costs missing for the Resource (DAVERISU missing):
  DASUCAP_<Q>_<R>_<SP>_<ST> = Resource Category Startup Offer Generic Cap
DASUPR_<Q>_<R>_<SP>_<ST> =
Min(DASUO_<Q>_<R>_<SP>_<ST> , DASUCAP_<Q>_<R>_<SP>_<ST>)
Ensures Startup Cap at VC or GC
(NPRR617)
* Above DASUCAP calculations for Non-AGRs. AGRs currently, and will continue to, be capped (DASUCAP) at their Verifiable Startup Costs scaled by the ratio of online generators for the aggregate.
Startup $ allowed in guarantee
(NPRR617)

## Slide 8: NPRR617- Day Ahead Make Whole revisions
DAVERIME_<Q>_<R>_<SP> = [VFCLSL * ((GASPERME * FIP) + (OILPERME * FOP) + (SFPERME * SFP))] + VOMLSL
  If Verifiable Costs present for the Resource (DAVERIME has been produced):
  DAMECAP_<Q>_<R>_<SP>= DAVERIME_<Q>_<R>_<SP>
  If Verifiable Costs missing for the Resource (DAVERIME missing):
  DAMECAP_<Q>_<R>_<SP>= Resource Category Minimum-Energy Generic Cap
Ensures Min Energy Cap at VC or GC
(NPRR617)
DAMEPR_<Q>_<R>_<SP> =
Min(DAMEO_<Q>_<R>_<SP> ,DAMECAP_<Q>_<R>_<SP>)
Min Energy $ allowed in guarantee
(NPRR617)
Verifiable Min Energy Costs
(NPRR617)

## Slide 9: NPRR617- Day Ahead Make Whole revisions
DAMGCOST_<Q>_<R>_<SP> =
(DAMSUFLAG_<Q>_<R>_<SP> * DASUODASUPR_<Q>_<R>_<SP>_<ST>) +
(DAMTFLAG_<Q>_<R>_<SP> *( DASUODASUPRaftercc_<Q>_<R>_<SP>_<ST> - DASUODASUPRbeforecc_<Q>_<R>_<SP>_<ST>)
(DAMWENEFLAG_<Q>_<R>_<SP> * (DAMEODAMEPR_<Q>_<R>_<SP>
* DALSL_<Q>_<R>_<SP>)) +
(DAMWENEFLAG_<Q>_<R>_<SP> * (DAAIEC_<Q>_<R>_<SP> * (DAESR_<Q>_<R>_<SP> - DALSL_<Q>_<R>_<SP>)))
Min Energy $ allowed in guarantee
(NPRR617)
Startup/CCTransition $ allowed in guarantee
(NPRR617)

## Slide 10: NPRR617- RUC Make Whole revisions
Bill Determinant | Short Description | Extract | Extract Table
RTPERFIPME | RTM Percentage of FIP (specified in offer) used for generation up to LSL | RTM CODE | MKTINPUTHEADER MKTINPUTINTERVAL
RTPERFOPME | RTM Percentage of FOP (specified in offer) used for generation up to LSL | RTM CODE | MKTINPUTHEADER MKTINPUTINTERVAL
New input bill determinants

## Slide 11: NPRR617- RUC Make Whole revisions
  SUPR when SUO exists for the hour:
  If Verifiable Costs present for the Resource (VERISU has been produced):
  SUPR_<Q>_<R>_<SP>_<ST> = Min(SUO_<Q>_<R>_<SP>_<ST> , VERISU_<Q>_<R>_<SP>_<ST>)
  If Verifiable Costs missing for the Resource (VERISU missing):
  SUPR _<Q>_<R>_<SP>_<ST> =Min(SUO_<Q>_<R>_<SP>_<ST>,
  Resource Category Startup Offer Generic Cap)
  SUPR when SUO is missing for the hour:
  If Verifiable Costs present for the Resource (VERISU has been produced):
  SUPR_<Q>_<R>_<SP>_<ST> = VERISU_<Q>_<R>_<SP>_<ST>
  If Verifiable Costs missing for the Resource (VERISU missing):
  SUPR _<Q>_<R>_<SP>_<ST> = Resource Category Startup Offer Generic Cap
Ensures Startup Cap at VC or GC
(NPRR617)
** Above SUPR calculations for Non-AGRs. AGRs currently, and will continue to, have SUPR capped at their Verifiable Startup Costs scaled by the ratio of online generators for the aggregate.
* SUPR is currently being utilized in intermediate RUC formulas that consider guaranteed costs. No downstream formulas require a change.

## Slide 12: NPRR617- RUC Make Whole revisions
  MEPR when MEO exists for the hour:
  If Verifiable Costs present for the Resource (VERIME has been produced):
  MEPR_<Q>_<R>_<SP> = Min(MEO_<Q>_<R>_<SP> , VERIME_<Q>_<R>_<SP>)
  If Verifiable Costs missing for the Resource (VERIME missing):
  MEPR _<Q>_<R>_<SP> =Min(MEO_<Q>_<R>_<SP>,
  Resource Category Min-Energy Generic Cap)
  MEPR when MEO is missing for the hour:
  If Verifiable Costs present for the Resource (VERIME has been produced):
  MEPR_<Q>_<R>_<SP> = VERIME_<Q>_<R>_<SP>
  If Verifiable Costs missing for the Resource (VERIME missing):
  MEPR _<Q>_<R>_<SP> = Resource Category Min-Energy Generic Cap
Ensures Min Energy Cap at VC or GC
(NPRR617)
* MEPR is currently being utilized in intermediate RUC formulas that consider guaranteed costs. No downstream formulas require a change.

## Slide 13
NPRR | Description | Release | Timeframe | Discussion
NPRR662 | Proxy Energy Offer Curves | R4 | AUG-2016 | JUL-2016
NPRR272 | Definition and Participation of QSGRs | R6 | DEC-2016 | NOV-2016
What’s on the horizon?