## Slide 1
SAWG
Update on
Multi-Interval Real Time Market
(MIRTM)
May 16, 2016

## Slide 2: How the MIRTM process works
MIRTM with six 5-minute intervals (total of 30 minutes)
8:40 8:45 8:50 8:55 9:00 9:05 9:10 9:15 9:20 9:25 9:30 9:35
Intervals where ONLY Commitment Instructions are binding and the LMPs and MW awards (energy, AS) are indicative
Interval where the LMPs, MW awards (energy, AS) and Commitment Instructions are ALL binding commitment instructions
Sequence of Multi-Interval RT Markets
Analysis window of rolling 30 minutes
RT Market Execution: Depicts the start and end times of the clearing process and the length of symbol is indicative of maximum time allowed to clear market
Pricing run
Pricing run
1st Interval Binding Base Point &
Binding commitments for ALL intervals
1st Interval Binding LMPs

## Slide 3: Modeling Review
Blocky Load Resources
Single part Energy Bid-to-Buy $/MWh (Not to exceed price, MW)
Same Energy Bid for all intervals in study period
Ramp Period (start time): Advance notice required
Minimum Run Time:
  If struck, the minimum time that the Blocky Load Resource is curtailed
Maximum Run Time:
  If struck, the maximum time that the Blocky Load Resource can be curtailed
Return to Service Time:
  After recall, the time period when Blocky Load Resource is not available to MIRTM
  During duration of return to service, the Load MW consumption is immediately restored back to original non-curtailed MW value and is fixed at this MW .
MIRTM will not consider a Blocky Load Resource if its Ramp Period + Minimum Run Time is more than the study period (30 minutes)
Maximum Run Time and Return to Service Time are partially managed outside the MIRTM engine because they can exceed the 30 minute window.

## Slide 4: Modeling Review
Fast Generation Resource
Three Part Offer (Temperature dependent StartUp Cost $, Minimum Energy Cost @LSL $/MW/h, EOC $/MWh)
Temperature dependent Start Time (Hot, Intermediate, Cold)
Minimum On Time
Minimum Off Time
Start Up and Shutdown constraints to cycle Fast Generator Resources
MIRTM will not consider a Quick Start Resource if its applicable temperature dependent StartTime + Minimum On Time is more than the study period (30 minutes)
When a Generation Resource is committed for a future interval, the MW output remains zero till its first committed interval. At the end of the first committed interval, the MW output of the Generation Resource is the desired Base Point.

## Slide 5: Simulation Design Tool Status
The commitment and dispatch (Base Point) component has been completed and has passed testing.
The supporting infrastructure is mostly complete:
  Involves development and testing of scripts to modify the extracted production data, apply data changes for the new short term load forecast, new Blocky Load resources, and create set of Fast Generation Resources with simulated offers and statuses
  Allows for relatively quick turnaround in analyzing “interesting” events from production
The pricing component development starting. The pricing run is like the current pricing run implementation (NPRR 626). This pricing run is required to allow MWs from curtailed Blocky Load Resource and the MWs of the 0-LSL of committed Fast Generation Resources by the MIRTM simulation tool to be part of price formation.

## Slide 6: Review of potential make-whole payments
Make-Whole due to prices (LMP) not being sufficient to cover costs
Potential make-whole payment to a Blocky Load Resource or Fast Generation Resource that is committed by the MIRTM process in future intervals, but the realized binding LMPs (when the future intervals become the 1st interval for subsequent MIRTMs) are insufficient for the Blocky Load Resources or Fast Generation Resource to fully recover their costs.
  Pricing run will mitigate but not eliminate this form of make whole payment, where:
    the curtailed MW from Blocky Load Resources is considered to be variable,
    LSL of Fast Generation Resources is set to zero and the 0-LSL MW is priced equal to the 1st point on the EOC,
    allows the curtailed Blocky Load Resource bids and 0-LSL of committed Fast Generation Resources to participate in price formation.
  For Fast Generation Resources, when 3-part Offers are used. The potential for make-whole payments, even after the pricing run, can arise from two sources:
    For the binding interval (1st five minutes of each MIRTM clearing process (includes pricing run), the committed Fast Generation Resource is marginal on its EOC (i.e. Base Point is above LDL but below HDL), and thus, the Resource cannot recover its startup and minimum energy costs.
    For the binding interval (even if Load Forecast is accurate) the binding LMPs do not provide sufficient revenue to meet the costs represented in the 3-PO. This also includes the scenario where the binding Base Point is at the Low Dispatch Limit (LDL).

## Slide 7: Mitigate Potential Make-Whole Payments to Fast Generation Resources via Single Part Offers
QSEs representing Fast Generation Resources can submit a single part offer (EOC) that incorporates startup costs and minimum energy costs.
  Internally to the software, the first price point on the submitted EOC will be used as the proxy for the Minimum Energy Cost ($/MW/h) at LSL.
  The assumption here is that the potential reduction on commitment efficiency using single part offers instead of three part offers is outweighed by the mitigation of Make-Whole payments
This preserves the single part offer structure by which QSGRs are offering into the current market (SCED), but will allow the system to take into account physical LSL and temporal constraints.

## Slide 8
Mitigation continues to be based on the current practice - IHR with verifiable startup and minimum energy costs baked in. If self-committed, the mitigation will be similar to other non-MIRTM committed Generation Resources.
Make whole, if required, is only to the price on the single part EOC. With this, make whole payment can be mitigated or eliminated via the pricing run
  If the Fast Generation Resource is marginal, then the binding LMP from the pricing run will capture the startup and minimum energy costs if they are incorporated into the EOC.
  If the Fast Generation Resource Base Point is at LSL/LDL then the binding LMP from the pricing run could be sufficient to cover startup and minimum energy costs if they have been incorporated into EOC provided that the dispatch in the pricing run is above 0 MW
Mitigate Potential Make-Whole Payments to Fast Generation Resources via Single Part Offers

## Slide 9: Review of potential make-whole payments – Cont’d
Make-Whole due to binding Resource Ramp Rate constraint
Potential make-whole payment to a Generation Resource for the 1st interval (binding Base Point and LMP), when its Base Point, LMP are not consistent with the Resource EOC and/or dispatch limits. This can happen for any Generation Resource being dispatched by MIRTM in cases where MIRTM is preparing for forecasted ramps in GTBD beyond the first interval being optimized.
  MIRTM analyzes 6 five minute intervals simultaneously for commitment and dispatch
  The 6 five minute intervals are coupled/connected via individual resource ramp constraints - the Base points to a Generation Resource between the 1st and 2nd 5 minute interval cannot exceed its 5 minute ramp capability

## Slide 10: Eliminate Potential Make-Whole Payments Due to Generation Resource Ramp Constraints
Introduce a SCED type step between the commitment and pricing run.
Commitment run. Commitment run - only use the binding commitment instructions
NEW: Binding Dispatch/Base Point run. Run SCED (single interval dispatch using HDL/LDL) for the upcoming 1st five minute interval, but use the binding commitment status of Blocky Load Resources and Fast Generation Resources for the 1st five minutes that is output from MIRTM and calculate HDL/LDL for these . The Base Point from this SCED run are the binding Base Points of ALL Resources for the 1st five minute interval. The LMPs from this SCED are the initial LMPs
Pricing run. Do a pricing run for the first interval (like 626 but with the ramp time set to 5 minutes instead of 60 minutes). In this pricing run, the blocky load resources that are curtailed are treated as variable bids (i.e. not blocky) and the QSGR LSL is relaxed to zero and the first point on EOC is extended horizontally to 0 MW. The output of the pricing run is the positive change to system lambda. Add the positive change to system lambda to all LMPs from the Binding Dispatch/Base Point run. These will be the binding LMPs for the first interval.

## Slide 11: How it would work with Dispatch Run
MIRTM with six 5-minute intervals (total of 30 minutes)
8:40 8:45 8:50 8:55 9:00 9:05 9:10 9:15 9:20 9:25 9:30 9:35
Intervals where ONLY Commitment Instructions are binding and the LMPs and MW awards (energy, AS) are indicative
Interval where the LMPs, MW awards (energy, AS) and Commitment Instructions are ALL binding commitment instructions
Sequence of Multi-Interval RT Markets
Analysis window of rolling 30 minutes
RT Market Execution: Depicts the start and end times of the clearing process and the length of symbol is indicative of maximum time allowed to clear market
Dispatch Run & Pricing run
Dispatch Run & Pricing Run
1st Interval Binding Base Point &
Binding commitments for ALL intervals
1st Interval Binding LMPs
Note: The introduction of the Binding Dispatch/Base Point run while eliminating make-Whole payments to Generation Resources due to binding ramp constraints, can however, lead to missed commitments or too early decommitments/recalls. The assumption is that the benefits of eliminating this category of make-whole payments outweighs the disadvantages of missed commitments or too early decommitments/recalls.

## Slide 12: Evaluating MIRTM process: Comparison of Sequential SCED to MIRTM runs
Find target days that are of interest for various reasons. Certain events that could be of interest would be price spikes, load ramp, wind ramp, etc.
Determine the study period based on the event of interest and run a sequential SCED for the entire study period using the Energy Offers from actual Real Time SCED runs. This is considered the “baseline” that simulates all resources following base points while the GTBD mimics the production case.
For the same study period as the sequential SCED run, run MIRTM tool with Blocky Load Resources and Fast Generation Resources as committable for the following four variations:
  Combined commitment and dispatch followed by a pricing run with:
    Three Part Offers for Fast Generation Resources
    Single Part Offers derived from Three Part Offers for Fast Generation Resources
  Separate commitment and dispatch followed by a pricing run with:
    Three Part Offers for Fast Generation Resources
    Single Part Offers derived from Three Part Offers for Fast Generation Resources
Compare the production costs of the sequential run to various MIRTM study runs

## Slide 13: Calculation of Production Costs
Sequential SCED run:
Total Production Cost is calculated as the sum of:
The area under the EOC from LSL to Base Point of each Online Generation Resource for each SCED run in the study period.
If a Generation Resource EOC is mitigated for a SCED run, then for that SCED run, the production cost calculation utilizes the MOC instead of the submitted EOC.
MIRTM run:
Over the study period, the Total Production Cost is calculated as the sum of :
All the Binding Startup Costs for Fast Generation Resources.
Minimum Energy Cost of Fast Generation Resources for the intervals which MIRTM issued binding commitments.
Dispatch costs of Generation Resources in the 1st interval of each MIRTM run during the study period. This component is calculated the same way as the Production Cost of each SCED run in the Sequential SCED run (including use of MOC).
The avoided cost for curtailed Blocky Load Resources (Bid-to-buy), are calculated as the product of the submitted bid to buy ($/MWh) and the curtailed MW.

## Slide 14: Calculation of Make Whole Payments
The Make Whole payment calculation for Fast Generation Resources is as follows:
For each Fast Generation Resource, calculate the Revenue as the sum of Total Base Point x LMP for the binding interval minus the cost which is calculated as the total Minimum Generation Cost x LSL MW, plus Start Up costs, plus Energy cost from LSL to Base Point.
If Revenue is greater than cost, then no Make Whole required; if less than Revenue, then Make Whole payment is required. If Resource is already online at the beginning of the study period, and MIRTM process extends the online period, no Start Up cost is considered.
The Make Whole payment calculation for Blocky Load Resources is as follows:
For the intervals that a Blocky Load Resource is issued binding commitment to curtail by the MIRTM process, calculate the Actual Avoided Cost as the sum of the Bid MW x Binding LMP from the 1st interval of each MIRTM run.
Calculate the Required Avoided Cost for the curtailed blocky Load Resources as the Bid MW x Bid-to-Buy Price for the MIRTM committed intervals.
If the Actual Avoided Cost is greater than the Required Avoided Cost, then no Make Whole payment is required. Otherwise, the Make-Whole payment is equal to the Required Avoided Cost minus the Actual Avoided Cost.

## Slide 15: Evaluation of impact from binding Generation Resource ramp constraints
Once we add the dispatch run we will evaluate the impacts of binding Generation Resource ramp constraints as follows:
Combined Commitment and dispatch run followed by pricing run: For all Resources, calculate the Revenue as the sum of Base Point x Final LMP (after pricing run).
Separate Commitment and dispatch run followed by pricing run: For all Resources, calculate the Revenue as the sum of Base Point x Final LMP (after pricing run).
Difference in the above two amounts ($) will be the impact of binding Generation Resource ramp constraints

## Slide 16: Next Steps
The MIRTM process evaluation will be an iterative process that involves ERCOT staff presenting results of studies and gathering feedback from stakeholders on adjustments to software functionality and data and ERCOT staff redoing studies with adjustments where feasible
ERCOT
Implement Dispatch module
Implement Pricing module
Study and report back to SAWG on results (after Dispatch and Pricing module implemented)
Stakeholders
Feedback/guidance on 3 Part Offer for Fast Generation Resources
Feedback/guidance on Bid-to-Buy for Load Resources
Feedback/guidance on temporal constraints to be used for Fast Generation Resources
Historical days/time periods to analyze
Feedback/guidance on any changes to how ERCOT presents the results

## Slide 17: Bids for Blocky Load Resources (DSWG survey subset – created in each Load Zone)
Load Resource | $/MWh | MW | Ramp Period | Minimum Run Time | Maximum Run Time | Return To Service Time
1 | 200 | 40 | 10 min. | 15 min | 48 hr | 24 hr
2 | 250 | 50 | 10 min | 15 min | 4 hr | 0 hr
3 | 250 | 100 | 10 min | 15 min | 0.5 hr | 0.5 hr
4 | 300 | 1 | 10 min | 15 min | 1 hr | 1.5 hr
5 | 498 | 30 | 15 min | 15 min | 1.25 hr | 2 hr
6 | 500 | 5 | 15 min | 15 min | 2 hr | 0.0166 hr
7 | 665 | 30 | 15 min | 15 min | 3 hr | 20 hr
8 | 800 | 30 | 15 min | 15 min | 2 hr | 0.0666 hr
9 | 1431 | 25 | 15 min | 15 min | 1.25 hr | 1 hr
10 | 2008 | 20 | 15 min | 15 min | 6 hr | 20 hr
11 | 2008 | 20 | 15 min | 15 min | 3 hr | 20 hr
12 | 3365 | 15 | 15 min | 15 min | 6 hr | 20 hr

## Slide 18: Offers for Fast Generation Resources
Gas Turbines (FIP = 1.79 $/MMBTU)
Reciprocating Engines
Cold StartUp Cost | Intermediate StartUp Cost | Hot StartUp Cost | Minimum Energy Cost @LSL | EOC
$9000 | $6000 | $4000 | 64.79 $/MWh | 15*FIP $/MWh
Cold StartUp Cost | Intermediate StartUp Cost | Hot StartUp Cost | Minimum Energy Cost @LSL | EOC
$2500 | $2500 | $2500 | 16*FIP $/MWh | 15*FIP $/MWh

## Slide 19: Temporal constraints for Fast Generation Resources
Gas Turbines
Reciprocating Engines
Minimum On Time | Minimum Off Time | Hot to Intermediate Time | Intermediate to Cold Time | Cold StartUp Time | Intermediate StartUp Time | Hot StartUp Time
15 min. | 10 min. | 6 min. | 12 min. | 10 min. | 6 min. | 6 min.
Minimum On Time | Minimum Off Time | Hot to Intermediate Time | Intermediate to Cold Time | Cold StartUp Time | Intermediate StartUp Time | Hot StartUp Time
5 min. | 5 min. | 0 min. | 0 min. | 0 min. | 0 min. | 0 min.

## Slide 20
Questions?