## Slide 1
Multi-Interval Real-Time Market (MIRTM)
Demand and Wind Estimation Updates
SAWG
Sean Chang
Market Analysis
May 16, 2016

## Slide 2
Table of Contents
Introduction
Improving Demand Estimation
Improving Wind HSL Estimation
Examining Net Load Estimation Error Distribution
Observations & Next Steps
Appendix

## Slide 3: Introduction
Improving Demand Estimation
Short-Term Load Forecast (STLF)
Generation-To-Be-Dispatched (GTBD) Calculation Methodology
2. Improving Wind HSL Estimation
Indicative Pricing Tool currently uses a heuristically determined linear equation to estimate wind HSL
Currently, plan is for MIRTM to use Persistence to estimate wind HSL
Improvements using ARIMA at the system-wide level were devised to show potential improvement in short-term wind HSL estimation
If time permits, ERCOT will devise plant or region specific ARIMA coefficients for wind HSL estimation

## Slide 4: Introduction
3. Examining Net Load Error Distribution
Combines the impact of demand and wind estimation
  Note that this is not a direct input into MIRTM
Examine error distribution to see performance at outer percentiles
Net Load for this presentation is defined as:
  Estimated Demand – Estimated Wind HSL
  and
  Actual Demand – Actual Wind HSL

## Slide 5
Improving Demand Estimation

## Slide 6: Introduction
Both STLFs use weather and calendar variables as basic inputs.
Current STLF (Legacy system in the EMMS)
  Based on regression similar day model using lagged load values as well as lagged load from 24 hours ago of a similar day
New STLF (Blended Model)
  First 15 minutes is based on a regression model using lagged load values (forecast of total MW for a weather zone)
  Next 45+ minutes is based on a regression model of ramp rates (forecast of total MW change from last actual value)
See May 2015 SAWG meeting page for previous presentation: http://www.ercot.com/calendar/2015/5/27/55033-SAWG

## Slide 7: Introduction
A new methodology for calculating GTBD of MIRTM intervals has been found to be an improvement over current methodology
Applying Look-Ahead SCED methodology:
Modified methodology for MIRTM:
TelemMW0 = Sum of Telemetered Gen output at MIRTM Run time
i = 5-Minute MIRTM Intervals Within Study Window
(ex: i=6 represents 30 Min. Ahead)

## Slide 8: Introduction
Both the current STLF and new STLF are used in the analysis along with the modified methodology for four combinations:
  MIRTM GTBD with current STLF
  MIRTM GTBD with new STLF
  MIRTM GTBD Modified with current STLF
  MIRTM GTBD Modified with new STLF
The calculated MIRTM GTBD errors are benchmarked using Estimated – Reference where Reference is:
  First interval (i=1): Actual SCED GTBD
  Intervals 2 – 6 (i=2…6): Sum of generator output at end of SCED interval

## Slide 9: Statistics of MIRTM GTBD Modified with New STLF vs. Reference

## Slide 10: Statistics of MIRTM GTBD Modified with New STLF vs. Reference

## Slide 11
Improving Wind HSL Estimation

## Slide 12: Improving Wind HSL Estimation in MIRTM
Applying Look-Ahead SCED Implementation
t = Current Time
TelemHSL = Current telemetered HSL
STWPF = AWS Short-Term Wind Power Forecast
i = 5-Minute MIRTM Intervals Within Study Window
(ex: i=6 represents 30 Min. Ahead)
Current Look-Ahead SCED coefficients:
Coefficients using Persistence:
New coefficients calculated using ARIMA (4,0,0) autoregressive model on 2014 wind:
Notes: Performance is calculated using system-wide wind. Actual implementation would require each unit to be treated separate. Further work is being done.

## Slide 13: Statistics of Estimated Wind HSL vs. Actual Wind HSL

## Slide 14: Statistics of Estimated Wind HSL vs. Actual Wind HSL

## Slide 15
Examining Net Load Error Distribution

## Slide 16: Examining Net Load Error Distribution
Both the STLF and Wind HSL Estimation are combined into a singular value to examine its distribution. The following three combinations are chosen:
  MIRTM GTBD Modified with Current STLF minus Persisted Wind HSL
  MIRTM GTBD Modified with New STLF minus Persisted Wind HSL
  MIRTM GTBD Modified with New STLF minus ARIMA Wind HSL
The calculated net load errors are benchmarked using:
(Actual Demand – Actual Wind HSL) – (Estimated Demand – Estimated Wind HSL).

## Slide 17
Net Load Estimation Error Analysis
July 1, 2015 – April 30, 2016
All Intervals

## Slide 18: MAE of Load, Wind, and Net Load Forecasts

## Slide 19
Overestimate
Underestimate

## Slide 20
Underestimate

## Slide 21
Overestimate

## Slide 22
Underestimate
Overestimate

## Slide 23
Underestimate

## Slide 24
Overestimate

## Slide 25
Underestimate
Overestimate

## Slide 26
Underestimate

## Slide 27
Overestimate

## Slide 28
Underestimate
Overestimate

## Slide 29
Underestimate

## Slide 30
Overestimate

## Slide 31
Underestimate
Overestimate

## Slide 32
Underestimate

## Slide 33
Overestimate

## Slide 34
Underestimate
Overestimate

## Slide 35
Underestimate

## Slide 36
Overestimate

## Slide 37: Observations
New STLF continues to outperform current STLF on average
Estimating wind HSL using ARIMA at the system-wide level continues to outperform persistence on average
Examining net load error distribution demonstrates that the combination of new STLF and estimating wind HSL using ARIMA at the system-wide level outperforms other methods even at the outliers

## Slide 38: Conclusions and Next Steps
New STLF will be used in MIRTM studies
For now, persistence will be used to estimate wind HSL for MIRTM studies
ERCOT will conduct further studies on developing ARIMA models to estimate Wind HSL on a seasonal/time of day and regional/wind plant granularity
ERCOT is also engaged with AWS to see if they can create a 5 min. resolution Wind HSL forecast
Appendix contains detailed graphs in the same order and format of the February 22, 2016 SAWG meeting presentation

## Slide 39
Questions?

## Slide 40
Appendix

## Slide 41
MIRTM Demand Estimation Performance
January 1, 2016 – April 30, 2016
All Intervals

## Slide 42: MAE of Estimated GTBD vs. Reference

## Slide 43: MAE of Estimated GTBD vs. Reference

## Slide 44: Standard Deviation of Estimated GTBD vs. Reference

## Slide 45: Standard Deviation of Estimated GTBD vs. Reference

## Slide 46: Mean of Estimated GTBD vs. Reference

## Slide 47: Mean of Estimated GTBD vs. Reference

## Slide 48: MIRTM GTBD Error by Reference (30 min. ahead)

## Slide 49: MIRTM GTBD Error by Reference (25 min. ahead)

## Slide 50: MIRTM GTBD Error by Reference (20 min. ahead)

## Slide 51: MIRTM GTBD Error by Reference (15 min. ahead)

## Slide 52: MIRTM GTBD Error by Reference (10 min. ahead)

## Slide 53: MIRTM GTBD Error by Reference (5 min. ahead)

## Slide 54: MIRTM GTBD Error by Delivery Time (30 min. ahead)

## Slide 55: MIRTM GTBD Error by Delivery Time (25 min. ahead)

## Slide 56: MIRTM GTBD Error by Delivery Time (20 min. ahead)

## Slide 57: MIRTM GTBD Error by Delivery Time (15 min. ahead)

## Slide 58: MIRTM GTBD Error by Delivery Time (10 min. ahead)

## Slide 59: MIRTM GTBD Error by Delivery Time (5 min. ahead)

## Slide 60
MIRTM Demand Estimation Performance
January 1, 2016 – April 30, 2016
239 Intervals when System Lambda >= $75/MWh

## Slide 61: MAE of Estimated GTBD vs. Reference

## Slide 62: MAE of Estimated GTBD vs. Reference

## Slide 63: Standard Deviation of Estimated GTBD vs. Reference

## Slide 64: Standard Deviation of Estimated GTBD vs. Reference

## Slide 65: Mean of Estimated GTBD vs. Reference

## Slide 66: Mean of Estimated GTBD vs. Reference

## Slide 67: MIRTM GTBD Error by Reference (30 min. ahead)

## Slide 68: MIRTM GTBD Error by Reference (25 min. ahead)

## Slide 69: MIRTM GTBD Error by Reference (20 min. ahead)

## Slide 70: MIRTM GTBD Error by Reference (15 min. ahead)

## Slide 71: MIRTM GTBD Error by Reference (10 min. ahead)

## Slide 72: MIRTM GTBD Error by Reference (5 min. ahead)

## Slide 73: MIRTM GTBD Error by Delivery Time (30 min. ahead)

## Slide 74: MIRTM GTBD Error by Delivery Time (25 min. ahead)

## Slide 75: MIRTM GTBD Error by Delivery Time (20 min. ahead)

## Slide 76: MIRTM GTBD Error by Delivery Time (15 min. ahead)

## Slide 77: MIRTM GTBD Error by Delivery Time (10 min. ahead)

## Slide 78: MIRTM GTBD Error by Delivery Time (5 min. ahead)

## Slide 79: MIRTM Demand Estimation Performance on Speciic Days
In the following slides, the estimation performance of the following specific days are analyzed:
  January 16, 2016
  February 23, 2016
  March 31, 2016
For each of these three dates, two high priced SCED intervals are further examined.
The LDL-HDL energy offer curve is shown along with the effects that the New STLF and Modified GTBD Methodology have on the resulting price based the curve.
This is not the actual LDL-HDL curve MIRTM would use for each interval (i). It is the LDL-HDL curve at the SCED snapshot (i =1) simply to give a representation of how sensitive the energy offer curve is to differing GTBD values.

## Slide 80
MIRTM Demand Estimation Performance
January 16, 2016

## Slide 81: MIRTM GTBD Error on January 16, 2016 (30 min. ahead)

## Slide 82: MIRTM GTBD Error on January 16, 2016 (25 min. ahead)

## Slide 83: MIRTM GTBD Error on January 16, 2016 (20 min. ahead)

## Slide 84: MIRTM GTBD Error on January 16, 2016 (15 min. ahead)

## Slide 85: MIRTM GTBD Error on January 16, 2016 (10 min. ahead)

## Slide 86: MIRTM GTBD Error on January 16, 2016 (5 min. ahead)

## Slide 87: LDL to HDL Energy Offer Curve from January 16, 2016 17:50 SCED Run
At SCED Snapshot:
1.2 * 446 = 535.2 MW Load Ramp Component
0.35 * -114 = -39.9 MW Regulation Down Component
Recall that SCED GTBD = (at snapshot)
= Sum of Generator Output
+ K3 * Predicted Load Ramp
+ K4 * Regulation Deployed
At 17:55:
166 MW Regulation Down Deployed

## Slide 88: LDL to HDL Energy Offer Curve from January 16, 2016 19:15 SCED Run
At 19:20:
112 MW Regulation Down Deployed
At SCED Snapshot:
1.2 * 56 = 67.2 MW Load Ramp Component
0.35 * 173 = 60.6 MW Regulation Up Component

## Slide 89
MIRTM Demand Estimation Performance
February 23, 2016

## Slide 90: MIRTM GTBD Error on February 23, 2016 (30 min. ahead)

## Slide 91: MIRTM GTBD Error on February 23, 2016 (25 min. ahead)

## Slide 92: MIRTM GTBD Error on February 23, 2016 (20 min. ahead)

## Slide 93: MIRTM GTBD Error on February 23, 2016 (15 min. ahead)

## Slide 94: MIRTM GTBD Error on February 23, 2016 (10 min. ahead)

## Slide 95: MIRTM GTBD Error on February 23, 2016 (5 min. ahead)

## Slide 96: LDL to HDL Energy Offer Curve from February 23, 2016 18:35 SCED Run
At 18:40:
112 MW Regulation Down Deployed
At SCED Snapshot:
1.2 * 212 = 254.4 MW Load Ramp Component
0.4 * 136 = 54.4 MW Regulation Up Component

## Slide 97: LDL to HDL Energy Offer Curve from February 23, 2016 18:55 SCED Run
At 19:00:
176 MW Regulation Up Deployed
At SCED Snapshot:
1.2 * 36 = 43.2 MW Load Ramp Component
0.4 * 339 = 135.6 MW Regulation Up Component

## Slide 98
MIRTM Demand Estimation Performance
March 31, 2016

## Slide 99: MIRTM GTBD Error on March 31, 2016 (30 min. ahead)
Due to site failover, new STLF dropped out for two hours.

## Slide 100: MIRTM GTBD Error on March 31, 2016 (25 min. ahead)
Due to site failover, new STLF dropped out for two hours.

## Slide 101: MIRTM GTBD Error on March 31, 2016 (20 min. ahead)
Due to site failover, new STLF dropped out for two hours.

## Slide 102: MIRTM GTBD Error on March 31, 2016 (15 min. ahead)
Due to site failover, new STLF dropped out for two hours.

## Slide 103: MIRTM GTBD Error on March 31, 2016 (10 min. ahead)
Due to site failover, new STLF dropped out for two hours.

## Slide 104: MIRTM GTBD Error on March 31, 2016 (5 min. ahead)

## Slide 105: LDL to HDL Energy Offer Curve from March 31, 2016 14:20 SCED Run
At 14:25:
154 MW Regulation Down Deployed
At SCED Snapshot:
1.2 * 29 = 34.8 MW Load Ramp Component
0.4 * 226 = 90.4 MW Regulation Up Component

## Slide 106: LDL to HDL Energy Offer Curve from March 31, 2016 16:20 SCED Run
At 16:25:
159 MW Regulation Up Deployed
At SCED Snapshot:
1.2 * 47 = 56.4 MW Load Ramp Component
0.4 * 130 = 52 MW Regulation Up Component

## Slide 107
Wind HSL Estimation Performance
January 1, 2016 – April 30, 2016
All Intervals

## Slide 108: MAE of Estimated Wind HSL vs. Actual Wind HSL

## Slide 109: MAE of Estimated Wind HSL vs. Actual Wind HSL

## Slide 110: Standard Deviation of Estimated Wind HSL vs. Actual Wind HSL

## Slide 111: Standard Deviation of Estimated Wind HSL vs. Actual Wind HSL

## Slide 112: Mean of Estimated Wind HSL vs. Actual Wind HSL

## Slide 113: Mean of Estimated Wind HSL vs. Actual Wind HSL

## Slide 114: MIRTM Wind HSL Error by Actual Wind HSL (30 min. ahead)

## Slide 115: MIRTM Wind HSL Error by Actual Wind HSL (25 min. ahead)

## Slide 116: MIRTM Wind HSL Error by Actual Wind HSL (20 min. ahead)

## Slide 117: MIRTM Wind HSL Error by Actual Wind HSL (15 min. ahead)

## Slide 118: MIRTM Wind HSL Error by Actual Wind HSL (10 min. ahead)

## Slide 119: MIRTM Wind HSL Error by Actual Wind HSL (5 min. ahead)

## Slide 120: MIRTM Wind HSL Error by Delivery Time (30 min. ahead)

## Slide 121: MIRTM Wind HSL Error by Delivery Time (25 min. ahead)

## Slide 122: MIRTM Wind HSL Error by Delivery Time (20 min. ahead)

## Slide 123: MIRTM Wind HSL Error by Delivery Time (15 min. ahead)

## Slide 124: MIRTM Wind HSL Error by Delivery Time (10 min. ahead)

## Slide 125: MIRTM Wind HSL Error by Delivery Time (5 min. ahead)

## Slide 126
Wind HSL Estimation Performance
January 1, 2016 – April 30, 2016
239 Intervals when System Lambda >= $75/MWh

## Slide 127: MAE of Estimated Wind HSL vs. Actual Wind HSL

## Slide 128: MAE of Estimated Wind HSL vs. Actual Wind HSL

## Slide 129: Standard Deviation of Estimated Wind HSL vs. Actual Wind HSL

## Slide 130: Standard Deviation of Estimated Wind HSL vs. Actual Wind HSL

## Slide 131: Mean of Estimated Wind HSL vs. Actual Wind HSL

## Slide 132: Mean of Estimated Wind HSL vs. Actual Wind HSL

## Slide 133: MIRTM Wind HSL Error by Actual Wind HSL (30 min. ahead)

## Slide 134: MIRTM Wind HSL Error by Actual Wind HSL (25 min. ahead)

## Slide 135: MIRTM Wind HSL Error by Actual Wind HSL (20 min. ahead)

## Slide 136: MIRTM Wind HSL Error by Actual Wind HSL (15 min. ahead)

## Slide 137: MIRTM Wind HSL Error by Actual Wind HSL (10 min. ahead)

## Slide 138: MIRTM Wind HSL Error by Actual Wind HSL (5 min. ahead)

## Slide 139: MIRTM Wind HSL Error by Delivery Time (30 min. ahead)

## Slide 140: MIRTM Wind HSL Error by Delivery Time (25 min. ahead)

## Slide 141: MIRTM Wind HSL Error by Delivery Time (20 min. ahead)

## Slide 142: MIRTM Wind HSL Error by Delivery Time (15 min. ahead)

## Slide 143: MIRTM Wind HSL Error by Delivery Time (10 min. ahead)

## Slide 144: MIRTM Wind HSL Error by Delivery Time (5 min. ahead)

## Slide 145
Wind HSL Estimation Performance
January 16, 2016

## Slide 146: Wind HSL on January 16, 2016

## Slide 147: MIRTM Wind HSL Error on January 16, 2016 (30 min. ahead)

## Slide 148: MIRTM Wind HSL Error on January 16, 2016 (25 min. ahead)

## Slide 149: MIRTM Wind HSL Error on January 16, 2016 (20 min. ahead)

## Slide 150: MIRTM Wind HSL Error on January 16, 2016 (15 min. ahead)

## Slide 151: MIRTM Wind HSL Error on January 16, 2016 (10 min. ahead)

## Slide 152: MIRTM Wind HSL Error on January 16, 2016 (5 min. ahead)

## Slide 153
Wind HSL Estimation Performance
February 23, 2016

## Slide 154: Wind HSL on February 23, 2016

## Slide 155: MIRTM Wind HSL Error on February 23, 2016 (30 min. ahead)

## Slide 156: MIRTM Wind HSL Error on February 23, 2016 (25 min. ahead)

## Slide 157: MIRTM Wind HSL Error on February 23, 2016 (20 min. ahead)

## Slide 158: MIRTM Wind HSL Error on February 23, 2016 (15 min. ahead)

## Slide 159: MIRTM Wind HSL Error on February 23, 2016 (10 min. ahead)

## Slide 160: MIRTM Wind HSL Error on February 23, 2016 (5 min. ahead)

## Slide 161
Wind HSL Estimation Performance
March 31, 2016

## Slide 162: Wind HSL on March 31, 2016

## Slide 163: MIRTM Wind HSL Error on March 31, 2016 (30 min. ahead)

## Slide 164: MIRTM Wind HSL Error on March 31, 2016 (25 min. ahead)

## Slide 165: MIRTM Wind HSL Error on March 31, 2016 (20 min. ahead)

## Slide 166: MIRTM Wind HSL Error on March 31, 2016 (15 min. ahead)

## Slide 167: MIRTM Wind HSL Error on March 31, 2016 (10 min. ahead)

## Slide 168: MIRTM Wind HSL Error on March 31, 2016 (5 min. ahead)