## Slide 1
Appeal of PRS Rejection of NPRR 667
Dan Woodfin
Director, System Operations
TAC
May 26, 2016

## Slide 2: Resource mix has changed
Resource mix in ERCOT Market has changed significantly since current AS framework was developed
This has changed both the need for AS and the capability of resources to provide the AS
Gas-Steam
50%
Coal
25%
Gas-CT/CC
5%
Nuclear
8%
Cogen
11%
Other
0.9%
Renewables
0.008%
Gas-CT/CC
36.5%
Gas-Steam
14.8%
Coal
22.4%
Renewables
13.8%
Other
1.4%
Nuclear
5.7%
Cogen
5.3%
Late 1990s
2015

## Slide 3: Continued change in resource mix expected
Significant additional changes to the resource mix are likely over the next 3 years
  With a 3-year implementation plan for NPRR 667, the drivers for restructuring the AS framework need to be addressed now

## Slide 4: Current AS framework needs improvement
During high wind/low load periods, the current bundled AS framework will:
  Keep higher cost generation online to provide AS
  Extend and deepen negative price periods
  Curtail lower cost resources
  Result in increased AS prices and produce overall higher costs
The frequency of high wind/low load periods is increasing

## Slide 5: Existing “Bundled” Ancillary Services
AS Requirements designed around inherent capabilities of steam boiler units
These requirements serve as barriers to entry for new resources that otherwise could meet underlying technical needs of the system
Regulation Up
Fast-Responding Regulation Up
Current
Up to 30 minutes to deploy
Must be dispatched by SCED
59.7 Hz,
Must be able to sustain deployment
Non-Spin
Responsive
Regulation Down
Fast-Responding Regulation Down

## Slide 6: Proposed Future Ancillary Services
Regulation Up
Fast-Responding Regulation Up
Current
Proposed
Fast Frequency Response 1
Primary Frequency Response
Contingency Reserves 1
Synchronous Inertial Response
Supplemental Reserves 1
Mostly unchanged
59.8 Hz, Limited duration
59.7 Hz, Longer duration
Fast Frequency Response 2
Contingency Reserves 2
SCED-dispatched
Manually dispatched
Supplemental Reserves 2
SCED-dispatched
Manually dispatched
Ongoing development
Non-Spin
Responsive
Regulation Down
Fast-Responding Regulation Down
Regulation Up
Regulation Down
Fast-Responding Regulation Up
Fast-Responding Regulation Down

## Slide 7: Nearly 3 Years of Stakeholder Input
3 Years
ERCOT Posts Future
Ancillary Services
White Paper
9/2013
~25 Stakeholder work sessions
to gather input and improve proposal
ERCOT Files NPRR 667,
with significant modifications to original
proposal based on stakeholder input
11/2014
Additional stakeholder workshops
and Cost/Benefit Study; revisions to
NPRR based on Stakeholder input
Spring
2016
PRS/TAC/Board Approval
Implementation
Spring
2019

## Slide 8: Stakeholder input shaped the current proposal
ERCOT’s original proposal modified significantly through stakeholder input
  Fundamental Services were changed
  Details of NPRR modified
Current
Revised 667
Regulation Up
Fast-Responding Regulation Up
Fast Frequency Response 1
Primary Frequency Response
Contingency Reserves 1
Supplemental Reserves 1
Fast Frequency Response 2
Contingency Reserves 2
Supplemental Reserves 2
Non-Spin
Responsive
Regulation Down
Fast-Responding Regulation Down
Regulation Up
Regulation Down
Fast-Responding Regulation Up
Fast-Responding Regulation Down
Fast Frequency Response
Primary Frequency Response
Contingency Reserves
Regulation Up
Fast-Responding Regulation Up
Regulation Down
Fast-Responding Regulation Down
Original ERCOT Proposal

## Slide 9: Substitutability => liquidity
Regulation Up
Fast-Responding Regulation Up
Current
Proposed
Fast Frequency Response 1
Primary Frequency Response
Contingency Reserves 1
Supplemental Reserves 1
Mostly unchanged
59.8 Hz, Limited duration
59.7 Hz, Longer duration
Fast Frequency Response 2
Contingency Reserves 2
SCED-dispatched
Manually dispatched
Supplemental Reserves 2
SCED-dispatched
Manually dispatched
Non-Spin
Responsive
Regulation Down
Fast-Responding Regulation Down
Regulation Up
Regulation Down
Fast-Responding Regulation Up
Fast-Responding Regulation Down

## Slide 10: NPRR 667 supports TAC Goals for 2016
5. Develop and implement needed market design corrections and improvements which are cost effective.
  Brattle study found the NPRR had benefits much greater than costs (even after adjustment to lower gas prices) and was good market design.
6. Pursue the appropriate implementation of load participation
  NPRR provides several opportunities for increased load participation.
7. Pursue the appropriate implementation of emerging technologies.
  NPRR667 allows increased flexibility and efficiency in integrating new resources and facilitates their participation in the AS markets.
11. Collaborate with ERCOT Staff on the review of Ancillary Service needs and implement changes as necessary.
  ERCOT and stakeholders have worked together to refine NPRR667.
12. Maintain market rules that support open access to the ERCOT markets and transmission network.
  NPRR667 removes significant barriers to entry for diverse types of resources needed to reliably support the continually changing resource mix.

## Slide 11: Appeal
ERCOT requests that TAC recommend approval of NPRR667, in order to:
  Provide a holistic and efficient set of AS to meet the changing reliability challenges of the ERCOT System;
  Remove barriers to entry for new Resources that can meet the technical needs of the system; and
  Allow a coordinated transition to address future AS needs rather than addressing these needs through a piecemeal approach.