## Slide 1: EFL Renewable Content Calculator
RMS – June 7, 2016

## Slide 2: Background
Several productive discussions with ERCOT already to reach agreement on certain minor changes to EFL calculator for next year to enhance usability
  Adding benchmark value, de-emphasizing emissions data that is no longer required, incorporating out-of-state renewable contracts
Need stakeholder guidance on other contemplated changes regarding EFL calculator mechanics

## Slide 3: Motivation
Eliminate Confusion About EFL Renewable Content Calculation
Promote Consistency Across the Market
Chart: Renewable Content Disclosures on Power To Choose (5/27/16)
| 0% | 3% | 5% | 6% | 9% | 10% | 11% | 12% | 50% | 100%
Total | 12 | 6 | 23 | 65 | 10 | 15 | 97 | 4 | 2 | 80

## Slide 4: Key Concept: Default Scorecard
What is the “default scorecard”? See 25.476(e)(4)
Statewide (including non-ERCOT) fuel mix, less REC retirements (in ERCOT)
It is not the Renewable Portfolio Standard (RPS) required % (2015’s RPS was ~5.6%)
In 2015:
Statewide 2015 MWh | 380,604,455.23 |  |  |  |  | 
2015 REC Retirements (Any Vintage) | 30,241,759 |  |  |  |  | 
 | Coal/Lignite | Nat Gas | Nuclear | Renew | Other | Total
Statewide Avg % | 28.3% | 49.1% | 10.3% | 12.1% | 0.2% | 100.0%
MWh | 107,744,753.80 | 186,866,367.60 | 39,384,317.35 | 45,918,997.73 | 690,018.76 | 380,604,455.23
MWh (less RECs) | 107,744,753.80 | 186,866,367.60 | 39,384,317.35 | 15,677,238.73 | 690,018.76 | 350,362,696.23
Default Scorecard % | 30.8% | 53.3% | 11.2% | 4.5% | 0.2% | 100.0%
Notes: 2015 Statewide REC Requirement: 14,919,894
2015 Total Sales Subject to RPS: 264,868,692
Source: www.texasrenewables.com (ERCOT)

## Slide 5: Key Concept: Benchmark %
Established by 16 TAC 25.476(f)(5)(B)(ii)
Effectively requires all EFLs to have at least the Renewable Portfolio Standard (RPS) required %
Defined as SRR ÷ TS
  SRR = Statewide REC Requirement
  TS = Total Sales
Not the default scorecard required by 25.476(e)
In 2015: 14,919,894 ÷ 264,868,692 = 5.6%
5.6%
5.9%
5.0%
5.0%
Benchmark
Notes: Source: www.texasrenewables.com (ERCOT)

## Slide 6: Key Concept: Calculator Mechanics
Uses weighted averages – renewable content is determined by weighted average of RECs (100% renewable), purchased power contracts (generator-specific %), and default scorecard % (changes yearly)
Originally designed to support emissions reporting on EFLs (no longer required by PUC Rules)
Ex:
(10% x 100%) + (90% x 4.5%) = 10% + 4.05% = 14.1%
6

## Slide 7: Default Scorecard EFL Calculator Dynamics
Weighted averaging with the default % yields counterintuitive results
  a standard product (only retiring 5.6% RPS mandate) will show 9.9%
    (56/1000) x 100% + (944/1000) x 4.5% = 9.9%
  retiring no RECs yields 4.5% (default %)
    (0/1000) x 100% + (1000/1000) x 4.5% = 4.5%
  a 50% product need only retire 47.6% RECs
    (476/1000) x 100% + (524/1000) x 4.5% = 49.96%
  but a 100% product must retire 100% RECs
    (1000/1000) x 100% + (0/1000) x 4.5% = 100%
Chart: RECs vs. EFL - 1,000 MWh Example (2015)
Retiring 56 RECs (RPS Mandate)
results in an EFL disclosure
% of 9.9%
RPS % = 5.6%
Default % = 4.5%
EFL % and RECs as % of MWh converge towards 100%
EFL Calculator reports 50% before RECs/Sales = 50%

## Slide 8: Hypothesis: REPs Interpret EFL Calculator Differently
Using as intended (or using statewide average?)
Using old versions of the EFL Calculator
Not entering RECs retired (assuming Default=RPS)
Not using the EFL calculator at all
Who knows what else
2011 Default = 3%
2014 RPS+Default = 11%
2014 Statewide Avg=11%
2014 Default = 5%
Impossible Calculator Output
Actual 2014 RPS %
2012 RPS+Default = 9%
Maybe 2014 RPS+2013 Default?
2010 RPS+Default = 10%

## Slide 9: One Rule, Two (Separate) Compliance Obligations
ERCOT Compliance – 25.476(e)
The registration agent (ERCOT) shall maintain a database of TX generator scorecards reflecting fuel mix and environmental data
By April 1 each year, ERCOT shall calculate and publish a statewide average fuel mix, statewide average emission rates, and a default scorecard to account for generation not authenticated by retiring RECs
REP Compliance – 25.476(f)-(h)
REPs must update EFLs for prior year’s renewable content by July 1 and report to ERCOT
For EFL disclosures, renewable content may be determined using RECs, REC offsets, qualified out-of-state supply contracts, and the Texas State Average Fuel Mix [but not the default scorecard mix]
Each EFL must meet a minimum benchmark renewable % (statewide RPS)
PUC Rules do not require publication or use of a calculator, but do require ERCOT to publish certain information and dictate how REPs may validate renewable marketing claims

## Slide 10: Impression Of Required Use
ERCOT notice implies REPs must use EFL Renewable Content Calculator

## Slide 11: Question: Should The Default Scorecard Count In The EFL Calculator?
Not explicitly allowed for use by REPs in PUC Rules
Contributes to confusion over proper EFL calculator usage
Reflects non-ERCOT renewable content in competitive area (ERCOT-only) disclosures
Eliminating default % allows for more straightforward EFL content calculation
ERCOT can still publish (as required by 25.476(e)), but does not have to be in the EFL calculator

## Slide 12: Next Steps?
Present alternative calculator structure proposal at future meeting (posted to this meeting’s materials, however, use password ‘calculator’ to unlock spreadsheet)
Voting item?
Questions?