## Slide 1
Key Points of Voltage Profile
ERCOT Operations Planning
6/10/16

## Slide 2
Agenda
Voltage Profile Process
Voltage Profile Implementation
Review of Spreadsheet

## Slide 3: Voltage Profile Process
Summer/Fall Voltage Profile Study
  March – May
  Posted by June 1st
Winter/Spring Voltage Profile Study
  September – November
  Posted by December 1st
Generator feedback requested prior to the start of the study

## Slide 4: Voltage Profile Process
Pass 0
ERCOT sends out On-Peak and Off-Peak (ex. Summer Peak and Fall Off-Peak) cases and planning contingency files to TSP’s
Passes 1 - 4
ERCOT runs contingency analysis and sends contingency violations to TSP’s
Final
ERCOT posts Voltage Profile Spreadsheet on MIS
TSP’s submit changes to the cases and contingency files to ERCOT
Includes updated voltage set points
TSP’s submit feedback on contingency violations to ERCOT
ERCOT will ask generators for feedback from previous year’s profile

## Slide 5: Voltage Profile Implementation
Generation Resources required to provide VSS must hold their voltage set point at the Transmission POI when on-line
Generation Resources will coordinate with their respective TSP to implement the new set point
VPWG meetings are held once a month with an open morning session
PUBLIC_VPWG@lists.ercot.com

## Slide 6: Transmission POI
Point of Interconnection (POI)
The voltage level and substation where a Generation Entity’s interconnection Facilities connect to the Transmission Facilities as reflected in the Standard Generation Interconnection Agreement (SGIA) between a Generation Entity and a Transmission Service Provider (TSP) or the voltage level and substation where Load interconnects to the TSP Facilities.
Transmission Sw. Sta.
The POI can be several miles away from the Power Plant

## Slide 7: Voltage Profile Spreadsheet
Generator Details |  |  |  |  | Summer Peak Voltage Profile Data |  |  |  |  |  | Voltage Profile for High Side of GSU* |  | 
 |  |  |  |  | Voltage Pofile applicable at POI |  |  |  |  |  |  |  | 
Unit Code | Bus Number | Id | TDSP_ERCOT Planning_Bus_Name | Transmission Operator | In Service | Remote Bus | Nominal Voltage | EMS_Station Code | EMS_Station Long_Name | Voltage Profile | Remote Bus | Nominal Voltage | Voltage Profile
Unit1 | 111111 | C0 | Unit1 | STEC(913) | YES | 5501 | 138 | GEN | GENERATOR | 141.5 | 5506 | 138 | 142.5
Unit2 | 222222 | N1 | Unit2 | CNP(904) | NO | 5502 | 69 | GEN2 | GENERATOR 2 | 70.0 | 5503 | 69 | 71.0
Unit3 | 333333 | C1 | Unit3 | CNP(904) | YES | 2203 | 138 | GEN3 | GENERATOR 3 | 142.0 | 2203 | 138 | 142.0
Unit4 | 444444 | C2 | Unit4 | CNP(904) | YES | 2203 | 138 | GEN3 | GENERATOR 3 | 142.0 | 2203 | 138 | 142.0
*The High Side of the GSU Voltage Profile is a reference value. VSS is required at the transmission POI.

## Slide 8: Questions?