## Slide 1: NPRR784 Mitigated Offer Caps for RMR Units
Protocol Revision Subcommittee
June 16, 2016

## Slide 2: Motivation for NPRR784
Limit the ability for out-of-market units to interfere with market outcomes.
  Current rules will cause SCED to dispatch RMR Units before other units in the market during congestion.
  NPRR784 will allow SCED to dispatch RMR Units after other capacity available for transmission congestion relief has been utilized.
Lower RMR uplift costs to loads.
  Placing RMR Units farther back in the SCED dispatch order will reduce dispatch frequency lowering RMR energy costs and maintenance costs.
Improve the integrity of price formation when RMR Units are required to resolve congestion.
  PUCT, IMM, ERCOT Board, and Stakeholders have recognized the crucial need to “get prices right” in the energy-only market.

## Slide 3: Design of NPRR784
The language in NPRR784 was constructed to provide a flexible process that ERCOT can implement manually at little to no cost.
  During congestion, SCED’s dispatchable offer price range for each unit is based on the unit’s shift factor and the shadow price cap.
  Shift factors used in SCED will fluctuate frequently.
  NPRR784 allows ERCOT to choose a conservative (i.e. low) shift factor and, with consideration of the prevailing shadow price cap, set a conservative Mitigated Offer Cap (MOC) for the RMR Unit.
    Well below the SWCAP of $9,000/MWh.
  Establishing a MOC for RMR Units using this process will position them farther back in the SCED dispatch order and limit displacement of market resources while minimizing further RMR cost.
Under NPRR784, the MOC for GBY5 is expected to be set to a value between $500/MWh and $700/MWh most of the time.
  If adjustment is required, it will be lower. NPRR784 provides ERCOT the flexibility to raise it back to the higher level if appropriate.
Fully transparent to market participants.
  ERCOT will issue a market notice to communicate the initial value of the RMR MOC and any subsequent changes.

## Slide 4: Other Considerations
Why is NPRR784 appropriate?
  Offer mitigation is applied to units associated with a QSE that can exert local market power.
    i.e. Fails Constraint Competitiveness Test and QSE is the Decision Making Entity (DME).
  However, ERCOT controls the offering, commitment, and operation of RMR Units, not the QSE.
    ERCOT is really the DME for RMR Units, but not feasible to implement.
    No ability for QSEs to set or modify offer curves for RMR Units.
    Local market power will be mitigated through RUC and CCT.
      Non-RMR Units controlled by QSEs will be committed through RUC and then mitigated.
  NPRR784 sends a more appropriate price signal when RMR Units are needed to manage congestion. A more appropriate price signal incentivizes supply response to help resolve congestion.
    Continual evolution in ERCOT market design to “get the price right”. Essential for this market to succeed.
    Pricing during congestion just as important as system wide scarcity pricing.
      See Irresolvable Constraint pricing mechanism.
Responsive to concerns raised by the Board on June 14th.
  Need for better “localized price signals”.