## Slide 1: A Midsummer Night’s DREAM
Vision for NPRR 777

## Slide 2: Goal:
SENA developed NPRR 777 with the intent to implement the findings of the DREAM task force, with a focus on integrating price responsive resources connected to the distribution system. SENA also elected to:
Create a new resource type
Enable a load-zone dispatch
Leverage existing settlements, RUC practices, price discovery, and performance metrics associated with traditional resources
Such that distribution-connected resources that behave like traditional resources may opt-in to participate in a SCED dispatch

## Slide 3: Goal:
Efficient price formation, where deployment of price-responsive distribution connected resources is reflected as a resource serving load, rather than a reduction in demand.
Increased market efficiency and reliability, through transparency and ISO awareness of price-responsive distribution connected resources.
Incremental resources available to ERCOT for
  Assessment of transmission needs / studies
  RMR alternatives

## Slide 4: Exclusions
777 focused on protocol revisions that enable existing distribution connected resources that cannot currently participate in SCED. The current NPRR excludes distributed resource participation in
Nodal Dispatch
Ancillary Service Markets
Day-Ahead Markets
Congestion Revenue Rights Markets*
*Note: This exclusion prohibits development of a resource node / settlement point for a distribution-connected resource. All market participants may participate in CRR markets, subject to meeting requirements defined in ERCOT Protocols

## Slide 5: Exclusions / Rationale: Nodal Dispatch
SENA supports an efficient dispatch of all resources. Resources that can monetize their locational value to alleviate constraints through a SCED dispatch should have the ability to do so.
However, NPRR 777 was authored acknowledging the challenges associated with a nodal dispatch, including:
The potential for registering as an MDR (for nodal payment) when nodal prices favor the resource, and de-registering as an MDR (for zonal payment) when nodal prices do not favor the resource.
Incentives to create a mobile generation fleet.

## Slide 6: Exclusions / Rationale: Ancillary Services
NPRR 777, as written excludes MDRs from providing ancillary services. SENA is supportive of a competitive market structure where any resource can provide Ancillary Services, provided that they have the technical capabilities to provide that service.
Existing market structures permit (and do not change by virtue of 777) opportunities for MDRs to provide certain Ancillary (or comparable services)

## Slide 7: Exclusions / Rationale : Ancillary Services
Non Spin
(10/30 Min Response)
ERS
(10/30 Min Response)
Responsive Reserve
(10 min / Governor Response)
Load Resource participation by high-set UF Relay
Regulation
No comparable product
Protocol revisions need to include storage when deployment is commercial and material
Regulation provided by Natural Gas and Diesel fired Resources would likely be uneconomic compared to other lower-cost alternatives.

## Slide 8: Exclusions / Rationale:
Day-Ahead Market: Market Participants may participate in the DAM, however no new settlement points will be created for each MDR. Load Zone dispatch and Payment allows each MDR to be perfectly hedged to the Load Zone, and can participate in DAM activities.
Congestion Revenue Rights:
  Development of a Settlement Point for each MDR may burden existing infrastructure
  Load-zone dispatch of MDRs allows Market Participants to Hedge from the Load Zone to any existing point on the system, enabling a perfect hedge if desired. Load Zone payment also guarantees each MDR is perfectly hedged to the Load Zone, without procuring any CRR instrument.

## Slide 9: Path Forward
SENA proposes that WMS host monthly discussions to build consensus on the following topics:
Settlement: Does the current MDR treatment as a resource align with current resource settlement practices?
RUC: Does the current MDR treatment make a MDR eligible for RUC? Inclusion in transmission studies?
Telemetry: Is telemetry adequate for ERCOT and achievable by MDRs?
Performance Metrics: Are existing resource performance metrics appropriate and achievable for MDRs?
Other?