## Slide 1
ERCOT: Energy Management System (EMS)
July 07, EMS Outage
TAC
Date: July 28, 2016

## Slide 2: EMS Outage – Thursday July 07, 2016
  Impact: 1hour 42 minutes
  EMS Applications
  LFC (Load Frequency Control)
  SCED Solutions
  Root Cause: Information Technology: Situational Awareness
  Multiple Sessions including EMS & Model Verification Environment (MVE)
  Command intended for MVE was executed in EMS
  Recovery: Great Effort
  Immediate awareness that there was an issue
  Identify problem, recovery & restore data and verify in sequence
Notes:   Description: EMS Outage
  11:41am incorrect command corrupted data in the network model in the EMS system.
  The corrupt data passed to downstream systems such as MMS, Settlements, and Reports
  11:59am-12:16pm QSE was instructed to assume Constant Frequency Control
  1:23pm data was corrected and verified and operations returned to normal

## Slide 3: Settlements Impact
Subsequent to the EMS issue corrected prices were posted for the affected SCED intervals.
Emergency Base Point data was determined to not be reliable and was therefore not used for Initial Settlement.
ERCOT is continuing to evaluate alternatives that may impact subsequent settlements and will provide updates as necessary.

## Slide 4: EMS Outage – Lessons Learned
  Training
  IT Operations
  IT Support
  Hardening
  Processes
    Production and Lower Environments
  Procedures
    Re-Enforcement
  Automation
  Lessons Learned – IT Situational Awareness
  Internal – IT Operations, Grid Operations, IT Support
  External – TRE, NERC, EMS Working Groups
  Market Participants