## Slide 1
Multi-Interval Real-Time Market Update to SAWG
August 15, 2016

## Slide 2: Refresher on the MIRTM Process
MIRTM six 5-minute intervals (30 minutes total) with separate commitment and dispatch
8:40 8:45 8:50 8:55 9:00 9:05 9:10 9:15 9:20 9:25 9:30 9:35
Intervals where ONLY Commitment Instructions are binding and the LMPs and MW awards (energy, AS) are indicative
Interval where the LMPs, MW awards (energy, AS) and Commitment Instructions are ALL binding commitment instructions
Sequence of Multi-Interval RT Markets
Analysis window of rolling 30 minutes
RT Market Execution: Depicts the start and end times of the clearing process and the length of symbol is indicative of maximum time allowed to clear market
Dispatch Run & Pricing run
Dispatch Run & Pricing Run
Binding commitments for ALL intervals
1st Interval Binding Base Point & Binding LMPs
Note: The introduction of the Binding Dispatch/Base Point run while eliminating make-Whole payments to Generation Resources due to binding ramp constraints, can however, lead to missed commitments or too early decommitments/recalls. The assumption is that the benefits of eliminating this category of make-whole payments outweighs the disadvantages of missed commitments or too early decommitments/recalls.

## Slide 3: Overview of Recent Activity
Implement Dispatch module
Implement Pricing module
Developed Three part offers (TPO) based on average Verifiable Costs and unit HSL
Developed Single part offers (SPO) from TPO allocating start costs over min up time
Allowed for Wartsila units to have zero start time and zero min off time (allows fast ramping resources to meet demand in same interval)
Studied the following dates:7/1/2015, 8/11/2015, 8/13/2015, 11/11/2015, 11/27/2015, 3/27/2016, 7/25/2016

## Slide 4: Today’s Agenda
Refresher on study inputs
For study day 8/13/2015 review and compare all of the Separate Commitment and Dispatch MIRTM runs listed on the next slide
For remaining six study days
  7/1/2015 – Luminant request (Volatile wind, little congestion, low system lambda)
  8/11/2015 - Luminant request (Little congestion, low dispatchable capacity)
  11/11/2015 - ERCOT (New STLF over forecasts load)
  11/27/2015 – ERCOT (New STLF under forecast load, large wind down ramp)
  3/27/2016 – ERCOT (Low wind, units shutting down, low dispatchable capacity)
  7/25/2016 – ERCOT (Low wind, low dispatchable capacity)
  Compare two MIRTM runs:
    Fast responding resources and load (3PO)
    Fast responding resources to mimic production i.e. not committable by MIRTM (LOAD)

## Slide 5: Study Runs
For the 8/13 run we will step incrementally through the progression of studies as follows:
Production SCED
Sequential SCED
MIRTM with Separate Commitment and Dispatch:
  Loads only with QSGR not committable to mimic production (LOAD)
  QSGRs have Production offers with single part offers (SPO Prod. SCED EOCs)
  QSGRs have three-part offer based on average Verifiable Costs (3PO)
  QSGRs have single-part offer based on average Verifiable Costs (SPO)
  Note: we could come back at a later date with a comparison between MIRTM Combined Commitment and Dispatch and MIRTM Separate Commitment and Dispatch. It was too much data to show in one session.

## Slide 6: Study Process
Determine the study period based on the day of interest and run a sequential SCED for the entire study period using the Energy Offers from actual Real Time SCED runs.
Sequential SCED considered the “baseline” that simulates all resources following base points while the GTBD mimics the production case.
Run MIRTM Separate Commitment and Dispatch with different offer structures (SPO Prod. SCED EOCs, 3PO, SPO) as inputs while the GTBD mimics the production case.
Use new STLF and Wind Persistence to “look ahead” 30 minutes to determine if commitments needed

## Slide 7: Study Process
Calculate Production Costs: Four Components
  Generation Costs: Integrate Step 2 EOC from LSL to BP + Power Balance Violation
  Transmission Penalty Cost: Violated MW * Shadow Price
  QSGR Startup/Mingen Cost: Startup and Minimum Energy Costs
  Blocky Load Cost: Bid Price * Commit MW
Calculate Make Whole
  QSGR Make whole across entire study period
    Prod. SCED & Seq. SCED: Emergency Operations QSGR payments (Per 6.6.9 (3))
    MIRTM: Max(0,QSGR Verifiable Cost - QSGR Revenue)
  Blocky Load Make whole across entire study period
    MIRTM: Max(0, [Bid Price * Commit MW] -[Binding LMP * Commit MW])
Notes: QSGR revenue:
(Binding LMP + ORDC Online Price Adder + Pricing Run Price Adder) * Binding Base Point of Committable QSGR Unit List
QSGR Verifiable cost:
QSGR Verifiable Cost Above LSL - Integrate Input EOC or Verifiable Cost EOC (if no QSGRs in MIRTM) from LSL to BP of Committable QSGR Unit List
plus
QSGR Startup/Mingen Cost of Committable QSGR Unit List - Startup and Minimum Generation Costs of Committable QSGR Unit List

## Slide 8: Simulation Assumptions – Blocky Load Resources
Offers were received for 12 Blocky Loads from DSWG
A total of 366 MW split between the load zones (each zone has 12 resources)

## Slide 9: Simulation Assumptions – Fast Generation Resource Temporal Constraints
All Resources that are Quick Start qualified are considered “fast responding resources”. If the Resource was “OUT” or “ONTEST” during the study period they are not considered as “committable” Gas Turbines (36 units)
Reciprocating Engines (3 units)
Minimum On Time | Minimum Off Time | Hot to Intermediate Time | Intermediate to Cold Time | Cold StartUp Time | Intermediate StartUp Time | Hot StartUp Time
0 min. | 0 min. | 0 min. | 0 min. | 0 min. | 0 min. | 0 min.
Wartsilas (4 units)

## Slide 10: Simulation Assumptions – Fast Responding Resources
Four average Verifiable Costs groups were identified.
Each Fast Responding Resources is assigned a group cost based on HRL/LSL
The Single Part offer is structured in order to recover Start Up and Minimum Energy cost over the Minimum On time
Minimum EOC is $75 if Resource had Non-Spin responsibility during study period
Res Type | HRL (MW) | LRL (MW) | Seasonal LSL (MW) | Startup Cost ($) | Min-Energy Price ($/MWh) | Min EOC ($/MWh) | Max EOC ($/MWh) | Single Part Cost ($/MWh)
SCLE90 | 54.0 | 10.0 | 13.0 | 4,322.05 | 52.39 | 30.86 | 33.91 | 1,287.26
SCLE90 | 60.0 | 0.0 | 12.0 | 3,448.99 | 48.85 | 28.47 | 31.05 | 1,198.51
SCLE90 | 95.0 | 0.0 | 41.0 | 6,058.75 | 56.12 | 40.35 | 41.88 | 647.21
DSL | 8.9 | 6.0 | 6.0 | 962.21 | 39.93 | 34.84 | 39.79 | 1,964.34

## Slide 11: Other Assumptions – Days Analyzed
  The Capacity from all Fast Responding Resources is considered online in MIRTM study runs; this has the impact of changing the ORDC calculation slightly; however, the resource capacity is only shifted from offline to online.
  The Block Load Resources are considered “new” Resources which increases the RTOLCAP and shifts the curve to the right by 366MW.
  Keep this in mind when comparing the ORDC price adder revenues across the Production SCED, Sequential SCED, and MIRTM study runs.
  The Reliability Deployment Price Adder in MIRTM treats the deployment by ERCOT as a “deployment event” therefore MIRTM may find a RTDP when Production and Sequential SCED did not.

## Slide 12: Study Day: August 13, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
Generation Cost | 4797543.2906 | 4511059.4623 | 4497899.0416 | 4442096.4527 | 4533296.9168 | 5072238.6267
Transmission Penalty Cost | 42320.8333 | 39439.0148 | 39198.0202 | 21928.204 | 7223.5526 | 117641.4014
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 177305.0123 | 362737.7094 | 937656.5265
Blocky Load Cost | 0 | 0 | 3562.5 | 2781.25 | 0 | 141795.8333

## Slide 13: Study Day: August 13, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
Average System Lambda | 93.5205 | 86.0555 | 85.7228 | 81.8263 | 69.0051 | 485.1258
Average RTORPA | 90.4866 | 57.3711 | 26.1343 | 25.6677 | 26.1336 | 21.5396
Average RTRDPA | 0 | 0 | 0.2021 | 0.3277 | 0.7095 | 18.3349
Average RTOFFPA | 71.2621 | 47.9189 | 23.516 | 23.1791 | 23.6214 | 19.5432
Increase in prices due to offer assumptions (see slide 10)

## Slide 14: Study Day: August 13, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_SPO_PROD_EOC | MIRTM_3PO | MIRTM_SPO
QSGR Makewhole | 16.61 | 16.61 | 0 | 0 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 0 | 0 | 0 | 0
Zero Make Whole

## Slide 15: Study Day: August 13, 2015 Cost and Revenue
Notes: Increase in Generator Revenue in 3PO and SPO due to price increase at 14:20 caused by GTBD regulation component and load ramp component

## Slide 16: Study Day: August 13, 2015 HDL-GTBD, SL
$9k

## Slide 17: Study Day: August 13, 2015 Commitment Summary

## Slide 18: Study Day: July 1, 2015
  7/1/2015 – Luminant request (Volatile wind, little congestion, low system lambda)

## Slide 19: Study Day: July 01, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -606109.3782 | -609429.9318 | -610763.2004 | -600711.3099
Transmission Penalty Cost | 0 | 0.0059 | 0 | 0
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 0
Blocky Load Cost | 0 | 0 | 0 | 0
Note: Negative Production costs are because we have significant MW on output schedules. Production costs for those resources are integrated at $-250 from LSL to output schedule.
Notes: Negative Production costs are because we have significant MW on output schedules. Production costs for those resources are integrated at $-250 from LSL to output schedule.

## Slide 20: Study Day: July 01, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 24.8437 | 24.8727 | 24.8724 | 24.9347
Average RTORPA | 0 | 0 | 0 | 0
Average RTRDPA | 0 | 0 | 0 | 0
Average RTOFFPA | 0 | 0 | 0 | 0

## Slide 21: Study Day: July 01, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 0 | 0 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 0 | 0
Zero Make Whole

## Slide 22: Study Day: July 1, 2015 – Cost and Revenue

## Slide 23: Study Day: July 1, 2015 – HDL-GTBD, SL

## Slide 24: Study Day: July 1, 2015 – Commitment Summary
Zero Commitments
QSGR mimic Production self commitments
Notes: MIRTM Load Only commitment of QSGR is mimicking production self commitments.

## Slide 25: Study Day: August 11, 2015
  8/11/2015 - Luminant request (Little congestion, low dispatchable capacity)

## Slide 26: Study Day: August 11, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | 4068477.83 | 4061046.7 | 4070382.34 | 4162934.26
Transmission Penalty Cost | 845.83 | 847.15 | 848.42 | 848.96
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 464463.6
Blocky Load Cost | 0 | 0 | 0 | 0
Increases from Combined Cycle modeling, offer assumptions and dispatch decisions (see note)
Notes: We have identified that MIRTM has increase Production costs due to a Combined Cycle assumption which causes ~$40k difference from Seq SCED. When a Combined Cycle changes configuration, that config has new HDL/LDL. Seq SCED uses the production SCED HDL/LDL. MIRTM sets HDL/LDL based on previous interval BP. Since the CC EOC did not cover to the new HDL, EOC was set to $9k causing the unit to be dispatched at LDL which caused separation of Production Costs between SS and MIRTM. Additionally, the assumed offers and dispatch decisions caused by withholding capacity drive production costs up.

## Slide 27: Study Day: August 11, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 49.73 | 49.62 | 49.64 | 51.66
Average RTORPA | 64.91 | 46.71 | 20.86 | 20.5
Average RTRDPA | 0 | 0 | 0 | 1.27
Average RTOFFPA | 45.74 | 34.48 | 16.97 | 16.68

## Slide 28: Study Day: August 11, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 26.94 | 26.94 | 0 | 0
Blocky Load Makewhole | 0 | 0 | 0 | 0

## Slide 29: Study Day: August 11, 2015 – Cost and Revenue

## Slide 30: Study Day: August 11, 2015 – HDL-GTBD, SL

## Slide 31: Study Day: August 11, 2015 – Commitment Summary

## Slide 32: Study Day: Nov 11, 2015
  11/11/2015 - ERCOT (New STLF over forecasts load)

## Slide 33: Study Day: Nov 11, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -2414334.8031 | -2446877.2077 | -2435333.4584 | -2380936.6978
Transmission Penalty Cost | 9858.3333 | 0.081 | 0 | 43962.9929
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 169257.6689
Blocky Load Cost | 0 | 0 | 0 | 0

## Slide 34: Study Day: Nov 11, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 34.97 | 26.3053 | 23.7557 | 25.4511
Average RTORPA | 0.9121 | 1.0002 | 0.2739 | 0.1994
Average RTRDPA | 0 | 0 | 0 | 2.1662
Average RTOFFPA | 0.4893 | 0.5215 | 0.1741 | 0.1639

## Slide 35: Study Day: Nov 11, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 8093.28 | 8093.28 | 0 | 76488.7517
Blocky Load Makewhole | 0 | 0 | 0 | 0

## Slide 36: Study Day: Nov 11, 2015 – Cost and Revenue

## Slide 37: Study Day: Nov 11, 2015– HDL-GTBD, SL

## Slide 38: Study Day: Nov 11, 2015 – Commitment Summary

## Slide 39: Study Day: Nov 27, 2015
  11/27/2015 – ERCOT (New STLF under forecast load)

## Slide 40: Study Day: Nov 27, 2015
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -1942859.3054 | -1941061.9079 | -1710966.8024 | -1657960.622
Transmission Penalty Cost | 93.3333 | 11.7349 | 13.0132 | 32.4919
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 240040.5745
Blocky Load Cost | 0 | 0 | 18048.75 | 0
Combined Cycle modeling
~$250k
Notes: See 8/11 description of Combined cycle modeling. Same issue here which causes MIRTM to have ~$250k additional Production costs.

## Slide 41: Study Day: Nov 27, 2015
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 35.1227 | 32.6424 | 28.0265 | 49.1269
Average RTORPA | 0.3631 | 0.367 | 0.0528 | 0.0177
Average RTRDPA | 0 | 0 | 0.2363 | 4.9812
Average RTOFFPA | 0.0948 | 0.0955 | 0.0168 | 0.0153

## Slide 42: Study Day: Nov 27, 2015
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 24390.36 | 24390.36 | 21948.8879 | 128020.7372
Blocky Load Makewhole | 0 | 0 | 16728.4546 | 0
Notes: QSGR Make Whole under Load only run is due to low system lambda and change in dispatch due to Load commitment.

## Slide 43: Study Day: Nov 27, 2015 – Cost and Revenue
$4M
$15M

## Slide 44: Study Day: Nov 27, 2015– HDL-GTBD, SL

## Slide 45: Study Day: Nov 27, 2015 – Commitment Summary

## Slide 46: Study Day: March 27, 2016
  3/27/2016 – ERCOT (Low wind, units shutting down, low dispatchable capacity)

## Slide 47: Study Day: March 27, 2016
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | -2536432.0842 | -2588363.4331 | -2637098.3153 | -2637403.3887
Transmission Penalty Cost | 51187.5 | 59946.2646 | 85465.8887 | 178669.8649
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 77823.6698
Blocky Load Cost | 0 | 0 | 30431.0417 | 0

## Slide 48: Study Day: March 27, 2016
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 66.1421 | 61.9415 | 51.7143 | 288.483
Average RTORPA | 1.4842 | 1.5104 | 0.3667 | 0.0154
Average RTRDPA | 0 | 0 | 3.6297 | 0.2786
Average RTOFFPA | 0.0282 | 0.0286 | 0.0079 | 0.0029
One interval @ 20:10 there was a price spike of $9k due to load forecast under forecasting a load in future interval. When that interval became the binding interval, 2 units shutdown resulting in GTBD being higher and no time to commit more resources due to ramp constraints. Blocky load will not get committed unless we see increase in price in intervals 3 and beyond (depends on notification time).

## Slide 49: Study Day: March 27, 2016
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 38860.45 | 38860.45 | 0 | 3007.7383
Blocky Load Makewhole | 0 | 0 | 3057.1212 | 0

## Slide 50: Study Day: March 27, 2016 – Cost and Revenue
$4M
$25M

## Slide 51: Study Day: March 27, 2016 – HDL-GTBD, SL
$1k
$9k

## Slide 52: Study Day: March 27, 2016 – Commitment Summary

## Slide 53: Study Day: July 25, 2016
  7/25/2016 – ERCOT (Low wind, low dispatchable capacity)

## Slide 54: Study Day: July 25, 2016
Chart: Production Costs
| PROD_SCED * | SEQ_SCED * | MIRTM_LOAD_ONLY * | MIRTM_3PO
Generation Cost | 1608446.2282 | 1121847.1099 | 1043599.5486 | 993052.7269
Transmission Penalty Cost | 606.6667 | 294.9481 | 307.0676 | 1376.0883
QSGR Startup/Mingen Cost | 0 | 0 | 0 | 296808.4079
Blocky Load Cost | 0 | 0 | 44627.5 | 0

## Slide 55: Study Day: July 25, 2016
Chart: Average Prices
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
Average System Lambda | 76.0182 | 90.0329 | 81.8297 | 41.2646
Average RTORPA | 5.6845 | 5.9699 | 1.799 | 1.2285
Average RTRDPA | 0.971 | 0.9745 | 7.8375 | 1.1711
Average RTOFFPA | 2.7325 | 2.8511 | 1.0501 | 1.0685

## Slide 56: Study Day: July 25, 2016
Chart: Make Whole Amounts
| PROD_SCED | SEQ_SCED | MIRTM_LOAD_ONLY | MIRTM_3PO
QSGR Makewhole | 5362 | 5362 | 0 | 86342.1451
Blocky Load Makewhole | 0 | 0 | 15626.6151 | 0

## Slide 57: Study Day: July 25, 2016 – Cost and Revenue

## Slide 58: Study Day: July 25, 2016 – HDL-GTBD, SL

## Slide 59: Study Day: July 25, 2016 – Commitment Summary

## Slide 60: Questions and Next Steps
We would like to concentrate on these study days going forward.
Based on today’s discussion we can bring more details on specific events.
Changes in assumptions?

## Slide 61
Appendix A. Additional Scenario Graphs

## Slide 62: Study Day: August 13, 2015 MIRTM Load only

## Slide 63: Study Day: August 13, 2015 MIRTM Load only

## Slide 64: Study Day: August 13, 2015 MIRTM Load only

## Slide 65: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 66: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 67: Study Day: August 13, 2015 MIRTM Prod EOC

## Slide 68: Study Day: August 13, 2015 MIRTM 3PO

## Slide 69: Study Day: August 13, 2015 MIRTM 3PO

## Slide 70: Study Day: August 13, 2015 MIRTM 3PO

## Slide 71: Study Day: August 13, 2015 MIRTM SPO

## Slide 72: Study Day: August 13, 2015 MIRTM SPO

## Slide 73: Study Day: August 13, 2015 MIRTM SPO

## Slide 74: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 75: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 76: Study Day: July 1, 2015 – MIRTM Load Only

## Slide 77: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 78: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 79: Study Day: July 1, 2015 – MIRTM 3PO

## Slide 80: Study Day: August 11, 2015 – MIRTM Load only

## Slide 81: Study Day: August 11, 2015 – MIRTM Load only

## Slide 82: Study Day: August 11, 2015 – MIRTM Load only

## Slide 83: Study Day: August 11, 2015– MIRTM 3PO

## Slide 84: Study Day: August 11, 2015– MIRTM 3PO

## Slide 85: Study Day: August 11, 2015– MIRTM 3PO

## Slide 86: Study Day: Nov 11, 2015 – MIRTM Load only

## Slide 87: Study Day: Nov 11, 2015– MIRTM Load only

## Slide 88: Study Day: Nov 11, 2015 – MIRTM Load only

## Slide 89: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 90: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 91: Study Day: Nov 11, 2015 – MIRTM 3PO

## Slide 92: Study Day: Nov 27, 2015 – MIRTM Load only

## Slide 93: Study Day: Nov 27, 2015– MIRTM Load only

## Slide 94: Study Day: Nov 27, 2015 – MIRTM Load only

## Slide 95: Study Day: Nov 27, 2015 – MIRTM 3PO

## Slide 96: Study Day: Nov 27, 2015 – MIRTM 3PO

## Slide 97: Study Day: Nov 27, 2015 – MIRTM 3PO

## Slide 98: Study Day: March 27, 2016 – MIRTM Load only

## Slide 99: Study Day: March 27, 2016 – MIRTM Load only

## Slide 100: Study Day: March 27, 2016 – MIRTM Load only

## Slide 101: Study Day: March 27, 2016 – MIRTM 3PO

## Slide 102: Study Day: March 27, 2016 – MIRTM 3PO

## Slide 103: Study Day: March 27, 2016 – MIRTM 3PO

## Slide 104: Study Day: July 25, 2016 – MIRTM Load only

## Slide 105: Study Day: July 25, 2016 – MIRTM Load only

## Slide 106: Study Day: July 25, 2016 – MIRTM Load only

## Slide 107: Study Day: July 25, 2016 – MIRTM 3PO

## Slide 108: Study Day: July 25, 2016 – MIRTM 3PO

## Slide 109: Study Day: July 25, 2016 – MIRTM 3PO

## Slide 110
Appendix B. Example MIRTM Study Run

## Slide 111: Example MIRTM Study Run
System with the following conditions:
Initial load is 50,000 MW
Assume demand (GTBD) forecast is correct
Generation Mix:
50,001 MW of dispatchable generation priced at $50/MWh
100 MW Fast Start Resource:
  Single Part Offer with all MWs at $200/MWh
  LSL=0, HSL=100
  Minimum Run Time = 15 minutes
  Notification Time = 5 minutes
    When a Generation Resource is committed for a future interval, the MW output remains zero till its first committed interval. At the end of the first committed interval, the MW output of the Generation Resource is the desired Base Point. Thus, this fast start resource will be fully at its Base Point in 10 minutes with a notification time of 5 minutes.

## Slide 112: Example MIRTM Study Run

## Slide 113: Example MIRTM Study Run

## Slide 114: Example MIRTM Study Run

## Slide 115: Example MIRTM Study Run

## Slide 116: Example MIRTM Study Run

## Slide 117: Example MIRTM Study Run

## Slide 118: Example MIRTM Study Run

## Slide 119: Example MIRTM Study Run

## Slide 120: Example MIRTM Study Run

## Slide 121: Example MIRTM Study Run

## Slide 122: Example MIRTM Study Run

## Slide 123: Example MIRTM Study Run

## Slide 124: Example MIRTM Study Run

## Slide 125: Example MIRTM Study Run