## Slide 1
ERCOT Update to DSWG
DSWG – August 19, 2016

## Slide 2
Agenda Item #5
Inclusion of UFR Deployments in Reliability Adder

## Slide 3: Load Resource RRS UFR Deployments

## Slide 4: Adding LR UFR Deployments to the Reliability Adder
Telemetry is available for all LRs providing RRS
  Resource Status – ONRL
  RRS Responsibility and RRS Schedule
  Net Power Consumption
  Low Power Consumption
  UFR Status – Armed or Online when active
  Circuit Breaker Status – Closed when active
RRS Schedules do not change during a UFR type deployment
No electronic instruction for dispatch or recall for UFR deployments – currently only have a verbal instruction for the recall
Ancillary Service Monitor relies on difference between RRS Responsibility and RRS Schedule to show quantity that has been deployed and as a result it does not show the amount deployed for UFR deployments
To add this capacity to the Reliability Adder, we need to identify a deployment trigger, a recall trigger and a way to measure the amount of capacity that tripped on under-frequency and its recovery following the recall. None of these items are currently in our systems today.

## Slide 5: Proposed Solution
ERCOT recommends the following to include the LR UFR capacity in the Reliability Price Adder
The following would only apply to LRs with ONRL COP status
Deployment Trigger
  New resource specific telemetry requirement signaling relay trip
Capacity (MW)
  ERCOT Calculated Value
  Net Power Consumption (T-1 minute) – Net Power Consumption (NPC)
Recall Trigger
  Modification to the ERCOT Deployment Manger
  Add XML signal from the ERCOT Operator
Recovery Period
  Back out capacity using NPC
Note: Additional emphasis will be added to require QSE’s to reflect schedule changes with UFR deployments and recovery of load following recall.

## Slide 6: ERCOT Observations
Of the 9 UFR deployments over the past 5 years
  7 of the 9 deployments have lasted less than 15 minutes
  Only 1 of 9 deployments were during capacity insufficiency events
    The other 8 deployment events were unlikely to have any discernible impact on prices

## Slide 7
Agenda Item #8
Potential ERS Settlement Changes

## Slide 8
Payment Reduction for 2 test failures sent to QSE for Review
Resolve missing meter data issue
Finalize Availability and Payment Reductions for Test Failures
ERS Settlement 75day (55 + 20)
Last day of the SCT
Meter data due 35 days
Availability 45 days following the end of the SCT
RTM Final Settlement 55 days following the operating day
Activities that begin after day 55
-Settlement team calculates Load Ratio Share for each LSE - need for SPUCL calculation - 2 business days
-ERS team creates settlement workbooks for Resource Level and QSE Level – 4 business days
-Settlement team creates payments and uplift cuts for each QSE and LSE and imports to database – min of 4 days
Note: excluding 6 days for weekends during this period only 14 business days available to complete these activities
ERS Settlement Timeline