## Slide 1
Discussion on Start Time Logic for the Commitment of Resources in the Market Management Systems
David Maggio
Manager, Market Analysis and Validation
October 14, 2016

## Slide 2: Introduction
A concern was recently raised regarding the logic used in the Market Management System (MMS) to determine the first Operating Hour in which a Resource is available for commitment
Currently, the MMS takes into consideration the start time of the Resource, the Current Operating Plan (COP) status of the Resource, and the amount of time between when the commitment is being decided and the Operating Hour
It does not consider COP statuses in between these two times
The purpose of this presentation is describe the specific scenario and get feedback from the group on any future steps

## Slide 3: Example of the Concern
Say we have the following scenario:
  Resource start time is 6 hours
  Resource COP status is OUT hours ending 1 through 12 and OFF hours ending 13 through 24
  Hourly Reliability Unit Commitment (HRUC) is executed just after 8 AM
  HRUC projects an issue for hour ending 17 for which the Resource is needed
~8:00 - HRUC Study
12:00 – Resource Outage Ends
16:00 – 17:00 - HRUC projects an issue & Resource is committed
Resource is available for commitment because the status is OFF for hour ending 17 and start time is considered relative to the HRUC execution time

## Slide 4: Example of the Concern
If the Resource physically takes 6 hours to start and that process cannot begin until after the outage ends, hour ending 19 is the first hour in which the Resource can be online and responding to dispatch
~8:00 - HRUC Study
12:00 – Resource Outage Ends
18:00 – 19:00 - Resource can be online and dispatched
16:00 – 17:00 - HRUC projects an issue & Resource is committed

## Slide 5: Discussion for the Group
Questions for discussion by the group:
  Is this a concern that others share and/or have observed with RUC instructions to their QSE?
  If the group believes this in an issue, should changes to the MMS be considered? Both the Day-Ahead Market (DAM) and RUC?

## Slide 6: Potential System Change
Change the commitment logic to take into consider future COP statuses
  Specifically looking for cases of a future OUT status and setting hours of commitment availability relative to outaged hours and start times
~8:00 - HRUC Study
12:00 – Resource Outage Ends
18:00 – 19:00 - Resource can be online and dispatched
16:00 – 17:00 - HRUC projects an issue but Resource is not available for commitment
Should both the DAM and RUC logic be changed to consider future statuses?

## Slide 7: Discussion