## Slide 1
Analysis of Mitigated Offer Cap Curve Proposals for Reliability Must-Run Resources
David Maggio
Manager, Market Analysis and Validation
October 17, 2016

## Slide 2: Introduction
During the September meeting, ERCOT offered to bring back analysis comparing proposals for setting the Mitigated Offer Cap (MOC) curves for Reliability Must-Run (RMR) Resources
2 approaches were analyzed and compared with the proposal under Nodal Protocol Revision Request (NPRR) 784, Mitigated Offer Caps for RMR Units

## Slide 3: Analysis Assumptions
In order to provide a comparison of the different approaches:
  Used Green Bayou Unit 5 (GBY5) as the sole RMR Resource
  Focused on Real-Time Market (RTM) constraints in which transmission elements SNGZEN98_A or SNGZEN99_A were the constrained element
    These constraints have a max. shadow price of 4,500 $/MWh
  Analyzed each Security-Constrained Economic Dispatch (SCED) interval separately, for intervals in which a constraint with SNGZEN98_A or SNGZEN99_A was binding (active in SCED with a shadow price greater than 0)

## Slide 4: Approach 1 Methodology
For each SCED interval:
For all non-RMR Resources with a shift factor < -.02, calculate a value = (Highest point on the MOC curve for that Resource)/Abs(Shift factor for that Resource for the specified constraint)
Set SPu as the maximum of the values determined in step 1
Set SPmax as the minimum of:
  SPu + 50 $/MWh
  Constraint max. shadow price – 1 $/MWh
Set the RMR Resource MOC as SPmax x Abs(RMR Resource shift factor for the specified constraint)

## Slide 5: Approach 2 Methodology
For each SCED interval:
For all non-RMR Resources with a shift factor < -.02, calculate a value = (Highest point on the Step 2 Energy Offer Curve (EOC) for that Resource)/Abs(Shift factor for that Resource for the specified constraint)
  If the value < Constraint max. shadow price, then set to value
  Else, set to null (Resources that cannot be dispatched by SCED are ignored)
Set SPu as the maximum of the values determined in step 1
Set SPmax as the minimum of:
  SPu + 50 $/MWh
  Constraint max. shadow price – 1 $/MWh
Set the RMR Resource MOC as SPmax x Abs(RMR Resource shift factor for the specified constraint)

## Slide 6: NPRR 784
For comparing these approaches to the proposal under NPRR 784, we again focused on GBY5 and constraints in which SNGZEN98_A or SNGZEN99_A were the constrained element
Determined the least negative shift factor that GBY5 had that helped the constraint (-0.14077)
Set the RMR Resource MOC as the Abs(-0.14077) x Constraint max. shadow price (~633 $/MWh)

## Slide 7: Approach Comparison – Since Go-Live
Chart: Duration Curve of MOC Proposals for the RMR Resource

## Slide 8: Approach Comparison – Since Go-Live
Chart: MOC Proposals for the RMR Resource in Chronological Order

## Slide 9: Approach Comparison – 2016 Only
Chart: Duration Curve of MOC Proposals for the RMR Resource

## Slide 10: Approach Comparison – 2016 Only
Chart: MOC Proposals for the RMR Resource in Chronological Order

## Slide 11: Summary of Analysis Conclusions
Approach 1 generally resulted in MOC values higher than the ~633 $/MWh estimated under the NPRR 784 proposal
Approach 2 generally resulted in MOC values less than the ~633 $/MWh estimated under the NPRR 784 proposal
There are some cases in which approach 1 produces a value less than approach 2
Both approach 1 and 2 were fairly volatile when evaluated for each SCED interval individually
These trends occurred both when looking at all periods since Nodal Go-Live and at only recent history (2016)