## Slide 1
Load Forecast Boundary Threshold Implementation
PLWG
October 19, 2016

## Slide 2
Agenda
Background
Forecast Error Factors
Proposal
Threshold Deviation Considerations

## Slide 3: Background
PGRR042
2017 RTP and Independent Review studies
See Calvin’s September PLWG presentation: http://www.ercot.com/calendar/2016/9/21/81126-PLWG

## Slide 4: Factors leading to forecast error
Forecast Error
Weather Error
Model Error
Economic Error
Boundary Threshold

## Slide 5: Weather
Forecast Error
Weather Error
Model Error
Economic Error
In planning studies weather error is negated by assuming 90/10 weather.
In a sense, the weather variable is fixed.

## Slide 6: Model
Forecast Error
Weather Error
Model Error
Economic Error
Per Calvin’s September PLWG presentation, the 2016 model error ranged between -3.7% to 4.5% by weather zone with the exception of the South Central which had an error of 8.8%.
Of the five other weather zones that were under-forecast, the average was 2.5%.
A factor to consider is that the model is new so there is not a lot of history, but it should improve over time.

## Slide 7: Economic
Forecast Error
Weather Error
Model Error
Economic Error
Economic error is the forecast error caused by imperfect economic growth assumptions.
This can include general economic growth trend misses or unforeseen growth in a particular sector.

## Slide 8: Economic Error
Weather Zone | Under Forecast | Over Forecast
North |  | -13.3%
North Central | 0.4% | 
East |  | -13.8%
Far West | 1.3% | 
West |  | -8.9%
South Central | 1.3% | 
Coast |  | -1.8%
South |  | -5.6%
ERCOT Overall |  | -1.4%
Average | 1.0% | -7.5%
2011 Non-Farm Employment Forecast Error for 2016

## Slide 9: Proposal
ERCOT proposes to use a flat 5% boundary threshold for 2017 RTP and Independent Reviews
  Based on model error of ~2.5-4.5% and economic error of ~1%
ERCOT does not propose to use a different default threshold for different zones or years
  TSPs can justify a higher forecast if needed on a case-by-case basis

## Slide 10: Factors to be considered if a TSP proposes a higher forecast
Historic load growth
Committed load additions
Forecast methodology
Past forecast performance
Special circumstances
Other?

## Slide 11: Questions and Answers

## Slide 12: Appendix – 2016 RTP comparison
“Current” Higher-Of Totals (Losses=NO / LNG=YES / SS=YES) |  |  |  |  |  |  |  |  | 
Year | Coast | East | Far West | North | North Central | South Central | Southern | West | Total
2017 | 26257 | 2924 | 3364 | 1692 | 26921 | 12937 | 6428 | 2312 | 82835
2018 | 27162 | 2943 | 3514 | 1723 | 27243 | 13221 | 6564 | 2356 | 84725
2019 | 27474 | 2981 | 3670 | 1763 | 27500 | 13551 | 6660 | 2396 | 85993
2020 | 27795 | 3008 | 3813 | 1794 | 27723 | 13837 | 6749 | 2436 | 87154
2021 | 27992 | 3041 | 3928 | 1830 | 27943 | 14170 | 6840 | 2487 | 88231
2022 | 28212 | 3069 | 4057 | 1859 | 28165 | 14446 | 6967 | 2540 | 89315
Bounded Higher-Of Totals (Losses=NO / LNG=YES / SS=YES) @ X=5% |  |  |  |  |  |  |  |  | 
Year | Coast | East | Far West | North | North Central | South Central | Southern | West | Total
2017 | 25775 | 2617 | 3117 | 1536 | 26921 | 12937 | 6428 | 2258 | 81589
2018 | 26428 | 2648 | 3208 | 1534 | 27243 | 12999 | 6564 | 2325 | 82948
2019 | 26605 | 2672 | 3300 | 1536 | 27500 | 13044 | 6660 | 2395 | 83712
2020 | 26797 | 2697 | 3393 | 1540 | 27723 | 13079 | 6749 | 2436 | 84413
2021 | 26936 | 2725 | 3492 | 1543 | 27943 | 13118 | 6840 | 2487 | 85083
2022 | 27105 | 2752 | 3590 | 1545 | 28165 | 13159 | 6967 | 2540 | 85822
*Note: Numbers do not take into account latest load forecast nor if a TSP were to present evidence that the boundary threshold is too low for a particular region.