## Slide 1
Multi-Interval Real-Time Market (MIRTM)
Update to SAWG
ERCOT Staff
Market Design & Analysis
October 24, 2016

## Slide 2: Today’s Agenda
Overview of recent activity
Refresher on study inputs and outputs
For all study days, review and compare all of the Separate Commitment and Dispatch MIRTM runs

## Slide 3: MIRTM - Changes since September SAWG
Changes made after discussion with Market Participant’s at last SAWG:
  GTBD in first interval altered in both Sequential SCED and MIRTM
TelemMW0 = Sum of Telemetered Gen output at MIRTM Run time
i = 5-Minute MIRTM Intervals Within Study Window
(ex: i=6 represents 30 Min. Ahead)
  Include Start Up and Minimum Energy calculation in Sequential SCED in order to be consistent with MIRTM
  Update Energy Offer Curve for fast responding resources based on commitment decision in Production (suggested by IMM after the SAWG meeting):
    If the Resource was self committed in production and the EOC is lower in production, then use the lower offer in MIRTM instead of the higher “bucketed average” value
    If the Resource was in QS mode in production, use the “bucketed average” value in MIRTM (assumes that the production EOC would have considered some value for SU/ME)

## Slide 4: MIRTM - Changes since September SAWG
Changes made after discussion with Market Participant’s at last SAWG:
  For Sequential SCED, Add to production cost the estimate of Start Up and Minimum Energy cost in order to be consistent with MIRTM
  Update Energy Offer Curve for fast responding resources based on commitment decision in Production (suggested by IMM after the SAWG meeting):
    If the Resource was self committed in production and the EOC is lower in production, then use the lower offer in MIRTM instead of the higher “bucketed average” value
    If the Resource was in QS mode in production, use the “bucketed average” value in MIRTM (assumes that the production EOC would have considered some value for SU/ME)

## Slide 5: MIRTM - Changes since September SAWG cont.
Changes made after detailed analysis of results
  ERCOT staff corrected the treatment of start-up cost which had been incorrectly scaled relative to Minimum Energy Cost and Energy Offer Cost
  For some LR, input data error in the ramp period (notification time) error was corrected
  ERCOT staff re-ran all of the study data after data changes

## Slide 6: Study Runs
For all the study days we will step incrementally through the progression of studies as follows:
Production SCED (information only)
Sequential SCED
MIRTM with Separate Commitment and Dispatch:
  Loads only with QSGR not committable to mimic production (LOAD)
  QSGRs have three-part offer based on average Verifiable Costs (3PO)

## Slide 7: Study Process
Determine the study period based on the day of interest and run a sequential SCED for the entire study period using the Energy Offers from actual Real Time SCED runs.
Sequential SCED considered the “baseline” that simulates all resources following base points while the GTBD is consistent with MIRTM.
Run MIRTM Separate Commitment and Dispatch with QSGR Production EOC replaced with 3PO as inputs
Use new STLF and Wind Persistence to “look ahead” 30 minutes to determine if commitments needed

## Slide 8: Study Process
Calculate Production Costs: Four Components
  Generation Costs: Integrate Step 2 EOC from LSL to BP + Power Balance Violation
  Transmission Penalty Cost: Violated MW * Shadow Price
  QSGR Startup/Mingen Cost: Startup and Minimum Energy Costs
  Blocky Load Cost: Bid Price * Commit MW
Calculate Make Whole
  QSGR Make whole across entire study period
    Prod. SCED & Seq. SCED: Emergency Operations QSGR payments (Per 6.6.9 (3))
    MIRTM: Max(0,QSGR Verifiable Cost - QSGR Revenue)
  Blocky Load Make whole across entire study period
    MIRTM: Max(0, [Bid Price * Commit MW] -[Binding LMP * Commit MW])
Notes: QSGR revenue:
(Binding LMP + Operating Reserve Demand Curve (ORDC) Online Price Adder + Pricing Run Price Adder) * Binding Base Point of Committable QSGR Unit List
QSGR Verifiable cost:
QSGR Verifiable Cost Above LSL - Integrate Input EOC or Verifiable Cost EOC (if no QSGRs in MIRTM) from LSL to BP of Committable QSGR Unit List
plus
QSGR Startup/Mingen Cost of Committable QSGR Unit List - Startup and Minimum Generation Costs of Committable QSGR Unit List

## Slide 9: Simulation Assumptions – Blocky Load Resources
Offers were received for 12 Blocky Loads from DSWG
A total of 366 MW split between the load zones (each zone has 12 resources)
Load Resource | $/MWh | MW | Ramp Period | Minimum Run Time | Maximum Run Time | Return to Service Time
1 | 200 | 40 | 10 Min. | 15 Min. | 48 hours | 24 hours
2 | 250 | 50 | 10 Min. | 15 Min. | 4 hours | 0 hours
3 | 250 | 100 | 10 Min. | 15 Min. | 0.5 hours | 0.5 hours
4 | 300 | 1 | 10 Min. | 15 Min. | 1 hour | 1.5 hours
5 | 498 | 30 | 15 Min. | 15 Min. | 1.25 hours | 2 hours
6 | 500 | 5 | 15 Min. | 15 Min. | 2 hours | 10 Min.
7 | 665 | 30 | 15 Min. | 15 Min. | 3 hours | 20 hours
8 | 800 | 30 | 15 Min. | 15 Min. | 2 hours | 5 Min.
9 | 1431 | 25 | 15 Min. | 15 Min. | 1.25 hours | 1 hour
10 | 2008 | 20 | 15 Min. | 15 Min. | 6 hours | 20 hours
11 | 2008 | 20 | 15 Min. | 15 Min. | 3 hours | 20 hours
12 | 3365 | 15 | 15 Min. | 15 Min. | 6 hours | 20 hours

## Slide 10: Simulation Assumptions – Fast Generation Resource Temporal Constraints
All Resources that are Quick Start qualified are considered “fast responding resources”. If the Resource was “OUT” or “ONTEST” during the study period they are not considered as “committable”
Gas Turbines (36 units) |  |  |  | 
Minimum On Time | Minimum Off Time | Cold Start-Up Time | Intermedate Start-Up Time | Hot Start-Up Time
15 Min. | 15 Min. | 10-15 Min. | 10-15 Min. | 10-15 Min.
Reciprocating Engines (3 units) |  |  |  | 
Minimum On Time | Minimum Off Time | Cold Start-Up Time | Intermedate Start-Up Time | Hot Start-Up Time
5 Min. | 15 Min. | 10 Min. | 10 Min. | 10 Min.
Wartsilas (4 units) |  |  |  | 
Minimum On Time | Minimum Off Time | Cold Start-Up Time | Intermedate Start-Up Time | Hot Start-Up Time
5 Min. | 5 Min. | 5 Min. | 5 Min. | 5 Min.

## Slide 11: Simulation Assumptions – Fast Responding Resources
Four average Verifiable Costs groups were identified.
Each Fast Responding Resources is assigned a group cost based on HRL/LSL
The Single Part offer is structured in order to recover Start Up and Minimum Energy cost over the Minimum On time and can vary due to individual units’ LSL
Minimum EOC and Min. Gen. is $75 if Resource had Non-Spin responsibility during study period

## Slide 12: Simulation Assumptions – Fast Responding Resources
Sample of costs
Res Type | HRL (MW) | LRL (MW) | Seasonal LSL (MW) | Startup Cost ($) | Min-Energy Price ($/MWh) | Min EOC ($/MWh) | Max EOC ($/MWh)
SCLE90 | 54.0 | 10.0 | 13.0 | 4,322.05 | 52.39 | 30.86 | 33.91
SCLE90 | 60.0 | 0.0 | 12.0 | 3,448.99 | 48.85 | 28.47 | 31.05
SCLE90 | 95.0 | 0.0 | 41.0 | 6,058.75 | 56.12 | 40.35 | 41.88
DSL | 8.9 | 6.0 | 6.0 | 962.21 | 39.93 | 34.84 | 39.79
NOTE: Min EOC will be equal to the production EOC if the Resource was self committed in production and the EOC value is lower

## Slide 13: Other Assumptions – Days Analyzed
  The Capacity from all Fast Responding Resources is considered online in MIRTM study runs; this has the impact of changing the Operating Reserve Demand Curve (ORDC) calculation slightly; however, the resource capacity is only shifted from offline to online.
  The Block Load Resources are considered “new” Resources for MIRTM which increases the RTOLCAP and shifts the curve to the right by 366MW.
  The Reliability Deployment Price Adder in MIRTM treats the deployment by ERCOT as a “deployment event” therefore MIRTM may find a RTDP when Production and Sequential SCED did not.
  MIRTM Commitment decisions are based on new short-term load forecast and DC tie schedule changes while dispatch uses production SCED GTBD based on old short-term load forecast ramp and regulation component

## Slide 14: Average Price of All Study Dates

## Slide 15: Production Cost of All Study Dates
Negative production costs are due to significant MW on output schedules. Production costs for those resources are -$250/MWh from LSL to output schedule.

## Slide 16: Make Whole Amounts of All Study Dates

## Slide 17: August 13, 2015

## Slide 18: August 13, 2015
Changes in ORDC price adders due to NCLRRRS calculation change in Seq. SCED (NPC-LPC)
Changes in ORDC price adders due to 366 MW of new Blocky Load capacity in RTOLCAP
Impact of high price interval separated for all 4 scenarios

## Slide 19: August 13, 2015

## Slide 20: August 13, 2015 – HDL-GTBD & Price
Cause for price spike at 14:20 in MIRTM 3PO explained on next slide
HDL is reduced in MIRTM 3PO due to less QSGRs committed to be online by MIRTM

## Slide 21: August 13, 2015
  MIRTM 3PO had a spike due to a combination of a unit tripping (~160 MW) and missed load forecast
By waiting until the last minute, binding QSGR commitments were not made in this time frame due to forecast decrease

## Slide 22: August 13, 2015 – Commitment Summary
Tighter QSGR commitment with MIRTM 3PO than with production self-commitment. Loads committed in both scenarios.

## Slide 23: August 13, 2015 – Cost and Revenue

## Slide 24: July 1, 2015 – Observations
  Luminant Request
  Little congestion and low system lambda
  MIRTM 3PO prices slightly higher due to no QSGRs being committed and the load requirement distributed to rest of generation fleet

## Slide 25: July 1, 2015
Negative production costs are due to significant MW on output schedules. Production costs for those resources are -$250/MWh from LSL to output schedule.

## Slide 26: July 1, 2015

## Slide 27: July 1, 2015
Zero make-whole on July 1, 2015

## Slide 28: July 1, 2015 – HDL-GTBD & Price

## Slide 29: July 1, 2015 – Commitment Summary
These QSGRs mimic self-commitment in production
No QSGRs were committed in 3PO
Notes: MIRTM Load Only commitment of QSGR is mimicking production self commitments.

## Slide 30: July 1, 2015 – Cost and Revenue

## Slide 31: August 11, 2015 – Observations
  Luminant Request
  Little congestion and low dispatchable capacity
  Higher LMP and dispatch cost in MIRTM 3PO scenario than Seq. SCED due to tighter QSGR commitment
  MIRTM had no make-whole payments due to high ORDC price adders

## Slide 32: August 11, 2015

## Slide 33: August 11, 2015

## Slide 34: August 11, 2015
MIRTM study scenarios had no make-whole

## Slide 35: August 11, 2015 – Commitment Summary
Many QSGRs had LMPs below cost in Seq. SCED. No loads were committed.

## Slide 36: August 11, 2015 – HDL-GTBD & Price

## Slide 37: August 11, 2015 – Cost and Revenue

## Slide 38: November 11, 2015 – Observations
  Large wind down ramp
  Many active constraints
  Make-whole payments were necessary as a result of tight commitment window for MIRTM 3PO but less than in production SCED

## Slide 39: November 11, 2015

## Slide 40: November 11, 2015

## Slide 41: November 11, 2015

## Slide 42: November 11, 2015 – HDL-GTBD & Prices
Cause for price spike at 17:50 in MIRTM 3PO explained on next slide

## Slide 43: November 11, 2015 – Analysis
  MIRTM 3PO had a spike primarily due to low dispatchable capacity and missed forecast
By waiting until the last minute, binding QSGR commitments were not made in this time frame due to forecast decrease
GTBD used for Binding Prices

## Slide 44: November 11, 2015 – Wind HSL Estimation
Sudden drop in HDL-GTBD due to very large wind down ramp

## Slide 45: November 11, 2015 – Wind HSL Estimation Error
Persistence results in a large wind HSL estimation error during the down ramp

## Slide 46: November 11, 2015 – Commitment Summary
Increase Load commitment

## Slide 47: November 11, 2015 – Cost and Revenue
MIRTM production cost spike due to combination of telemetry error from outaged coal unit and unit’s EOC not being mitigated
Base case constraint activated at 15:55 and was immediately violated in MIRTM. QSGRs with helping shift factor were self-committed in production but MIRTM could not dispatch QSGR until 16:00 due to temporal constraint

## Slide 48: November 27, 2015 – Observations
  Wind steadily decreasing throughout the day
  Very little congestion
  New short-term load forecast over-forecast over peak contributes to make-whole payments
  High price spike in MIRTM 3PO caused by unit shutting down, wind HSL decrease, and AS responsibility increase
  Binding commitments made at 17:35 and 17:45 cause LMPs to go below some QSGR costs and they are subsequently de-committed after fulfilling minimum run time

## Slide 49: November 27, 2015

## Slide 50: November 27, 2015

## Slide 51: November 27, 2015

## Slide 52: November 27, 2015 – HDL-GTBD & Price
Multiple contributors to MIRTM 3PO price spike at 21:05:
When HDL-GTBD is very low, prices are very sensitive to GTBD
Regulation Up AS responsibility increased by 100 MW across the hour
170 MW of wind HSL decrease from 20:55 to 21:05
Unit shutting down, unit going from ON to ONTEST at a lower output, and combined cycle changing configurations
Multiple contributors to MIRTM 3PO price spike at 19:10:
Missed load forecast
Unit shutting down

## Slide 53: November 27, 2015 – Analysis
  MIRTM 3PO had a spike primarily due to low dispatchable capacity and missed forecast
GTBD used for Binding Prices

## Slide 54: November 27, 2015 – Wind HSL Estimation
Wind steadily decreases throughout the day

## Slide 55: November 27, 2015 – Wind HSL Estimation Error
Wind over-estimates due to steady wind down ramp

## Slide 56: November 27, 2015 – Commitment Summary
Binding commitments made at 17:35 and 17:45 cause LMPs to go below some QSGR costs and they are subsequently de-committed after fulfilling minimum run time

## Slide 57: November 27, 2015 – Cost and Revenue

## Slide 58: March 27, 2016 – Observations
  Very low dispatchable capacity and inability to commit QSGRs in 5 minutes led to sudden capacity shortage
  Low wind
  Unit shutting down
  Missed load forecast

## Slide 59: March 27, 2016

## Slide 60: March 27, 2016

## Slide 61: March 27, 2016

## Slide 62: March 27, 2016 – HDL-GTBD & Prices
Multiple contributors to MIRTM 3PO price spikes around 20:00:
Very low dispatchable capacity period is greatly affected by accuracy of input data
Load forecast missed multiple intervals (300-500 MW)
Multiple units shutting down (~200 MW)

## Slide 63: March 27, 2016 – Analysis
  MIRTM 3PO had spikes primarily due to load under forecast 300-500 MW for consecutive intervals
By waiting until the last minute, binding QSGR commitments were not made in this time frame due to forecast decrease
GTBD used for Binding Prices

## Slide 64: March 27, 2016 – Analysis
STLF thought load would stop ramping up when in reality load was rapidly increasing
New STLF was recently modified to be based on regression model of ramp rates so this issue should be mitigated

## Slide 65: March 27, 2016 – Analysis
This was a case where the current STLF also missed the ramp

## Slide 66: March 27, 2016 – Commitment Summary

## Slide 67: March 27, 2016 – Cost and Revenue

## Slide 68: July 25, 2016 – Observations
  New short-term load forecast performs well
  Low wind and dispatchable capacity
  Much tighter QSGR commitment in MIRTM 3PO scenario still reduces LMPs by ~$29 million and production cost by ~$57k at the expense of ~$58k more make-whole than sequential SCED
  MIRTM Load scenario reduces prices by ~$26 million and production cost by ~$29k at the expense of $27k more make-whole than sequential SCED

## Slide 69: July 25, 2016

## Slide 70: July 25, 2016

## Slide 71: July 25, 2016

## Slide 72: July 25, 2016 – HDL-GTBD & Prices

## Slide 73: July 25, 2016 – Commitment Summary

## Slide 74: July 25, 2016 – Cost and Revenue

## Slide 75
Appendix

## Slide 76: Refresher on the MIRTM Process
MIRTM six 5-minute intervals (30 minutes total) with separate commitment and dispatch
8:40 8:45 8:50 8:55 9:00 9:05 9:10 9:15 9:20 9:25 9:30 9:35
Intervals where ONLY Commitment Instructions are binding and the LMPs and MW awards (energy, AS) are indicative
Interval where the LMPs, MW awards (energy, AS) and Commitment Instructions are ALL binding commitment instructions
Sequence of Multi-Interval RT Markets
Analysis window of rolling 30 minutes
RT Market Execution: Depicts the start and end times of the clearing process and the length of symbol is indicative of maximum time allowed to clear market
Dispatch Run & Pricing run
Dispatch Run & Pricing Run
Binding commitments for ALL intervals
1st Interval Binding Base Point & Binding LMPs
Note: The introduction of the Binding Dispatch/Base Point run while eliminating make-Whole payments to Generation Resources due to binding ramp constraints, can however, lead to missed commitments or too early decommitments/recalls. The assumption is that the benefits of eliminating this category of make-whole payments outweighs the disadvantages of missed commitments or too early decommitments/recalls.

## Slide 77: Overview of Recent Activity
Implement Dispatch Module
Implement Pricing Module
Developed three part offers (TPO) based on average verifiable costs and unit HSL
Developed single part offers (SPO) from TPO allocating start costs over minimum up time and LSL
Allowed for Wartsila units to have zero start time and zero min off time (allows fast ramping resources to meet demand in same interval)
Studied the following dates:7/1/2015, 8/11/2015, 8/13/2015, 11/11/2015, 11/27/2015, 3/27/2016, 7/25/2016

## Slide 78: MIRTM – Changes since August SAWG
Make the processing of Combined Cycles consistent between MIRTM and Sequential SCED
Correct the Minimum Energy for Resources carrying Non Spin to agree with $75 Energy offer curve
Streamline the Commitment Summary to two categories:
  Count of Resources below cost
  Count of Resources at or above cost
Corrected two study days that had short SCED runs which caused double counting in the MIRTM post process
Determination and book keeping of noncompetitive constraints are different between MIRTM and Seq. SCED: ERCOT will evaluate the impact and actions taken, if any, at a future SAWG meeting