## Slide 1
Multi-Interval Real-Time Market (MIRTM)
Supply Analysis Working Group
January 17, 2017
ERCOT Staff
Market Design & Analysis

## Slide 2: Today’s Agenda
Review ERCOT findings report
Review Capacity and Load Forecast error at different time horizons
Overview of recent activity
  GTBD setup the same way as studies presented in October SAWG
  Study design changed in order to get a more “apples to apples” comparison so that all of the offers in each run, MIRTM and Sequential SCED (SSCED), are based on same approved Verifiable Costs
Review of Study day results

## Slide 3: MIRTM – Different commitment horizons
ERCOT performed studies to determine the available committable capacity and net load forecast error with different commitment horizons
Although not studied by ERCOT, more capacity may be available if MIRTM can consider transitioning between different combined cycle configurations
*combination of data sources
Horizon | Mean Absolute Error of Net Load Forecast in 2016 | Load Resources From DSWG Survey | Generation Resources * (DSL, SCLE90, SCGT90)
15 minutes | 197 MW | 0 MW | 247 MW
30 minutes | 341 MW | 366 MW | 2983 MW
45 minutes | 485 MW | 501 MW | 3340 MW
Hour Ahead | 575 MW | 601 MW | 3403 MW

## Slide 4: MIRTM – MIRTM Study design
Changes to MIRTM inputs and outputs
    Any resource that self committed at any point in the study period was treated as self committed in MIRTM
    The list of committable Fast Start (FS) resources was changed to include only resources that either:
      ran in quick start mode during Production SCED study period; or
      had status of OFF for the entire study period
      List of MIRTM committable Resource reduced
    For each study day, run MIRTM with FS resources as committable (no load resources)
    For each study day, run MIRTM with load resources as committable (no FS resources)

## Slide 5: MIRTM – Build a story day by day
Committable FS Resources and Total MW for each study day
OD | Number | LSL | HSL
8/11/2015 | 17 | 552 | 956
8/13/2015 | 17 | 584 | 956
11/11/2015 | 14 | 535 | 768
11/27/2015 | 26 | 934 | 1592
3/27/2016 | 26 | 943 | 1541
7/25/2016 | 23 | 905 | 1400

## Slide 6: MIRTM 3PO vs. SSCED Study design
Fast Start (FS)
Start Up
MIRTM Three Part Offer (3PO)
SSCED 1
SSCED 2
Fast Start
Min Gen
Fast Start
EOC
Run a:
EOC = MOC
(SU/ME Amortized over 2+ hours)
Set FS LSL = 0
Run b:
For FS BP > 0
Set LSL = Actual LSL
Run a:
EOC = MOC
(SU/ME Amortized over 15 min.)
Set LSL = 0
Run b:
For FS BP > 0
Set LSL = Actual LSL
Note: A SSCED 3b run was also done using Production EOCs. The comparison graphs are made available for review but are not included in comparison slides.

## Slide 7: MIRTM 3PO vs. SSCED Study design
  Changes to SSCED inputs, design, and outputs
  Using the same approved verifiable costs as the MIRTM 3PO, single part Energy Offer Curves were created two ways:
    RUN 1: The Start Up/ Min Energy component is amortized in the production Mitigated Offer Cap over a minimum of 2 hour recovery time
    RUN 2: The same as above but amortized over a 15 minute recovery time
  For both RUN 1 & 2 in order for SSCED to simulate treatment of current SCED for any Fast Start (FS) online resource :
    Run an “a” run where all committable FS resources are “ON” with LSL = 0
    RUN a “b” run where, for each five minute interval, if the FS resources in the a run with BP > 0 set LSL = actual LSL and status “ON”, else set status “OFF”
    Compare both 1b and 2b runs to MIRTM run in order to get a “range” of outcomes

## Slide 8: MIRTM Load Only vs. Seq. SCED Study design
366 MW of Committable Loads
FS treated same as Production SCED
MIRTM Loads Only
Sequential SCED 4
Load Resources not included in SSCED;
However, 366 MW added to ORDC

## Slide 9: MIRTM Load Only vs. SSCED Study design
  A separate SSCED (RUN 4) run was done to compare with the MIRTM Load only case
    The Load Resources were not modeled in SSCED
    The 366 MW of additional Load Resources capacity was added to the ORDC calculation for SSCED to align with MIRTM Load only run

## Slide 10: MIRTM – build a story day by day
MIRTM 3PO
  Production Costs, Average Prices, and Make Whole amounts for all days
  Compare Production Cost
    Main indicator of efficiency improvements, if any
  Charge to Load including Make Whole charge, if any
  Generator Revenue including Make Whole payment, if any
MIRTM Load Only
  Production Costs, Average Prices, and Make Whole amounts for all days
  Compare Production Cost
    Main indicator of efficiency improvements, if any
  Charge to Load including Make Whole charge, if any
  Generator Revenue including Make Whole payment, if any

## Slide 11: MIRTM – Day by day
  MIRTM 3PO by Day

## Slide 12: MIRTM 3PO Production Cost for all days

## Slide 13: MIRTM 3PO Average Prices for all days

## Slide 14: MIRTM 3PO Make Whole Payments for all days

## Slide 15: Study Day – MIRTM 3PO: August 11, 2015
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.

## Slide 16: Study Day – MIRTM 3PO: August 11, 2015

## Slide 17: Study Day – MIRTM 3PO: August 13, 2015
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.

## Slide 18: Study Day – MIRTM 3PO: August 13, 2015

## Slide 19: Study Day – MIRTM 3PO: November 11, 2015
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.

## Slide 20: Study Day – MIRTM 3PO: November 11, 2015
Chart: 11/11/2015 - Charges and Payments
| Total Charge to Load | Total Generator Revenue
MIRTM 3PO | 17028318.1826 | 16247512.208
Seq. SCED 1b | 17258833.4028 | 16473811.3606
Seq. SCED 2b | 17303771.4437 | 16517990.5529

## Slide 21: Study Day – MIRTM 3PO: November 27, 2015
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.

## Slide 22: Study Day – MIRTM 3PO: November 27, 2015
Chart: 11/27/2015 - Charges and Payments
| Total Charge to Load | Total Generator Revenue
MIRTM 3PO | 71756142.3467 | 71541298.2046
Seq. SCED 1b | 23236719.5586 | 23164611.4734
Seq. SCED 2b | 21359519.0626 | 21308913.5154

## Slide 23: Study Day – MIRTM 3PO: March 27, 2016
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.

## Slide 24: Study Day – MIRTM 3PO: March 27, 2016

## Slide 25: Study Day – MIRTM 3PO: July 25, 2016
Note: Total Production Costs are the sum of Committable, Other Generation, and Transmission penalty costs.
Chart: 7/25/2016 - Production Cost
| FS Committable by MIRTM | Other Generation | Total
MIRTM 3PO | 116311.4475 | 655071.3375 | 4142441.176
Seq. SCED 1b | 40222.4192 | 751691.7946 | 4150845.7283
Seq. SCED 2b | 42331.6656 | 765111.9404 | 4259054.4304

## Slide 26: Study Day – MIRTM 3PO: July 25, 2016

## Slide 27: MIRTM – day by day
  MIRTM Load Only (LO) by Day

## Slide 28: MIRTM LO Production Costs all days

## Slide 29: MIRTM LO Average Prices all days

## Slide 30: MIRTM LO Make Whole Payments all days

## Slide 31: Study Day – MIRTM LO: August 11, 2015
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 32: Study Day – MIRTM LO: August 11, 2015

## Slide 33: Study Day – MIRTM LO: August 13, 2015
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 34: Study Day – MIRTM LO: August 13, 2015

## Slide 35: Study Day – MIRTM LO: November 11, 2015
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 36: Study Day – MIRTM LO: November 11, 2015

## Slide 37: Study Day – MIRTM LO: November 27, 2015
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 38: Study Day – MIRTM LO: November 27, 2015

## Slide 39: Study Day – MIRTM LO: March 27, 2016
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 40: Study Day – MIRTM LO: March 27, 2016

## Slide 41: Study Day – MIRTM LO: July 25, 2016
Note: Total Production Costs are the sum of Blocky Load Curtailment, Other Generation, and Transmission penalty costs.

## Slide 42: Study Day – MIRTM LO: July 25, 2016