## Slide 1
Annual TAC Review of the Market Impacts of Reliability Unit Commitments
Analysis of 1/1/16 through 12/31/16
ERCOT Market Analysis
January 26, 2017

## Slide 2: Protocol Language
5.8 Annual RUC Reporting Requirement
(1) ERCOT shall report to the Technical Advisory Committee (TAC), each January, an assessment of market impacts and Settlements for the aggregate Reliability Unit Commitment (RUC) activity, delineated by type of RUC instruction as follows:
RUC instructions issued for Ancillary Service shortages (failure to sufficiently procure one or more Ancillary Service markets in the Day-Ahead Market (DAM) or subsequent Supplemental Ancillary Service Markets (SASMs));
RUC instructions issued for irresolvable transmission system constraints;
RUC instructions issued in anticipation of extreme cold weather/startup failures;
RUC instructions issued for capacity;
RUC instructions issued for system inertia; and
A summary of RUC Settlements;
(i) RUC charges associated with RUC Make-Whole Amount Total per RUC, as defined in Section 5.7.4.1, RUC Capacity-Short Charge; and
(ii) RUC Shortfall Total, as defined in Section 5.7.4.1.1, Capacity Shortfall Ratio Share.

## Slide 3: Previous RUC Process Presentation
For the Board of Directors on October 11th, 2016
  The Summer 2016 Operation and Market Review material included a significant amount of discussion regarding Reliability Unit Commitment (RUC) instructions
  http://www.ercot.com/calendar/2016/10/11/76339-BOARD
For the QSE Managers Working Group on October 17th, 2016
  Presentation provided a general description of the RUC process
  http://www.ercot.com/calendar/2016/10/14/87632-QMWG

## Slide 4: RUC-Committed Resource-Hours in 2015 and 2016
(*) - The difference between “Instructed” and “Effective” values is a result of Resources starting up, shutting down, or still being off-line for some portion of the RUC-committed hours or Resources not following RUC instructions
 | 2015 | 2016
Instructed Resource-Hours |  | 
Total Count | 411 | 1,514
Effective Resource-Hours (*) |  | 
Total Count | 398 | 1,417
Average LSL | 92 | 92
Average LDL | 109 | 120
Average BP | 116 | 131
Average HSL | 228 | 256

## Slide 5: RUC-Committed Resource-Hours in 2015 and 2016

## Slide 6: RUC Commitment Reasons
1,514 instructed RUC resource-hours in 2016
  1,481 resource-hours (97.8%) noted as for congestion
  33 resource-hours (2.2%) noted as for capacity
There were no resource-hours of commitment for ancillary service shortages, voltage/reactive support, system inertia, or for anticipation of extreme cold weather/startup failures
478 resource-hours were successfully bought back through use of the ONOPTOUT Resource status

## Slide 7: RUC Committed Resources Dispatched above LDL
170.1 resource-hours were dispatched above the Resource’s Low Dispatchable Limit (LDL) when the Resource was not opted out
  For 4.2 resource-hours, the LMP for the RUC-instructed Resource was at a price above the RUC offer floor
  For 127.1 resource-hours, the RUC-instructed Resource was mitigated and the LMP at the Resource was less than the RUC offer floor
    Expected given the percent of RUC instructions for local congestion
  For 38.8 resource-hours, the RUC-instructed Resource was not mitigated and the LMP at the Resources was less than the RUC offer floor
    This implies an issue with the Energy Offer Curve (EOC) for the Resource

## Slide 8: Inconsistency with Settlement Treatment
17% of the instructed RUC resource-hours were settled as ONRUC but the Resource did not telemeter ONRUC
  15% of the resource-hours also had an EOC less than the RUC offer floor
  This also impacts the triggering of the Real-Time Reliability Deployment Price Adder (RTRDPA)
0.3% of the instructed RUC resource-hours were settled as ONOPTOUT but the Resource telemetered ONRUC

## Slide 9: NPRR 744
The project for NPRR 744, RUC Trigger for the Reliability Deployment Price Adder and Alignment with RUC Settlement, is currently in the planning phase
Approved by ERCOT Board on 4/19/2016 and scheduled to be implemented in R3 2017
Requires a QSE to opt out of RUC settlement by telemetering a Resource status of ONOPTOUT during the first SCED interval the Resource is online and available to SCED during the first hour of a RUC commitment
Uses a snapshot of the Resource’s telemetered status and a valid RUC commitment flag to trigger both the RTRDPA and the correct settlements treatment
Will reconcile differences between the RTRDPA and RUC settlement treatment

## Slide 10: Reliability Deployment Price Adders
Month of 2016 | Total RTRDPA Time (Hours) | Time-weighted Average RTRDPA During RTRDPA Intervals ($/MWh)
JAN | 33 | 0.08
FEB | 23 | 0.30
MAR | 45 | 2.23
APR | 39 | 0.40
MAY | 46 | 0.56
JUN | 81 | 0.62
JUL | 105 | 0.66
AUG | 50 | 2.68
SEP | 88 | 3.09
OCT | 87 | 1.30
NOV | 0 | NA
DEC | 0 | NA

## Slide 11: RUC Make-Whole and Claw-Back
Make-whole amounts were fully covered by capacity-short charges for all months in both years

## Slide 12: RUC Make-Whole and Claw-Back
Month | RUC Make-Whole Amount ($1000s) |  | RUC Capacity-Short Charges ($1000s) |  | Uplift Charges ($1000s) |  | Claw-Back Charges ($1000s) |  | RUC Shortfall Total (MWh in 1000s) | 
 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016 | 2015 | 2016
Jan | 0 | -29 | 0 | 29 | 0 | 0 | 23 | 0 | 0 | 499
Feb | 0 | -4 | 0 | 4 | 0 | 0 | 0 | 38 | 0 | 192
Mar | 0 | -13 | 0 | 13 | 0 | 0 | 0 | 608 | 0 | 212
Apr | -5 | -70 | 5 | 70 | 0 | 0 | 0 | 3 | 115 | 1673
May | -240 | -45 | 240 | 45 | 0 | 0 | 3 | 88 | 938 | 1569
Jun | -16 | -176 | 16 | 176 | 0 | 0 | 0 | 115 | 202 | 2229
Jul | -2 | -372 | 2 | 372 | 0 | 0 | 10 | 156 | 34 | 3341
Aug | -13 | -138 | 13 | 138 | 0 | 0 | 0 | 2 | 321 | 2427
Sep | -139 | -240 | 139 | 240 | 0 | 0 | 175 | 46 | 1680 | 2447
Oct | -65 | -153 | 65 | 153 | 0 | 0 | 126 | 81 | 1102 | 3581
Nov | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 275 | 0 | 145
Dec | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 13: Conclusions
1,514 instructed RUC resource-hours resulted in 1,417 effective RUC resource-hours
The total RUC make-whole amount was ~$1.2M
  These payments were fully covered through capacity-short charges
Inconsistencies between settlement treatment and the triggering of the RTRDPA were still observed
  This will be resolved with the implementation of NPRR 744 later this year