## Slide 1
Overview of New Control Room Desk
Dan Woodfin
Sr. Director, System Operations
ROS
ERCOT Public
February 2, 2017

## Slide 2: Traditional Operational Risks
Operational
Monitoring
and Analysis
ERCOT operators deal with a variety of traditional risks in the Control Room:
  Transmission line faults and outages
  Generation Resource trips
  Load Forecast errors
  Base Point Deviations
Control Room primarily assesses risk to operational reliability through:
  Characterization of contingencies and their consequences,
  Determination of operating reserves and limits to be maintained,
  Informed, experienced operator judgment
Operating
Actions

## Slide 3: Evolving Risks
Operating
Actions
Operating
Actions
With the changing resource mix on the system, the need to assess and manage certain risks has grown
Improved quantitative analysis and dynamic consideration of these risks and controls are needed
Traditional Needs
Evolving Needs
Operational
Monitoring
and Analysis

## Slide 4: Evolving Risks
Operating
Actions
Operating
Actions
Intent is to perform existing activities with more in-depth monitoring and analysis
Type and volume of resulting operating actions is not expected to change, except in situations where the increased risks manifest themselves
Traditional Needs
Evolving Needs
Operational
Monitoring
and Analysis

## Slide 5: Reliability Risk Desk Status
To meet ERCOT’s strategic goal of adapting to the changing resource mix, staffing for a new desk in Control Room was approved in 2016-17 budget
Initial tools, procedures, staffing and training has been completed and new desk went live on 1/30/2017
  New Operations Procedures are posted – Power Operations Bulletin 770

## Slide 6: Reliability Risk Desk Goals
Facilitate improved accuracy of renewable forecasts
  Promote improved telemetry performance from wind/solar plants
  Perform forecast adjustments during icing and other extreme weather events
Maintain sufficient frequency responsive reserves
  Confirm critical level of inertia is online
  Ensure frequency responsive capacity is available to cover actual inertia conditions
Maintain sufficient temporally available capacity to cover remaining forecast errors and net load ramps

## Slide 7: Reliability Risk Desk Activities
1. Renewable Forecast and Extreme Weather Monitoring
3. Forecast Error Risk and NSRS Sufficiency
4. Intra-Hour Resource Monitoring
2. Inertia Monitoring and RRS Sufficiency

## Slide 8: 1. Renewable Forecast and Extreme Weather Monitoring
Reliability Risk Desk will:
  Monitor quality of data telemetered by intermittent resources and its accuracy in meeting the methodology outlined in ERCOT rules.
    Contact appropriate QSEs if needed to resolve the issues identified.
  Monitor the current performance of renewable forecasts. Evaluate large forecast errors and correct the forecast if warranted.
  Monitor the probability of experiencing large wind output ramps and the sufficiency of the available ramping capability.

## Slide 9: 2. Inertia Monitoring and RRS Sufficiency
Reliability Risk Desk will:
  Monitor that the inertia on the system is above the Critical Level of Inertia
  Monitor adequacy of currently available RRS in comparison to the actual RRS requirement based on Real Time system inertia conditions.
  Evaluate the sufficiency of posted RRS requirement in the next 24 to 36 hour timeframe in comparison to the estimated RRS needed based on most recent COP submissions.
AS Methodology Posted Minimums
Less synchronous unit commitment
More Frequency Responsive capacity needed
Less Inertia
RRSactual-req
Less load and/or more wind

## Slide 10: Forecast Risk and NSRS Sufficiency Monitoring
Reliability Risk Desk will:
  Monitor the adequacy of scheduled resources (COPs) to cover the forecasted Load, ramp, and the uncertainty around the Load and renewable forecasts for the next 6 hours and identify hours with insufficiency
  Retain sufficient NSRS in every hour to cover the higher of:
    the current level of net load ramp risk or
    the amount that will be needed, based on currently expected operating conditions, to restore frequency and recover contingency reserves
Forecasted Load
Net Load Forecast Error

## Slide 11: Intra-hour Resource Monitoring
Reliability Risk Desk will:
  Monitor the short-term Load, wind and solar forecasts
    Intra-hour net load patterns due to load/wind/solar can be vastly different even with same hourly average values.
  Monitor the adequacy of available generation and reserves to cover the expected volatility in short-term net load over the next 60 minutes and identify sub-hourly intervals with insufficiency
  Tools for this functionality still under development

## Slide 12: Operating Actions
Implementation of new desk should be almost imperceptible to stakeholders
  Additional analysis and monitoring to support current activities of existing desks
  Type and volume of resulting operating actions is not expected to change significantly
Operating Procedures are currently written to require notification of Shift Supervisor and appropriate existing desk when monitoring shows issues
  Informs existing decision processes
If additional resources are required to cover risk, will use existing tools and processes
  Preference is to allow market to respond, procure additional A/S as time permits, defer RUC and only as necessary preserve reliability

## Slide 13: Questions?