## Slide 1
Analysis of Load Reductions Associated with 4-CP Transmission Charges and Price Responsive Load/Retail DR
Carl L Raish
Principal Load Profiling and Modeling
Demand Side Working Group – March 24, 2017

## Slide 2: Overview
  4CP Analysis
    Competitive and NOIE Areas
    2015 update and 2016 results
  Price Response and Retail DR
    Block and Index Pricing (BI)
    Other Load Control (OLC)
    Other Voluntary DR (OTH)
    Peak Rebate (PR)
    Real Time Pricing (RTP)
    Time-of-Use Pricing (TOU)
      Analysis not available
  Still to come – updated analysis of the interaction of 4CP and price response

## Slide 3: How 4CP Works
‘BUSIDRRQ’ customers ≥ 700 kW or served at transmission (69 kV) voltage are subject to 4CP charges.
  Simple average of the metered load during ERCOT system monthly peak 15-minute intervals in four summer months -- June, July, August & September.
  Multiplied by the applicable prevailing TDSP Tariff, as approved by PUC.
  Is the basis for the monthly 4CP-based rates for the following calendar year.
Analysis for this report addressed 4CP in both the competitive and NOIE areas of ERCOT.
The analysis used settlement system interval data
  For ESIIDs in competitive ERCOT areas with ‘BUSIDRRQ’ profile types.
  Calculated interval data of the native load in NOIE areas … NOIE area boundary metered imports plus generation located inside the NOIE area

## Slide 4: Analysis Methodology - Competitive
Identify 4CP and Near-CP days.
Identify High-Price days (to exclude from baseline determination).
Classify customers by voltage level (Transmission/Distribution) and weather sensitivity.
Classify customer and response type
  Weather sensitive (WS) – use regression baseline.
  Non-Weather sensitive NWS). – use Near20 baseline.
  Identify responding customers based on magnitude and frequency of response on identified 4CP and Near-CP days.
  Classify customers by type of reduction:
    Load reduction that targets the afternoon hours of 4CP/Near-CP days.
    Load reduction that starts early in the day and continues through the 4CP time period.
Calculate load reductions for specific 4CP/Near-CP days.
  Limited to responding customers identified in step 4.
  Include customer’s load in over-all reduction calculation if they have a significant reduction on the specific day.

## Slide 5: Analysis Methodology - NOIE
Used same 4CP, Near-CP and High-price days as identified for the analysis of competitive ESIIDs.
Analysis was limited to the largest NOIEs that account for 90% of summer weekday kWh (33 – 34 NOIEs depending on year).
Regression model was estimated for an analysis year using three closest years of data for each NOIE and interval estimates produced for each day … determined a predominant single weather zone for each NOIE.
Baseline-to-actual percent difference was calculated for non-CP days for each NOIE and the 75th percentile level difference was determined.
For each NOIE, counted CP- and Near-CP days for which the NOIE load was reduced if the hour-ending 17:00 MW reduction on the CP- / Near-CP day exceeded 75th percentile difference.
NOIE was deemed a 4CP responder if the frequency and magnitude of reductions was significant.

## Slide 6: Competitive 4 CP Days - 2015
CP Reduce = 491
CP Reduce = 581
CP Reduce = 584
CP Reduce = 620

## Slide 7: NOIE 4 CP Days - 2015
CP Reduce = 106
CP Reduce = 721
CP Reduce = 647
CP Reduce = 312

## Slide 8: Competitive + NOIE 4 CP Days - 2015
CP Reduce = 576
CP Reduce = 1,295
CP Reduce = 1,216
CP Reduce = 938

## Slide 9: Competitive 4 CP Days - 2016
CP Reduce = 435
CP Reduce = 626
CP Reduce = 452
CP Reduce = 577

## Slide 10: NOIE 4 CP Days - 2016
CP Reduce = 440
CP Reduce = 786
CP Reduce = 650
CP Reduce = 572

## Slide 11: Competitive + NOIE 4 CP Days - 2016
CP Reduce = 869
CP Reduce = 1,403
CP Reduce = 1,210
CP Reduce = 1,154

## Slide 12: Hour-ending 17:00 MW Reductions on 4 CP Days - 2015
Competitive -- All Responding 4-CP ESIIDS
Peak reduction exceeds day-use response and accounts for 74% of the total response
Most of the MW response came from Low LF ESIIDs

## Slide 13: Hour-ending 17:00 MW Reductions on 4 CP Days - 2016
Competitive -- Reductions by Voltage Group
Most of the MW response comes from Transmission and Distribution NWS ESIIDs

## Slide 14: Competitive 15-Minute Response 2009 - 2016

## Slide 15: NOIE 15-Minute Response 2009 - 2016

## Slide 16: Competitive Hour Ending 17:00 Response

## Slide 17: NOIE Hour Ending 17:00 Response

## Slide 18: Number of ESIIDs with 4 CP Responses – 2015
Across the 4 months ~1,600 (15%) of the ESIIDs subject to 4CP charges responded
Response rates: High LF 7%, Medium LF 8%, Low LF 30%
Low LF accounts for 64% of all responders

## Slide 19: Number of ESIIDs with 4 CP Responses – 2016
Across the 4 months ~1,600 (15%) of the ESIIDs subject to 4CP charges responded
Response rates: High LF 6%, Medium LF 8%, Low LF 29%
Low LF accounts for 64% of all responders

## Slide 20: Hour-ending 17:00 MW Reductions on 4 CP Days - 2016
Reductions as a Percent of Total Load Factor Group Load
Across all participants, ESIIDs reduce about 5% of their total load
Low LF ESIIDs reduce the highest percent of their total load (~17%)

## Slide 21: Hour-ending 17:00 Reductions on 4 CP Days - 2016
Percentage of Load Reduction by Load Factor and Voltage Group
Low LF and Transmission ESIIDs provide about half of the total reduction

## Slide 22: 2014 Block & Index Analysis
Jan 6, 2014
507.9 MW Reduce
16 Reps 6,800 Bus customers
2 Weekday high-price events were analyzed
Jan 6 was an EEA day
Mar 3, 2014
229.3 MW Reduce

## Slide 23: 2015 Block & Index Analysis
Jul 30, 2015
199.9 MW Reduce
14 Reps 8,643 Bus customers
6 Weekday high-price events were analyzed
May 18 event with small reduction not shown
Aug 11, 2015
159.3 MW Reduce
Aug 13, 2015
127.7 MW Reduce
Aug 12, 2015
96.6 MW Reduce
Aug 5, 2015
161.5 MW Reduce

## Slide 24: 2016 Block & Index Analysis
Aug 2, 2016
80.0 MW Reduce
18 Reps 13,117 Bus customers
2 Weekday high-price events were analyzed
Nov 29, 2016
157.1 MW Reduce

## Slide 25: 2014 OLC Analysis
May Composite Day
2.4 MW Reduce
3 Reps reported 7 deployments in 2014 affecting 3,200 Res and 5 Bus customers
4 events (3 in Aug, 1 in Oct) showed no evidence of any load reduction
May and October days combined into composite graphs to approximate the total OLC load reduction that could occur with same-day deployment
Early Oct Composite Day
2.3 MW Reduce
Mid October Composite Day
2.4 MW Reduce

## Slide 26: 2015 OLC Analysis
Jul 30, 2016
7.0 MW Reduce
2 Reps reported 14 deployments in 2015 affecting 11,516 Res and 8 Bus customers
Both REPs deployed 5 times on the same days, July 30, August 5, 11, 12 and 13
Aug 5, 2016
6.5 MW Reduce
Aug 11, 2016
7.3 MW Reduce
Aug 12, 2016
2.3 MW Reduce
Aug 13, 2016
5.4 MW Reduce

## Slide 27: 2016 OLC Analysis
Jun 6, 2016
2.0 MW Reduce
1 Rep reported 10 deployments in 2016 affecting 1,780 Res customers
The REP deployed 10 times across June – September 2016
Jul 25, 2016
3.7 MW Reduce
Aug 2, 2016
4.0 MW Reduce

## Slide 28: 2016 Other Voluntary DR Analysis
Aug 2, 2016
9.3 MW Reduce
1 Rep reported 23 deployments in 2016 affecting 33,872 Res and 50 Bus customers
Program description does not align with the other categories
Reductions ranged from 0 – 15.4 MW
Aug 3, 2016
10.9 MW Reduce
Aug 4, 2016
15.4 MW Reduce
Aug 16, 2016
5.9 MW Reduce

## Slide 29: 2014 Peak Rebate Analysis
August Composite Day
September Composite Day
4 Reps reported 9 deployments in 2014 affecting 32,1002 Res and 143 Bus customers
5 REPs deployed on Aug 10
3 events (1 in Sep, 2 in Oct) showed no evidence of any load reduction
6 events showed obvious reductions ranging from 27 – 40 MW
August and September days are combined into composite graphs to approximate the total PR load reduction that could occur with same-day deployment

## Slide 30: 2015 Peak Rebate Analysis
Aug 10, 2015
23.6 MW Reduce
7 Reps reported 19 deployments in 2015 affecting 43,602 Res and 1,759 Bus customers
5 REPs deployed on Aug 10
Composite Deployment 2015
30.4 MW Reduce

## Slide 31: 2016 Peak Rebate Analysis
3 Reps reported 22 deployments in 2016 affecting 75,568 Res and 2,938 Bus customers
No days with deployments by all 3 REPs
Composite Deployment 2016
28.2 MW Reduce

## Slide 32: 2014 Real Time Pricing Analysis
11 Reps 1,000 Res and 9,700 Bus customers
2 Weekday high-price events were analyzed
Note: EEA related Load reduction led to price drop, and RTP related load reduction mostly occurred following the price drop
Jan 6, 2014
12.9 MW Reduce
Mar 3, 2014
7.4 MW Reduce

## Slide 33: 2015 Real Time Pricing Analysis
Jul 30, 2015
10.5 MW Reduce
9 Reps 851 Res and 4,009 Bus customers
6 Weekday high-price events were analyzed
Aug 5, 2015
5.2 MW Reduce
Aug 11, 2015
9.6 MW Reduce
May 18, 2015
1.7 MW Reduce
Aug 12, 2015
11.1 MW Reduce
Aug 13, 2015
1.2 MW Reduce

## Slide 34: 2016 Real Time Pricing Analysis
Nov 29, 2016
0.4 MW Reduce
11 Reps 1,321 Res and 8,255 Bus customers
2 Weekday high-price events were analyzed
Aug 2, 2016
0.6 MW Reduce

## Slide 35: Questions?
ON
OFF
craish@ercot.com 512/248-3876