## Slide 1
Example for Discussion on Day Ahead Make Whole Adjustments due
to Ancillary Service Infeasibility
March 31st , 2017

## Slide 2: Previous discussion
A part of previous discussions, the shaded area was being viewed as additional real-time energy revenue
It is quite possible that this is not the case given that the change in the High Ancillary Service Limit (HASL) is also likely affecting the constraint shadow price and, as a result, Locational Marginal Prices (LMPs)
HASL’
HASL
HASL’ is what the HASL would have been if the AS had not been declared infeasible

## Slide 3: Why may this not be the case?
In reality, the AS is likely being declared infeasible because the constraint is more costly to solve otherwise (i.e., the shadow price for the constraint is at the max. value)
Let’s picture the following scenario:
  The constrained element is a 138kV transmission line and the constraint would have been at the max. shadow price if the AS had not being declared infeasible;
  HASL’ and HASL for the Resource are 250 and 300 MW, respectively
  The shift factor for the Resource on the constraint is -20%;
  System lambda for the entire period is 30 $/MWh (*); and
  The Energy Offer Curve (EOC) between HASL’ and HASL for the Resource is 45 $/MWh
(*) System lambda could also vary between the two cases

## Slide 4: Why may this not be the case?
If in the dispatch that is resolving the constraint with the higher HASL the Resource is marginal, there is a significant decrease in the energy payment for the Resource due to the lower LMP
Actually energy payments assuming a dispatch of 280 MW:
  280 MW * 45 $/MWh = 12,600 $/h
Expected payment under the original limit of HASL’
  250 MW * (30 $/MWh – (-.20 * 3500)) = 182,500 $/h
While the amount of energy produced increases, the LMP for the Resource is significantly affected by the change in the optimizations ability to manage the constraint

## Slide 5: Conclusions
Given that:
  The assumption that the Resource is being paid “extra” for the additional energy is not necessarily true
  The determination of LMPs and instructions for the alternate universe in which the AS was not declared infeasible is complex and potentially inexact
Reevaluation of the DAM Make-Whole to consider the change in AS revenue due to the claw-back is appropriate
However, the consideration of potential increases in real-time energy payments is not warranted