## Slide 1
Reliability Unit Commitment Discussion with QMWG
March 31st, 2017

## Slide 2: Evaluation of Changing Max. Shadow Prices in the RUC Engine
ERCOT re-executed a significant portion of 2016 Reliability Unit Commitment (RUC) cases that resulted in commitments to see how recommendations would have changed with different max. shadow prices for constraints
Manually reviewed the reduction in commitment and additional violations with regards to the impact to reliability
  Which Resources are no longer being committed and are there alternatives
  Historic congestion in real-time for the constraints that had increased violations
  Would ERCOT take manual action for the constraints that had increased violations
Evaluated the max. shadow prices that allow RUC to meet desired reliability objectives considering the Resource-specific information (actual cost & temporal constraint) for Resources that are likely to be committed through the RUC process (lower lead time and impact >2%)

## Slide 3: Proposal based on the Evaluation
  The max. shadow prices be reduced to a value that is 10% of the current 345 kV limits
    This value is expected to allow a good portion of the Resources to be accessible for commitment by RUC when the shift factor is -2% or better addressing the reliability issues
The same value would be applied for all voltage levels
  Even with the same $/MWh value, the pool of Resources is already decreased for lower voltage transmission equipment for an equivalent percent overloading due the relatively lower ratings of that equipment
Re-evaluate the possibility/need for updating the max. shadow price based on the experience gained from using these new values and improved information available for the Operator from the many changes currently being worked on (listed in the following slides)

## Slide 4: Additional Improvements
The following are some improvements related to RUC that are either recently implemented, in the queue for implementation, or under discussion
  Use of load-distributed slack bus shift factors for Operator displays
    Improved ability to identify related constraints and understand the effectiveness/benefit of the recommendation
    More comparable to SCED
    Currently enabled in production
  Improved warning message capability for temporal constraints
  Display for reviewing offline and available Resources that can start in one hour or less
    Introduced as part of NPRR712 and implemented in late 2016

## Slide 5: Additional Improvements
Continued
  NPRR 744, RUC Trigger for the Reliability Deployment Price Adder and Alignment with RUC Settlement
    Scheduled for implementation in June 2017
  Changing of down ramp rates for online Resources
    Ramp rates are effectively unlimited in the current system
    This can result in abnormal dispatch results and impact commitment recommendations
  Parallel execution of multiple RUC optimizations
    Intent would be to provide Operators with additional information on the reason(s) behind the RUC recommendation

## Slide 6: Additional Improvements
Continued
  Providing additional constraint information to Operators
    Currently only the constraint information from the final iteration of RUC is captured and displayed
    Displaying constraint information from all iterations would provide additional insight into why Resources were recommended for commitment
  Suggestion plan for Combined Cycle plants that are already online in a lower configuration, but could be moved to a higher configuration
    The display will be available to Operators later this year

## Slide 7: Additional Improvements
Continued
  Improved logic for notification times on Resources that are coming out of an outage
    This change came out of the stakeholder discussions last year
    The change is in the queue, but has not yet been implemented
  Other general display improvements
    Intent would be to simplify Operator processes
    Example of improvement is the consolidation of multiple displays