## Slide 1: Emerging Technologies Working Group update to the Wholesale Market Subcommittee
04/05/2017

## Slide 2: ETWG update to WMS
NERC DER Summary
IEEE1547 Update
ETWG Scope
Next Meeting

## Slide 3: ETWG update to WMS: NERC DER Reliability Whitepaper

## Slide 4: ETWG update to WMS: NERC DER Reliability Whitepaper

## Slide 5: ETWG update to WMS: IEEE1547 Revision Update
“General Definitions” Updates to IEEE1547
  Standard went from 16 pages to 113 pages.
  DER/DG Size limit (10 MW) removed
    Doesn’t impact Texas—previously defined by PUCT.
DER defined as sources of electric power
  Does not include demand response
Different Settings/classifications based on equipment performance and application
  Class I - Synchronous machines
  Class II- Inverters
  Class III- Inverters in High penetration areas
Considers Different Interconnections for DERs
  Stand alone
  Part of a local EPS
“Stability” Updates to IEEE1547
  BES stability features (New “Smart Inverter” functions)
    Voltage Regulation/Reactive power capability
      absorb or inject VARs
      Volt/VAR function
      power factor modes
    Voltage Regulation/Active power control
      Volt/watt function
    Wider operating voltage/freq. window
    Mandates Voltage/frequency ride through functions
  Other stability features
    Soft start reconnect
      ramping function
      random times

## Slide 6: ETWG update to WMS: Suggested Scope Changes

## Slide 7: ETWG update to WMS: Next Meetings
May 2, 2017, Tuesday, 9:30-12:00
June 6, 2017, Tuesday, 9:30-12:00