## Slide 1
Analysis of Load Reductions Associated with 4-CP Transmission Charges
and
Price Responsive Load/Retail DR
Carl L Raish
Principal Load Profiling and Modeling
WMS – April 5, 2017

## Slide 2: Overview
  4CP Analysis
    Competitive and NOIE Areas
    2015 update and 2016 results
  Price Response and Retail DR (Based on annual REP survey since 2013)
    Block and Index Pricing (BI)
    Other Load Control (OLC)
    Other Voluntary DR (OTH)
    Peak Rebate (PR)
    Real Time Pricing (RTP)
    Time-of-Use Pricing (TOU)
  Still to come – updated analysis of the interaction of 4CP and price response

## Slide 3: How 4CP Works
‘BUSIDRRQ’ customers ≥ 700 kW or served at transmission (69 kV) voltage are subject to 4CP charges.
  Simple average of the metered load during ERCOT system monthly peak 15-minute intervals in four summer months -- June, July, August & September.
  Multiplied by the applicable prevailing TDSP Tariff, as approved by PUC.
  Is the basis for the monthly 4CP-based rates for the following calendar year.
Analysis for this report addressed 4CP in both the competitive and NOIE areas of ERCOT.
The analysis used settlement system interval data
  For ESIIDs in competitive ERCOT areas with ‘BUSIDRRQ’ profile types.
  Calculated interval data of the native load in NOIE areas … NOIE area boundary metered imports plus generation located inside the NOIE area

## Slide 4: Analysis Methodology
Identify 4CP and Near-CP days.
  4CP days reported by ERCOT.
  Near-CP days identified by significant reductions in the total load of competitive transmission ESIIDs.
Identify High-Price days (to exclude from baseline determination).
Identify specific NOIEs and ESIIDs that respond based on frequency and magnitude of response
Calculate baselines and load reductions for each 4CP/Near-CP day.

## Slide 5: Competitive 4 CP Days - 2016
CP Reduce = 436
CP Reduce = 626
CP Reduce = 452
CP Reduce = 577

## Slide 6: NOIE 4 CP Days - 2016
CP Reduce = 440
CP Reduce = 783
CP Reduce = 481
CP Reduce = 552

## Slide 7: Competitive + NOIE Response 2009 - 2016

## Slide 8: Max CP/NearCP Reductions - Hour Ending 17:00
Slope = 21
Slope = 2
Slope = 88

## Slide 9: Growth of ESIIDs and NOIEs with 4CP Response
Slope = 10

## Slide 10: Max CP/NearCP Reductions - Hour Ending 17:00
Slope = 2
Postage Stamp Transmission Rates
2002-2017
Currently $52.91
Postage Stamp rate for Transmission Cost of Service has more than tripled since 2002
>$7B in Competitive Renewable Energy Zone (CREZ) transmission investment
  $4.9B of CREZ activated in 2013 alone
>$2B in projects activated in 2016
Source: PUCT Dockets
The postage stamp rate (per 4CP kW) is charged to DSPs, who in turn reimburse TSPs for their transmission investments

## Slide 11: REP DR Total Participation
ESIID counts
  2014: 763,000
  2015: 848,000 (+85,000)
  2016: 907,000 (+59,000)
REP counts
  2014: 33 (combining Sub-LSEs 23)
  2015: 32 (combining Sub-LSEs 25)
  2016: 35 (combining Sub-LSEs 27)

## Slide 12: 2015 Block & Index Analysis
Jul 30, 2015
199.9 MW Reduce
16 Reps reported 9,534 Business ESIIDs on annual survey
14 Reps with 8,643 Business ESIIDs on high-price day
6 Weekday high-price events were analyzed
Reductions 0 – 200 MW

## Slide 13: 2016 Block & Index Analysis
Aug 2, 2016
80.0 MW Reduce
19 Reps reported 14,371 Business ESIIDs reported on survey
18 Reps with 13,117 Business ESIIDs on high-price day
2 Weekday high-price events were analyzed
Nov 29, 2016
157.1 MW Reduce

## Slide 14: 2015 Other Load Control Analysis
2 Reps reported 9 BUS and 14,898 RES ESIIDs on annual survey
Both Reps reported 14 deployments affecting 11,516 Res and 8 Bus ESIIDs
Both REPs deployed 5 times on the same days, July 30, August 5, 11, 12 and 13
Reductions 2.3 – 7.3 MW
Aug 11, 2016
7.3 MW Reduce

## Slide 15: 2016 Other Load Control Analysis
2 Reps reported 4 BUS and 8,720 RES ESIIDs on annual survey
1 Rep reported 10 deployments in 2016 affecting 1,780 Res customers
Reductions 0.5 – 4.0 MW
Aug 2, 2016
4.0 MW Reduce

## Slide 16: 2016 Other Voluntary DR Analysis
1 Rep reported 23 deployments in 2016 affecting 33,872 Res and 50 Bus customers
Program description does not align with the other categories
Reductions ranged from 0 – 15.4 MW
Aug 4, 2016
15.4 MW Reduce

## Slide 17: 2015 Peak Rebate Analysis
Aug 10, 2015
23.6 MW Reduce
9 Reps reported 32,289 BUS and 465,527 RES ESIIDs on annual survey
7 Reps reported 19 deployments in 2015 affecting 1,759 Bus and 43,602 Res ESIIDs
5 REPs deployed on Aug 10
Composite graph shows total response if all REPs had deployed on the same day
Composite Deployment 2015
30.4 MW Reduce

## Slide 18: 2016 Peak Rebate Analysis
9 Reps reported 35,369 BUS and 478,243 RES ESIIDs on annual survey
3 Reps reported 22 deployments in 2016 affecting 75,568 Res and 2,938 Bus customers
No days with deployments by all 3 REPs
Composite graph shows total response if all REPs had deployed on the same day
Composite Deployment 2016
28.2 MW Reduce

## Slide 19: 2015 Real Time Pricing Analysis
9 Reps reported 4,612 BUS and 998 RES ESIIDs on annual survey
9 Reps with 4,009 Business and 851 Res ESIIDs on high-price day
6 Weekday high-price events were analyzed
Reductions 1.2 – 11.1 MW
Aug 12, 2015
11.1 MW Reduce

## Slide 20: 2016 Real Time Pricing Analysis
Nov 29, 2016
0.4 MW Reduce
12 Reps reported 8,479 BUS and 1,326 RES ESIIDs on annual survey
11 Reps 1,321 Res and 8,255 Bus customers on high-price day
2 Weekday high-price events were analyzed
Aug 2, 2016
0.6 MW Reduce

## Slide 21: Time-of-Use Pricing Analysis
16 Reps reported
  6,756 BUS and 321,504 RES ESIIDs on 2015 survey
  4,914 BUS and 331,138 RES ESIIDs on 2016 survey
Analysis not started
Analysis goal will be to determine response levels on high-price and peak days

## Slide 22: Summary
 | 2015 MW | 2016 MW | ESIIDs Deployed 2015 | ESIIDs Deployed 2016 | ESIIDs Not Deployed 2015 | ESIIDs Not Deployed 2016
4CP | 1,321 | 1,409 | 1,800 | 1,700 | 9,500 | 9,700
BI | 200 | 157 | 9,000 | 13,000 | - | -
OLC | 7 | 4 | 12,000 | 2,000 | 3,000 | 7,000
OTH | - | 15 | - | 34,000 | - | 34,000
PR | 30 | 28 | 45,000 | 79,000 | 452,000 | 435,000
RTP | 11 | 1 | 5,000 | 10,000 | - | -
TOU | - | - | 322,000 | 331,000 | - | -

## Slide 23: Still to Come
Interaction of high prices and 4CP response
  ESIIDs on Block & Index or Real Time Pricing that are also subject to 4CP charges
  NOIEs with significant response on high-price non-4CP days
  NOIEs with significant response on high-price days and 4CP days
TOU analysis

## Slide 24: Questions?
ON
OFF
craish@ercot.com 512/248-3876