## Slide 1
Revenue Neutrality Analysis
Presentation to CSWG
April 24, 2017

## Slide 2: Introduction
There has been an increase in revenue neutrality allocation in the first part of 2017
Total of about $42 million from January through March
In this period the primary cause is PTP obligation payments without offsetting energy imbalance charges

## Slide 3: Three Main Causes of Recent Charges
PUN net loads not being included in the Load Zone price calculations
Overselling of PTPs that occurs when a node is islanded under a contingency in the DAM
LDFs in the DAM not representative of load in RT

## Slide 4: PUN Net Loads and Load Zone Prices
PUN nodal prices and net load are not included in the load zone price calculation
PUNs have settlement points available for Point-to-Point (PTP) transactions
Congestion near a PUN can cause high settlement point prices at the PUN without corresponding increases in the Load Zone Price
PTPs sinking at the PUN node can result in PTP payments without offsetting in load charges
Net loads at PUNs pay the relevant load zone price so they do not have an economic incentive to resolve the congestion

## Slide 5: Stakeholder Discussion of PUN and LZ Prices
Discussed at WMS on 4/5/2017
  http://www.ercot.com/calendar/2017/4/5/108817-WMS
Referred to CMWG
Further discussion expected at CMWG on 4/25/2017
  http://www.ercot.com/calendar/2017/4/25/116932-CMWG
ERCOT is developing a proposal and will submit an NPRR

## Slide 6: Node Islanded under a Contingency in DAM
PTP modeling in DAM can result in overselling when a contingency disconnects one of the source or sink Settlement Points
In the contingency case power balance is maintained by ignoring any PTPs with an islanded Settlement Point
Ignoring these PTP flows can cause overselling of PTPs and lead to a revenue shortfall

## Slide 7: Stakeholder Discussion of Islanded Node PTPs
Discussed at WMS on 4/5/2017
  http://www.ercot.com/calendar/2017/4/5/108817-WMS
QMWG WebEx
  Discussion of potential design changes
  http://www.ercot.com/calendar/2017/4/13/122366-QMWG
Further discussion expected at QMWG on 5/1/2017
  http://www.ercot.com/calendar/2017/5/1/113935-QMWG
  ERCOT will present analysis of how often N-1 contingencies that result in islanding are binding in DAM and how other ISOs handle this issue

## Slide 8: DAM LDFs not Representative of Load in RT
Load Distribution Factors (LDFs) in DAM model may not accurately represent load patterns in RT
Differences in congestion patterns between DAM and RTM can lead to higher PTP payments than energy imbalance charges and a revenue shortfall

## Slide 9: Relative Market Impacts
Total Revenue Neutrality Allocation: about $42 million from January through March
PUN net load and LZ price calculations: about $26 million
Resource nodes islanded under a contingency: about $10 million
DAM LDFs not representative of RT load: a few million