## Slide 1: Private Use Network Load Distribution Factors
Steve Reedy
Potomac Economics
Deputy Director, ERCOT IMM
May 3rd, 2017

## Slide 2: PUN Loads are not included in Load Distribution Factors
Load Zone Load
PUN Load
PUN Resource Node

## Slide 3: Mechanics of the Problem
Load zone energy purchased in the Day-Ahead Market does not “flow” in the network model to PUN Loads
  Leaves more transmission capacity open near PUN Loads than if properly modeled
Energy Only bids/ PTP Obligation bids sinking at PUN resource nodes do not compete with Load Zone flows
  More can be sold than should be
High prices at PUN loads are not factored into appropriate Load Zone prices
  No revenue to fund payout to EO bids/PTPs sunk at PUN RNs
  Causes Revenue Neutrality hit

## Slide 4: Not Very Similar to “Dead Bus” Issue
Dead Bus | PUN Loads
Limited only by Breaker Ratings (9999MW available) | Limited by appropriate network ratings
Extremely low risk to bidders | Standard risk to bidders
Volume got very high very quickly | Volume not particularly high
Affects Revenue Neutrality | Affect Revenue Neutrality

## Slide 5: PTP OBL MWs Sunk at “Poster Child” PUN RN – Nodal

## Slide 6: PTP OBL MWs Sunk at “Poster Child” PUN RN – 2017