## Slide 1: NPRR829 Incorporate Real-Time Telemetered Net Generation for Non-Modeled Generation into the Real-Time Liability Estimate
ERCOT PRS Meeting
May 11, 2017

## Slide 2: NPRR Business Case
Currently it is difficult for non-modeled generation to hedge in the DA market due to potential superfluous collateral calls during high priced RT market events.
Using telemetered data from non-modeled generation will allow ERCOT to more accurately calculate QSE collateral requirements.
This NPPR will increase DA market liquidity due to increased participation of non-modeled generation in the DA market.
Implementing this NPRR has the potential to allow ERCOT to gain near real-time transparency into non-modeled generation which could increase their ability in analyzing real-time system conditions.
Furthermore, ERCOT will better understand the true position of the QSE by operating day and will also better understand their cash flow.

## Slide 3: IDR Meter Challenge
IDR Meters are read once a month. As a result:
Payments for energy aren’t received until the Final Statement
  55 days after the operating day
  A large part of calculating collateral calls stems from Invoice timing
ERCOT therefore does not know the true position of a QSE for a given operating day until the IDR Meter Data is submitted to them from the TDSP (once a month)
NPRR753 is related to this NPRR
  If the TDSP’s were to incorporate the AMS daily-read system for IDR’s, the process would have the potential to reduce or minimize collateral requirements

## Slide 4: Day-Ahead Market Example
QSE offers 2 MW On-Peak (HE0700-HE2200) in DAM
  Awarded - $40/MWH Energy Price in all 16 hours
    DA On-Peak Average $40/MWH, ($40 x 16hrs) / 16hrs
  32 Total MWH’s offered in (2MW x 16hrs)
Real Time Prices
  Spikes to $1000/MWH for 4 Hours
    QSE Strike Price ($100) – means non-modeled gen will run whenever SPP above $100
  Balance On-Peak hours average $40/MWH
  Overall RT On-Peak Average $280/MWH, (($1000 x 4hrs) + ($40 x 12hrs)) / 16hrs
Collateral Call
  QSE owes
    ($40 - $280) * 32 = -$7,680
    This collateral call would come in 7 days and would be the average of the previous 14 days
Real Time Energy Revenue
  QSE generates:
    2 MW * 4 hours * $1000 = $8,000
  Money wouldn’t be paid until final statement – 55 days later
True Position for the day is therefore positive $320
  Telemetry would be used to show this and thus reduce collateral call

## Slide 5: NPRR Revision Description
This NPRR provides a mechanism for a QSE with Non-Modeled generation to inform ERCOT in a timely manner the net generation to the ERCOT grid from their Non-Modeled generators so that the output can be considered in the credit calculation.
Per the previous example, the QSE would supply data to ERCOT so they could subtract the $8000 from the $7,680 and eliminate or decrease any sort of collateral call

## Slide 6: NPRR Language Change Operational Data Requirements
6.5.5.2.(12) A QSE representing Non-Modeled generation may provide Real-Time telemetry of the net generation of those Non-Modeled generators for the purpose of having that net generation included in the Real-Time Liability Estimate.

## Slide 7: NPRR Language Change Real-Time Liability Estimate
16.11.4.3.2 (1) ERCOT shall estimate RTL for an Operating Day as the sum of estimates for the following RTM Settlement charges and payments:
  (b) Section 6.6.3.2, Real-Time Energy Imbalance Payment or Charge at a Load Zone, using 14 day or seven day old LRS for Load estimate and actual metered generation or net telemetry as the generation estimate;

## Slide 8: Collateral Calculation
  TPEA = Max [0, MCE, Max [0,EAL]] + PUL
  EAL = Estimated Aggregate Liability
    based on estimates and invoiced activity
  MCE = Minimum Current Exposure
    based on invoiced activity
  Total Potential Exposure Any (TPEA) reflects exposure related to Real-Time and Day Ahead Market (DAM) activity
  Currently the credit calculation doesn’t account for Non-Modeled Generation in the Real Time estimates or in the Initial settlements invoices. The Non-Modeled Generation is captured in the credit calculation once it is invoiced in the Final settlement invoices. By adding Telemetry, the EAL and MCE components will take into consideration the generation that offsets the load in a more timely manner.

## Slide 9: Collateral Calculation
Several of the Real-Time estimated and invoiced components of the credit calculation will be impacted by the proposed change
A component will be needed to capture Non-Modeled generation in the credit calculation:
  TWTGnmg - (Time-Weighted Telemetered Generation)
  ERTMGVOLQDTOTLZ - (Estimated Real-Time Metered Generation Volume QSE Daily Total for all Load Zone DG net generation)