## Slide 1
Point-to-Point Obligation (PTP) Settlements and Clearing Difference
QMWG
June 5th, 2017

## Slide 2: PTP Clearing and Settlement Difference
  Concern: Price difference between clearing and settlement of PTPs
  A contingency de-energizes one side of the PTP and causes a constraint to bind at high shadow price and hence high price at energized side
  To maintain power balance under PTP analysis, DAM creates an exception to exclude this contingency/constraint’s impact in PTP clearing due to one side being de-energized
  Constraint has impact to LMP at the energized side, while constraint has no impact to LMP at the de-energized side

## Slide 3: Proposed Changes to manage PTP Clearing and Settlement Difference
ERCOT Proposal (Modified with market participant input)
This is ERCOT’s preferred approach
To maintain power balance under PTP analysis, instead of ignoring PTP/CRR whose source or sink is disconnected in a contingency, modify DAM and CRR process to redistribute the PTP MW from the disconnected Settlement Point to all the other energized generator nodes
  This enables the constraint to influence the clearing of PTP in DAM
For DAM and Real-Time, modify the formula for calculating the Locational Marginal Price (LMP) at a Settlement Point disconnected in a contingency to use the “pickup” shift factor
  Makes optimization and settlement price consistent

## Slide 4: Proposed Changes to manage PTP Clearing and Settlement Difference
ERCOT Proposal (Modified with market participant input)
White paper “Processing of Contingencies that disconnect a Settlement Point” describes the proposed change. For example,
  Posted to QMWG June 5th, 2017 meeting page
  Changes to Real-Time, DAM and CRR described
  Review of redistribution methodology in Real-Time for correctness
  Align the redistribution process in DAM and CRR as close as feasible to Real-Time
For a facility with multiple Resource Node Settlement Points, there may be situations where the final LMP could be significantly different due to one of the Resource Nodes being disconnected in a contingency
  The electrically similar Settlement Point processing in DAM and CRR should mitigate any gaming opportunity

## Slide 5
Contingencies that disconnect a Resource but not their Settlement Point
&
Radial Load Contingencies

## Slide 6: Contingencies that disconnect a Resource but not their Settlement Point (Explicit G-1 contingencies)
A concern has been raised about explicit G-1 contingencies
  G-1 contingency in this discussion refers to a contingency that disconnects a Generation Resource but NOT its Settlement Point.
  Explicit G-1 contingencies are ONLY modeled in Real-Time
  In Real-Time, overloads detected by Contingency Analysis due to a explicit G-1 contingency are passed to SCED
    SCED uses pickup shift factor for the Generator Resource EOC
    Resource Node LMP (as it is energized) uses actual shift factor
  There is further discussion needed about explicit G-1 contingencies in Real-Time causing potential overselling

## Slide 7: Radial Load (L-1) Contingencies
There are scenarios where, a N-1 transmission contingency could disconnect a radial load
  Under this scenario, this contingency will be analyzed in Real-Time, DAM and CRR
  If there is a valid load rollover scheme, then the load rollover is considered and effectively no load is disconnected
  If there is no load rollover scheme defined then under this type of contingency;
    Real-Time: The load is considered lost and “pickup” approach is used to maintain power balance in the post contingency network.
    DAM and CRR: The load is NOT considered lost and is redistributed to all other loads in the same Load Zone.
  Further discussion and analysis needed