| NPRR Number |  | NPRR Title | Resource Limits in Providing Responsive Reserves Service |
| --- | --- | --- | --- |
| Date Posted |  |
| Requested Resolution | Normal |
| Nodal Protocol Sections Requiring Revision | 3.18, Resource Limits in Providing Ancillary Service |
| Related Documents Requiring Revision/Related Revision Requests | None |
| Revision Description | This NPRR changes the Resource Limits in Providing Responsive Reserves Service from a hard set upper limit of 20% of the unit capacity to a limit that is set by the actual performance of the unit. |
| Reason for Revision | Addresses current operational issues. Meets Strategic goals (tied to the ERCOT Strategic Plan or directed by the ERCOT Board). Market efficiencies or enhancements Administrative Regulatory requirements Other: (explain) (please select all that apply) |
| Business Case | Describe qualitative benefits (Examples: satisfies regulatory requirements, data transparency enhancement, etc.), quantitative benefits (benefit calculations), impacts to market segments and other information relating to the impacts or benefits of the NPRR. |

| Sponsor |
| --- |
| Name | Robert Helton |
| E-mail Address | Robert.helton@dynegy.com |
| Company | Dynegy Inc. |
| Phone Number | 832-435-7815 |
| Cell Number | 713-767-5174 |
| Market Segment | Independent Generator |

| Market Rules Staff Contact |
| --- |
| Name |  |
| E-Mail Address |  |
| Phone Number |  |

Proposed Protocol Language Revision

3.18	Resource Limits in Providing Ancillary Service

(1)	For both Generation Resources and Load Resources the High Sustained Limit (HSL) must be greater than or equal to the Low Sustained Limit (LSL) and the sum of the Resource-specific designation of capacity to provide Responsive Reserve (RRS), Regulation Up (Reg-Up), Regulation Down (Reg-Down), and Non-Spinning Reserve (Non-Spin).

(2)	For Non-Spin, the amount of Non-Spin provided must be less than or equal to the HSL for Off-Line Generation Resources.

(3)	For RRS Service:

(a)	The full amount of RRS provided from a Generation Resource must be less than or equal to the median of its actual performance as defined in Operating Guides for the last eight Measurable Events,, and must be less than or equal to ten times the Emergency Ramp Rate, and must be frequency responsive.  A new or previously disqualified Resource seeking generation portion of RRS qualification shall be qualified for providing RRS up to a capacity level demonstrated in Governor tests as specified in the Operating Guides.  (b)	Hydro Generation Resources operating in the synchronous condenser fast-response mode may provide RRS up to the hydro Generation Resource’s proven 20-second response capability (which may be 100% of the HSL).  The initiation setting of the automatic under-frequency relay setting shall not be lower than 59.80 Hz;

(c)	For any hydro Generation Resource with a 5% droop setting operating as a generator, the amount of RRS provided may never be more than 20% of the HSL; and

(d)	The amount of RRS provided from a Load Resource must be less than or equal to the HSL minus the sum of the LSL, Reg-Up Resource Responsibility, Reg-Down Resource Responsibility, and Non-Spin Resource Responsibility.