## Slide 1
Study Scope - Quarterly Stability Assessment
August 22, 2017
RPG Meeting

## Slide 2: Outline
Introduction
Study scope of Quarterly Stability Assessment (QSA)
Next steps

## Slide 3: Introduction
In April 2017, ERCOT Board of Directors approved PGRR052, Quarterly Stability Assessment (QSA). ERCOT sent a market notice in July. PGRR052 became effective as of August 1
Purpose of QSA
  Assess the impact of proposed generation resources connecting to the ERCOT system
  Identify any dynamic instability issues and establish Generic Transmission Constraints (GTC) and Generic Transmission Limits (GTL)
Standards: NERC Standard FAC 002-2 (Facility Interconnection) and ERCOT Planning Guide and Protocol

## Slide 4: Study Process
Case Conditioning
Case review and update
Input file Prepation
Event file creation
Dynamic Stability Analysis
Update dynamic data, channel and script files (e.g. DYRs and Python)
Dispatch of generator in area of study
Dynamic stability analysis for each study region
Report and Sharing
Flat Start simulation
GTC and GTL development for any instability issue if necessary
Report and MIS Posting (Secure Area)
Review the results with ERCOT Operations

## Slide 5: Assumption and Methodology
Study year and cases:
  The latest 2017DWG flat start cases will be used and updated for the 1st QSA.
    High Wind Low Load Conditions: 2020 High Wind Low Load Case
    Summer Peak Load Conditions: 2019 Summer Peak Load Case
Requirements for resources to be included in the first QSA:
  Initial Synchronization dates in Jan 1 ~ Mar 31 2018
  Planning Guide Section 5.9 has the detail of pre-requisites. Key pre-requisites are
    Planning Guide 6.9 Requirements are met
    Full interconnection studies are complete
    Reactive power studies are complete
    System improvements or mitigation plan
    All resource data are submitted and approved

## Slide 6: Assumption and Methodology
New generation resources included in the August QSA:
  Total 26 GINR projects ( 22 to be synchronized in 2017 and 4 in 1st quarter 2018)
INR | Project Name
11INR0082a | Val Verde Wind
12INR0059b | Barilla Solar 1B
13INR0049 | Friendswood G
13INR0056 | Fluvanna Renewable 1
14INR0031 | Baytown Chiller
14INR0038 | PHR Peakers
14INR0041a | Bruenning's Breeze
14INR0057 | Buckthorn Wind 1
14INR0060b | SALVTION
15INR0045 | Riggins Solar
INR | Project Name
16INR0087 | RTS Wind
16INR0091 | Santa Rita Wind
16INR0122 | Blue Summit Battery
17INR0022 | NET Power LaPorte
17INR0027 | Dermott Wind 1
17INR0042 | Castleman Chamon
INR | Project Name
15INR0061 | SolaireHolman 1
15INR0064 | BearKat Wind A
15INR0070_1b | Pearl Solar
15INR0082 | Flat Top Wind I
16INR0009 | Port Comfort
16INR0023 | BNB Lamesa Solar (Phase I)
16INR0054 | NASA-JSC CHP
16INR0055 | Chapman Ranch Wind I
16INR0065 | Castle Gap Solar
16INR0065b | CED Upton Solar

## Slide 7: Assumption and Methodology
Study Area:
  ERCOT Staff will determine study area(s) that are identified with stability concerns in the FIS stability study reports.
  Additional study areas may be considered by using engineering judgement and past experience.
Contingencies:
  Planning Event P0 will be tested for flat start behavior under no disturbance conditions
  Contingencies identified in the FIS stability reports
  In addition, ERCOT may use engineering judgement and past experience to study contingencies other than those identified as instability in the FIS stability studies

## Slide 8: Next Step
ERCOT is currently conducting the QSA.
End of October: Completion of Quarterly Stability Assessment
Within 10 business days of completion Summary report to be posted to the MIS Secure Area
Next QSA will start from November 1
  Submit Initial Synchronization Dates
  Meet all QSA requirements prior to November 1

## Slide 9: Question
?