## Slide 1
Fuel Adders in the ERCOT System
ERCOT
August 23, 2017
Note: Below is the original PPT presented to RCWG
on April 27, 2016

## Slide 2
Fuel Adders in the ERCOT System
ERCOT
April 27, 2016

## Slide 3: Fuel Adders in VC Cost Calculations
  a. Startup Cost: Fuel Rate * (Fuel Price +FA) + OM
    DAM Make-Whole Payments
    RUC Make-Whole Payments
    Startup Cost Caps
  b. Minimum Energy Cost: AHR * (Fuel Price +FA) + OM
    DAM Make-Whole Payments
    RUC Make-Whole Payments
    Minimum Energy Cost Caps
  c. Mitigated Offer Cap: {IHR * (Fuel Price +FA) + OM}*Multiplier
  Where:
  Fuel Price = combination of FIP or FOP or $1.50
  Note: For the Startup and Minimum Energy cost calculations, the FA will not be added to the Fuel Price directly, but will adjust the fuel rate component. The equations have been presented in a different manner for simplicity; the outcome is the same.

## Slide 4: Summary
Adjusting the Fuel Adders will impact the following areas:
  Startup Cap
  Minimum Energy Cap
  Mitigated Offer Cap
  DAM Make-Whole Payments
  RUC Make-Whole Payments

## Slide 5: Coal Pricing Short-Term Solution Options
  A. Fuel Adder Change
  B. Solid Price ($1.50/MMBtu) Change
  Note: For the Startup and Minimum Energy cost calculations, the FA will not be added to the Fuel Price directly, but will adjust the fuel rate component. The equations have been presented in a different manner for simplicity; the outcome is the same.
Advantages | Disadvantages
No system change required | Slight over compensation for Startup & Min Energy Costs
Quick approval and implementation (potential implementation date of July 2016) | Minor manual impact to VC process
Interim approach to long-term solution | Will require VC Manual change in the future with long-term approach
Advantages | Disadvantages
No manual impact to VC process | Requires NPRR to change
Interim approach to long-term solution | System impact (settlements, MMS)
Potentially more accurate calculation of Startup & Min Energy Costs than Option A | Will require adjustments to existing FA (VC Manual change)
 | Earliest Implementation date 1st quarter of 2017