## Slide 1
Revisions to the LDF Methodology: Analysis for Method of Calculating PUN LDFs
Agee Springer
9/6/2017
WMS

## Slide 2: Background
The TAC-approved LDF methodology is being updated to be in alignment with and provide details for the implementation of NPRR831, Inclusion of Private Use Networks in Load Zone Price Calculations.
  Scheduled for implementation in R5
The most notable change in the methodology is that ERCOT will now be using historical net consumption at a PUN site to determine that PUN’s LDF.
  Current process sets PUN LDFs to zero within the systems.
This presentation details the analysis behind ERCOT’s recommendation.
ERCOT is seeking WMS endorsement and needs TAC approval of the methodology prior to implementation of the NPRR.

## Slide 3: Background – LDF Methodology Change
V1 (2010)
  Generating new LDF depend on month-season mapping table
V2 (2017 improvement)
  Generating new LDF sets when required, based on significant changes in system-wide load patterns
  New process for PUN loads
  Based on most recent operational network model

## Slide 4: Background – LDF Methodology Change
Triggers for LDF updates:
Regular seasonal updates
Load model changes with a database load
Significant PUN net consumption changes due to its Resource outages
Significant Block Load Transfer (BLT) of load into the ERCOT system.

## Slide 5: Background – LDF Methodology Change
New process for PUN loads:
Based on historical data of the net power consumption at the PUN
Hourly average value of the net power consumption as the initial net load distribution at the PUN level
The net load distribution at the PUN level is further distributed to the individual loads inside the PUN

## Slide 6: Study Methodology
The key question for the PUN LDF calculation is regarding the look-back period.
Three look-back periods were evaluated (28-day, 7-day, and 1-day) for four “snapshot” dates:
  7/5
  7/12
  7/19
  7/26
These dates represent the start points for collecting historical data to calculate the LDFs.
For each snapshot date, three separate LDFs sets were calculated using three different lengths of historical data.

## Slide 7: Study Methodology
In the 28-day method, hourly load data from the previous 28 days from the snapshot was averaged by hour of the day to calculate the LDFs.
Snapshot Date
Previous 28 days
Averages by hour used to compute LDFs

## Slide 8: Study Methodology
In the 7-day method, hourly load data from the previous 7 days from the snapshot was averaged by hour to calculate the LDFs.
Snapshot Date
Previous 7 days
Averages by hour used to compute LDFs

## Slide 9: Study Methodology
In the 7-day method, hourly load data from the previous 7 days from the snapshot was averaged by hour to calculate the LDFs.
In the 1-day method, hourly load data from the previous operating day was used to calculate the LDFs.
Snapshot Date
Previous 1 day
Hourly loads used to compute LDFs

## Slide 10: Study Methodology
The initial analysis began by identifying PUNs that were net consumers on average for the previous 60 days. Nine PUNs were identified.
For each of those nine, LDFs were calculated using the various look-back periods for the four snapshot dates and compared.
Seven of the nine PUNs showed little (<10 MW) difference on average between the LDF sets for each of the four snapshot dates.
  This suggests that, for most PUNs in ERCOT, the LDFs calculated will be consistent regardless of which method is used.
The two remaining PUNs were analyzed further (PUN B and PUN C)

## Slide 11: Study Methodology
To evaluate the LDF performance, hourly load data for the 28 day period was pulled.
The absolute difference between LDF and actual load was then calculated by hour for all three LDF sets.
Snapshot Date
Next 28 days
Load data from this period compared to calculated LDFs

## Slide 12: Study Results
The graph below shows the performance of the three LDF sets for all four snapshot dates.
Note that the results have been normalized to the largest average difference for each PUN.
Chart: LDF Performance by Snapshot Date
| PUN B 7/5 Snapshot | PUN B 7/12 Snapshot | PUN B 7/19 Snapshot | PUN B 7/26 Snapshot | PUN C 7/5 Snapshot | PUN C 7/12 Snapshot | PUN C 7/19 Snapshot | PUN C 7/26 Snapshot
1-day average | 0.51426 | 0.8155 | 0.56777 | 0.66365 | 0.91507 | 1 | 0.28158 | 0.31882
7-day average | 0.47809 | 1 | 0.6265 | 0.78992 | 0.67548 | 0.99337 | 0.29881 | 0.27865
28-day average | 0.47258 | 0.47596 | 0.5577 | 0.65233 | 0.47625 | 0.40166 | 0.59276 | 0.6196

## Slide 13: Study Results
In general, it is clear that the 28-day LDF shows the best performance compared to the other two methods.
Chart: LDF Performance by Snapshot Date
| PUN B 7/5 Snapshot | PUN B 7/12 Snapshot | PUN B 7/19 Snapshot | PUN B 7/26 Snapshot | PUN C 7/5 Snapshot | PUN C 7/12 Snapshot | PUN C 7/19 Snapshot | PUN C 7/26 Snapshot
1-day average | 0.51426 | 0.8155 | 0.56777 | 0.66365 | 0.91507 | 1 | 0.28158 | 0.31882
7-day average | 0.47809 | 1 | 0.6265 | 0.78992 | 0.67548 | 0.99337 | 0.29881 | 0.27865
28-day average | 0.47258 | 0.47596 | 0.5577 | 0.65233 | 0.47625 | 0.40166 | 0.59276 | 0.6196

## Slide 14: Study Results
The exception to this trend are the 7/19 and 7/26 snapshots for PUN C, where the 28-day LDFs did not perform as well.
  This may have been due to outages at the plant.
Chart: LDF Performance by Snapshot Date
| PUN B 7/5 Snapshot | PUN B 7/12 Snapshot | PUN B 7/19 Snapshot | PUN B 7/26 Snapshot | PUN C 7/5 Snapshot | PUN C 7/12 Snapshot | PUN C 7/19 Snapshot | PUN C 7/26 Snapshot
1-day average | 0.51426 | 0.8155 | 0.56777 | 0.66365 | 0.91507 | 1 | 0.28158 | 0.31882
7-day average | 0.47809 | 1 | 0.6265 | 0.78992 | 0.67548 | 0.99337 | 0.29881 | 0.27865
28-day average | 0.47258 | 0.47596 | 0.5577 | 0.65233 | 0.47625 | 0.40166 | 0.59276 | 0.6196

## Slide 15: Study Results
While not applied for the study, the updated methodology does allow ERCOT to adjust LDFs to address this
Chart: LDF Performance by Snapshot Date
| PUN B 7/5 Snapshot | PUN B 7/12 Snapshot | PUN B 7/19 Snapshot | PUN B 7/26 Snapshot | PUN C 7/5 Snapshot | PUN C 7/12 Snapshot | PUN C 7/19 Snapshot | PUN C 7/26 Snapshot
1-day average | 0.51426 | 0.8155 | 0.56777 | 0.66365 | 0.91507 | 1 | 0.28158 | 0.31882
7-day average | 0.47809 | 1 | 0.6265 | 0.78992 | 0.67548 | 0.99337 | 0.29881 | 0.27865
28-day average | 0.47258 | 0.47596 | 0.5577 | 0.65233 | 0.47625 | 0.40166 | 0.59276 | 0.6196

## Slide 16: Study Results
Averaging across all four snapshot dates again indicates that the 28-day method for calculating PUN LDFs produces the least error overall.
Note that these results have also been normalized to the largest absolute error for each PUN.
LDF Type | PUN B Average Absolute Error | PUN C Average Absolute Error
1-day average | 0.64 | 0.63
7-day average | 0.72 | 0.56
28-day average | 0.54 | 0.52

## Slide 17: Conclusion
For the majority of PUNs studied, the method for calculating LDFs did not result in significantly different values.
For the remaining two PUNs, the analysis indicated the LDFs calculated using the 28-day method showed the best performance when compared with the next 28-days of load.
ERCOT is proposing to move forward with the 28-day method and is looking for endorsement of the methodology document by WMS.
Performance of the look-back period can be reviewed with the appropriate stakeholder group.